## Slide 1: CCA for Clauses 16, 17 and 19
Date: 2015-May
Authors:
NOTE: Includes inputs from Brian Hart (Cisco) and Guido Hiertz (Ericsson)

## Slide 2: Background
The standard presently allows an 11b Clause 16 STA to just use one of three CCA schemes: ED-CCA, CS and CS with ED threshold. Similarly Clause 17 devices also have a choice.
However, because many (if not all) 11b devices use just CS, 11g OFDM transmissions must use protection mechanism that is usually a RST/CTS or CTS-to-self.
As it stands an 11b device using only CS-CCA is not compliant with EN 300 328 V1.8.1 which specifies ED-CCA at -58dBm minimum.
Clause 19 and 20 devices must use both CS-CCA and ED-CCA.
NOTE: This proposal would not affect present 11b devices but would affect new 11b implementations.

## Slide 3: Summary of existing CCA Specs
Clause | Description | Min RX | CCA -CS | CCA-ED
16 | DSSS 1, 2Mbps 16.4.6.3 | -80dBm @ 2Mbps) | One of following: 1 – above ED 2 – any DSSS 3 – DSSS above ED | -80dBm >100mW -76dBm >50<100mW -73dm <50mW
17 | CCK 5.5, 11Mbps 17.3.8.2 | -76dBm @ 11Mbps | One of following: 1 – above ED 4 – any HR (with timer) 5 – HR above ED | -76dBm >100mW -73dBm >50<100mW -70dm <50mW
18 | 11a OFDM 18.3.10.6 | -82dBm 20MHz -85dBm 10MHz -88dBm 5MHz | -82dBm 20MHz -85dBm 10MHz -88dBm 5MHz | Mandatory -62dBm 20MHz -65dBm 10MHz -68dBm 5MHz
19 | 11g ERP 19.4.6 | -82dBm 20MHz | Valid signal -76dBm | No Spec
20 | 11n 20.3.20.5.2 | -82dBm 20MHz -79dBm 40MHz | HT signal -82dBm 20MHz -79dBm 40MHz | -62dBm 20MHz -59dBm 40MHz If not support HT-GF -72dBm for HT-GF (20MHz) -69dBm for HT-GF (40MHz)
22 | 11ac 22.3.18.5 |  | Primary Channel -82dBm 20MHz -79dBm 40MHz -76dBm 80MHz -73dBm 160MHz | Secondary channel Any signal -62dBm 20MHz -59dBm 40MHz -72dBm in any 20MHz of 40MHz
-82dBm
-62dBm
11b devices
tends to use these

## Slide 4: ETSI EN 300 328 V1.8.2
“The energy detection threshold for the CCA shall be proportional to the transmit power of the transmitter: for a 20 dBm e.i.r.p. transmitter the CCA threshold level (TL) shall be equal or lower than -70 dBm/MHz at the input to the receiver (assuming a 0 dBi receive antenna). For power levels below 20 dBm e.i.r.p. the CCA threshold level may be relaxed to TL = -70 dBm/MHz + 20 - Pout e.i.r.p. (Pout in dBm).”
In a 20MHz channel, this requirement equates to about -62dBm.
This creates the Upper Limit for ED CCA.

## Slide 5: Discussion on 11b CCA
OFDM, 11g and 11n recognize the 11b preamble and hence in practice we have the -82dBm CCA threshold between 11g/n and 11b
DSSS and CCK do not recognize an OFDM preamble even though they share the band AND are 802.11.
    Hence OFDM 11g/11n need to use “protection” which reduces throughput.
    This is because 11b can choose the ‘valid signal only’ option (which they do)
BUT OFDM 11g and 11n DO recognize DSSS and CCK at the -82dBm threshold because they understand 11b.
For ‘Fair Sharing’, 11b could recognize OFDM at about the -82dBm threshold, and this would be ED/CCA
  Note: The ED/CCA is presently set to -80dBm BUT not mandated
  IF Clause 16 , 17 ED/CCA was mandated, then 11g, 11n and 11b could share ‘equally’ and OFDM 11g/n would not need to send CTS or protective mechanism.

## Slide 6: Basic Options
Make ED/CCA mandatory for Clause 16 and 17.
  Minor change, just make “CCA-Mode 1” mandatory.
  Still allow ‘valid signal’ threshold
  Provides for 11b, 11g and 11n all sharing fairly and could eliminate the need for 11g/n OFDM to use protection with the associated efficiency improvement
Leave all the clause 16/17 CCA as is (select one of 3) BUT add mandatory -62dBm ED/CCA requirement.
  Minimum change but does bring 11b into line with ETSI.
  If device chooses the ED/CCA then same as A, but not mandated.
  As OFDM is seen as ‘energy’, 11g/n may need to use protection for themselves.
Bring 11b CCA into line with others, mandate -82dBm valid signal, with -62dBm ED/CCA
  As OFDM is seen as ‘energy’, 11g/n may need to use protection for themselves.

## Slide 7: Option A – Clause 16.4.6.5
Existing Text:
“The DSSS PHY shall provide the capability to perform CCA according to at least one of the following three methods
— CCA Mode 1: Energy above threshold. CCA shall report a busy medium upon detection of any
energy above the ED threshold. (Note: This is -80dBm)
— CCA Mode 2: CS only. CCA shall report a busy medium only upon detection of a DSSS signal. This signal may be above or below the ED threshold.
— CCA Mode 3: CS with energy above threshold. CCA shall report a busy medium upon detection of a DSSS signal with energy above the ED threshold.”
Revised Text:
“The DSSS PHY shall perform CCA according to CCA Mode 1 and may also provide the capability to perform CCA according to CCA Mode 2 or CCA mode 3.
— CCA Mode 1: Energy above threshold. CCA shall report a busy medium upon detection of any
energy above the ED threshold
— CCA Mode 2: CS only. CCA shall report a busy medium only upon detection of a DSSS signal. This signal may be above or below the ED threshold.
— CCA Mode 3: CS with energy above threshold. CCA shall report a busy medium upon detection of a DSSS signal with energy above the ED threshold.”
Similar change for Clause 17.3.8.5

## Slide 8: Option B – Clause 16.4.6.5
Existing Text:
“The DSSS PHY shall provide the capability to perform CCA according to at least one of the following three methods
— CCA Mode 1: Energy above threshold. CCA shall report a busy medium upon detection of any
energy above the ED threshold. (NOTE: This is -80dBm)
— CCA Mode 2: CS only. CCA shall report a busy medium only upon detection of a DSSS signal. This signal may be above or below the ED threshold.
— CCA Mode 3: CS with energy above threshold. CCA shall report a busy medium upon detection of a DSSS signal with energy above the ED threshold.”
Revised Text:
“The DSSS PHY shall provide the capability to perform CCA according to both:
A – At least one of the following options:
— CCA Mode 1: Energy above threshold. CCA shall report a busy medium upon detection of any
energy above the ED threshold.
— CCA Mode 2: CS only. CCA shall report a busy medium only upon detection of a DSSS signal. This signal may be above or below the ED threshold.
— CCA Mode 3: CS with energy above threshold. CCA shall report a busy medium upon detection of a DSSS signal with energy above the ED threshold.
And
B – CCA-ED coarse: Energy above threshold. CCA shall report a busy medium upon detection of any energy above -62dBm.
Similar change for Clause 17.3.8.5

## Slide 9: Option C – Clause 16.4.6.5
Existing Text:
“The DSSS PHY shall provide the capability to perform CCA according to at least one of the following three methods
— CCA Mode 1: Energy above threshold. CCA shall report a busy medium upon detection of any
energy above the ED threshold.
— CCA Mode 2: CS only. CCA shall report a busy medium only upon detection of a DSSS signal. This signal may be above or below the ED threshold.
— CCA Mode 3: CS with energy above threshold. CCA shall report a busy medium upon detection of a DSSS signal with energy above the ED threshold.”
Revised Text:
“The DSSS PHY shall provide the capability to perform CCA according to both:
— CCA Mode 1: Energy above threshold. CCA shall report a busy medium upon detection of any
energy above -62dBm.
— CCA Mode 3: CS with energy above threshold. CCA shall report a busy medium upon detection of a DSSS signal with energy above the ED threshold
Then change the ED threshold
The ED threshold shall be <= -82 dBm for TX power >100mW, -78 dBm for 50mW <TX power<=100mW, and -72 dBm for TX power <=50mW.
Alternative might be simply:
— CCA Mode 3: CS with energy above threshold. CCA shall report a busy medium upon detection of a DSSS signal with energy above -82dBm
Similar change for Clause 17.3.8.5

## Slide 10: Aside
The following note would be inserted
{Note to 802.11REVmc reader, to be removed before publication. The following change has no force until REVmc is ratified (for anticipated ratification date, see http://www.ieee802.org/11/Reports/802.11_Timelines.htm). Pre-existing HR/DSSS STAs compliant to 802.11-2012 remain compliant to 802.11-2012.}
Simply clarifying that the change would only affect new 11b devices.

## Slide 11: Quick Recap (Intro to Straw Poll)
Option A – Mandate ED/CCA for 11b
Already a choice
Meets ETSI requirement
Puts 11b and 11g/n on equal sharing, fairness
  11g/n recognize 11b at -82dBm
  11b would recognize 11g/n at -80dBm
Could eliminate ‘protection’ requirement and improve efficiency for 11g/n (Clause 9.26.2 Protection mechanism for non-ERP receivers)
  Only point is that NAV not set by OFDM.
Option B – Mandate -62dBm EDCCA for 11b
Meets ETSI requirement
Still requires ‘protection’ for 11g/n
Option C – Mandate -62dBm ED/CCA, -82dBm for valid signal 11b
Meets ETSI requirement
Common requirement,
Still requires ‘protection’ for 11g/n

## Slide 12: Straw Poll - A
Would you support a change to the CCA for DSSS and CCK along the lines as described for Option A, B or C
Yes
No

## Slide 13: Straw Poll - B
Which Option would you prefer for 11b devices?
Option A – Mandate ED/CCA (-80dBm, 100mw TX)
Option B - Add mandatory -62dBm ED/CCA
Option C – Mandate -82dB valid signal and -62dBm ED/CCA.
A
B
C
No preference