## Slide 1: TG ax Enterprise Scenario and DSC
Date: 2015-05
Authors:

## Slide 2: Background
The Enterprise scenario uses four 80MHz channels.
Estimating the relative signal strengths between the APs, APs and STAs and STAs can indicate if DSC can improve the throughput. This is examined.
Similarly, 9 channel re-use is examined.

## Slide 3: Topography
STAs

## Slide 4: 4 Channel re-use

## Slide 5: 4 Channel Re-use
Note AP to AP -64dBm
Furthest STA to AP -48dBm
Worse case SNIR at AP is 16dB

## Slide 6: 4 Channels with DSC
But SNIR reduced for furthest STAs
~45%

## Slide 7: 9 Channel Re-Use

## Slide 8: Summary
4 Channel Re-Use
  All APs and ALL STAs on same channel are overlapping.
  With DSC about 30% of STAs overlap, and AP SNIR is low for signals from ~45% of STAs
  What is the throughput difference?
9 Channel Re-Use
  All APs and ALL STAs on same channel are overlapping.
  With DSC APs do not overlap STAs do not overlap
  What is throughput difference compared to 4 channel and 9 channel?
  Throughput must be improved if DSC is employed

## Slide 9: Point when simulating DSC
DSC is Dynamic Sensitivity Control
If just setting CCA Threshold, then any signal over threshold (-90dBm) must be
  received,
  looked at, and then
  only if determined not for me, AND energy <-82dBm is packet dropped
  Time is wasted
DSC sets the RX Sensitivity
  If received signal below the DSC setting, it is simply not seen.
  No time wasted

## Slide 10: Conclusion
In the Enterprise Scenario DSC should improve the area throughput in both 4 channel and 9 channel cases
Legacy in 4 and 9 channels results in complete overlap
4 channel will still have overlapping STAs and reduced SNIR for APs, but uses 80MHz channels
9 channel will have no overlapping STAs but uses 40MHz channels.
In either case, DSC should show an improvement over legacy sensitivity and CCA threshold settings.
Well worthwhile simulating the two conditions with DSC