## Slide 1: L-Preamble Issues for UL-OFDMA
Date: 2015-05-08
Authors:

## Slide 2: Abstract
The inclusion of the legacy preamble (L-STF, L-LTF and L-SIG) in HE PPDU were agreed at the January 2015 meeting.
However, the legacy preamble part of PPDU for UL-OFDMA sent by multiple STAs will occupy the same band (e.g. 20MHzBW) at the same timing.
This submission analyzes feasibility of this overlapped L-Preamble, especially about L-STF, in the same band at the same timing.

## Slide 3: Overlap of L-Preamble (UL-OFDMA)
Data2
Data1
TX from STA1
TX from STA2
RX on the AP side
Overlap of preamble will happen.
UL-Data (STA1)
UL-Data (STA2)
UL-Data (STA2)
This will also happen in the case of ACK/BA transmission for MU DL-OFDMA if sub-channel based ACK is adopted.
…
UL-Data (STA-n)
~
UL-Data (STA1)

## Slide 4: Time Difference of Arrival (Overlapping L-STF)
Copied from IEEE std. 802.11-2012
t1
t2
t3
t4
t5
t6
t7
t8
t9
t10
8us
From STA1
t1
t10
From STA2
From STA3
t1
t10
t2
....
t3
It’s obvious to have some time differences of arrival among transmitted frames.
+
What will the mixed L-STF be?

## Slide 5: Effect of Arrival Time Difference
t1
t2
t3
t4
t5
t6
t7
t8
t9
t10
From
STA1
T/2 = 0.1ns
From
STA2
t2=0.1ns
It’s almost impossible for each STA to adjust signal arrival timing on the AP side for matching their phases among their signals for UL-OFDMA.
(f = 5.0GHz)
There is a phase shift of 180 degrees between STA1’s and STA2’s L-STF only when the arrival time difference is 0.1 ns.

## Slide 6: What will the mixed L-STF be?
I
Q
STA1
STA2
When there is a phase shift of 180 degrees between STA1’s and STA2’s L-STF, signal constellation may appear as the left figure.
How can the AP synchronize with this mixed signal?
It’s not feasible for AP to obtain synchronization from the overlapped L-STFs sent by MU STAs for UL-OFDMA.
e.g. Signal constellation

## Slide 7: Possible Solutions
Header part of PPDUs for UL-OFDMA should not be overlapped in frequency domain. Possible solutions are:
1. To define narrowed L-Preamble
2. Not to use L-Preamble format
N L-preamble
N L-preamble
N L-preamble
N L-preamble
HE header
HE header
HE header
HE header
UL Data (STA1)
UL Data (STA2)
UL Data (STA3)
UL Data (STA4)
e.g.
5MHz
5MHz
5MHz
5MHz
HE header
HE header
HE header
HE header
UL Data (STA1)
UL Data (STA2)
UL Data (STA3)
UL Data (STA4)
5MHz
5MHz
5MHz
5MHz
e.g.
Issues:
Detection by legacy devices
Frame reception with arrival timing differences
Issues:
Frame protection
Frame reception with arrival timing differences

## Slide 8: Possible(?) Preamble Design for 5MHzBW Inheriting L-Preamble Format
L-LTF
Preamble for non-HT (11a)
Possible preamble for 5MHzBW
Subcarrier
Index
Subcarrier
Index
Freq.
Will this design work well for legacy devices to detect these frames ?
L-LTF

## Slide 9: Available number of multiplex
An AP needs correlation power for detect and synchronize a narrowed band frame. There may be a limitation for available number of transmitters for UL-OFDMA.
2?
4?
8?

## Slide 10: Example of UL-OFDMA Procedure
L-Preamble
HE-header
Trigger
frame
AP
STAs
L-Preamble
HE-header
ACK/BA for MU
UL Data (STA1)
UL Data (STA2)
UL Data (STA3)
UL Data (STA4)
L-SIG TXOP Protection
Necessary header for UL-OFDMA
Time
Is this part needed?
with
without
L-Preamble format
L-Preamble format

## Slide 11: Summary
It’s not feasible to use 20MHzBW L-preamble for UL-OFDMA transmission.
   It is required to define header in narrower bandwidth to avoid overlap in the frequency domain for MU UL-OFDMA PPDU reception on the AP side.
Further discussions are necessary to reach a TG consensus about requirements for narrowed header.

## Slide 12: Straw Poll (1)
Do you agree to modify the current sentence in Spec Framework Document as follows?
An HE PPDU shall include the legacy preamble (L-STF, L-LTF and L-SIG), duplicated on each 20 MHz, for backward compatibility with legacy devices, except the case of narrower bandwidth (<20MHz) transmission for UL-OFDMA.
Y/N/A=
Y/N/A =

## Slide 13: Straw Poll (2)
Do you agree to add the following text into Spec Framework Document?
PPDU header for UL-OFDMA transmission shall be defined for narrower bandwidth (<20MHz).
Y/N/A =

## Slide 14: Straw Poll (3)
Do you agree to add the following text into Spec Framework Document?
The amendment shall define L-SIG TXOP Protection by a trigger frame(TBD) to mitigate frame collisions during UL-OFDMA procedure.
Y/N/A =

## Slide 15: References
11-13/1388r0, “Uplink multi-user transmission”
11-15/0378r1, “Channel Sensing in UL-OFDMA”
11-15/0354r1, “Bandwidth granularity on UL-OFDMA data allocation”
11-15/0132r4, “Specification Framework for TGax”