## Slide 1: Enhancing Performance of Hybrid-ARQ with Linear Constellation Precoding
Date: 2015-05-03
Authors:

## Slide 2: Agenda
Abstract
Existing Schemes
  Code Combining
  Constellation Rearrangement
New Scheme LCP-HARQ
Bit Error Rate Comparison
Throuhput Comparison
Conclusion
References

## Slide 3: Abstract
In this work we propose a novel hybrid-ARQ scheme, which outperforms Code combining (CC) and Constellation rearrangement (CoRe) in both packet error rate performance and transmission throughput over a wide range of SNR values.
The proposed scheme uses linear constellation precoding (LCP) to construct symbol vectors for transmission and re-transmissions.

## Slide 4: Code combining (CC)-HARQ [Chase1985]
Same information is sent in successive retransmissions and maximal ratio combining (MRC) is done at the receiver to decode the data.

## Slide 5: Constellation Rearrangement (CoRe) [Wengerter2004]
Observation:
Different protection levels are offered to different bits in higher order modulations.
Example (16-QAM):
Two of the four bits in a symbol have a higher probability of error than the other two bits.
CoRe:
Average the reliability of different bits over successive transmissions by swapping the position and/or negation of the least signiﬁcant bits (LSB).

## Slide 6: CoRe (cont.)
CoRe Example:
Adopted in 3G and 4G communication standard
  HSDPA transmission mode of the universal mobile telecommunications systems (UMTS) [3GPP],
  WiMax IEEE 802.16m.

## Slide 7: New Scheme LCP-HARQ
A distinct vector is chosen from a pre-constructed codebook for transmission of every B input information bits, and elements of this vector are transmitted one by one in case a NACK is received from the destination.

## Slide 8: Codebook Construction
Let be the set of all possible vectors of length L with
components taken from a conventional N-point QAM constellation.
Code book at the transmitter
Linear precoding matrix

## Slide 9: Example
Target: 4 bits/transmission
No. of vectors (M) = 16
N = 4, L = 2
Pre-coding matrix
Target: 6 bits/transmission
No. of vectors (M) = 64
N = 4, L = 3
Pre-coding matrix

## Slide 10: Advantage of LCP-HARQ
The LCP-ARQ scheme achieves averaging effect with application of LCP.
Example: 6 bits (b1b2…b5b6) per transmission
b1b2
b3b4
b5b6
1st time
2nd time
3rd time

## Slide 11: Bit Error Rate Comparison
AWGN Channel
CC and CoRe 64-QAM
LCP-HARQ (N = 4, L = 3)
  New scheme outperforms CC and CoRe schemes by 6.5 dB and 4.2 dB,
  respectively, at target BER = 10-3.

## Slide 12: Bit Error Rate Comparison (cont.)
Rayleigh Channel
CC and CoRe 64-QAM
LCP-HARQ (N = 4, L = 3)
  New scheme outperforms CC and CoRe schemes by 5 dB and 2.5 dB,
  respectively, at a target BER = 10-3.

## Slide 13: Throughput Comparison
Rayleigh Channel
CC and CoRe 64-QAM
LCP-HARQ (N = 4, L = 3)
Throughput
,
where Average number
of transmissions per packet.
New scheme has better throughput as compared to CC and CoRe for SNR range = 10-25 dB.

## Slide 14: Conclusion
New scheme with
  ML decoder complexity: M search operations
  (Same as CC-HARQ and CoRe-HARQ )
  Outperforms CC and CoRe schemes by 6.5 dB and 4.2 dB, respectively, at target BER = 10-3.
  Higher throughput as compared to CC and CoRe schemes.

## Slide 15: References
[Chase1985] D. Chase, “Code combining–a maximum-likelihood decoding approach for combining an arbitrary number of noisy packets,” IEEE Trans. Commun., vol. 33, no. 5, pp. 385–393, May 1985.
[Wengerter2004] C. Wengerter, A. von Elbwart, and E. Seidel, “Constellation rearrangement: Enhancement for multilevel modulation formats and transmit diversity,” Wireless Personal Communications, vol. 29, no. 1-2, pp. 35–45, 2004.
3GPP, Universal Mobile Telecommunications System (UMTS);. Multiplexing and Channel Coding (FDD). ETSI, 2002.
Panasonic, “Enhanced HARQ method with signal constellation rearrangement,” in TSG-RAN Working Group 1 Meeting, Las Vegas, USA, February 2001.