## Slide 1
Date: 2015-05-12
Authors:
802.11aj (45 GHz) Channel Access and BSS Operation
Weimin Xing, ZTE Corp.

## Slide 2: Abstract
Base on the channelization of 45GHz, we propose a framework for the channel operation in China 45 GHz frequency bands for 802.11aj, meeting the requirements specified in the functional requirements documents.
Further, we also propose a basic rules for channel access in China 45 GHz frequency bands for 802.11aj.
Weimin Xing, ZTE Corp.

## Slide 3
45 GHz Channelization
Weimin Xing, ZTE Corp.

## Slide 4: China 45 GHz Spectrum Allocation and Channelization
CH 1
CH 1
B0 = 1080 MHz
B0 = 540 MHz
CH 2
CH 3
CH 4
CH 5
CH 6
CH 7
CH 8
CH 9
CH 10
42.3 GHz
47.0 GHz
47.2 GHz
48.4 GHz
CH 2
CH 3
CH 4
CH 5
Frequency band: 42.3~47.0 GHz, 47.2~48.4 GHz
Bandwidth: 1080 MHz, 540 MHz
Frequency tolerance: 100×10-6
Maximum transmit power at antenna port: 20dBm
Maximum EIRP: 36dBm
Weimin Xing, ZTE Corp.
Channelization:
  Allows for 10 independent BSSs using channel bandwidth of 540 MHz.
  Allows for 5 independent BSSs using channels bandwidth of 1080 MHz.
  A mixture of both should be enough for logical channel requirements in most deployment scenarios.

## Slide 5
45 GHz BSS Operation
Weimin Xing, ZTE Corp.

## Slide 6: Some Requirements for 45 GHz
User experience for 45 GHz should be in consistence with that of existing 802.11 systems.
A maximum target PHY transmission rate over Gbps to be met as specified in the FRD.
Operating usages like video streaming, file transfer, internet access etc.
Weimin Xing, ZTE Corp.

## Slide 7
Scope of BSS Operation (1/2)
Channel Setup
efficiently support 45 GHz channelization
  PCP/AP may select to operate in one of the ten 540 MHz channels or one of the five 1080 MHz channel when it starts.
  PCP/AP may dynamically change its channel number with corresponding change in channel bandwidth.
  For a BSS occupying a 1080 MHz bandwidth channel, data transfer can be through 540 MHz bandwidth or 1080 MHz bandwidth
Weimin Xing, ZTE Corp.

## Slide 8
Scope of BSS Operation (2/2)
OBSS Mitigation
When two BSSs have devices overlapping in service area, or movement of BSSs to a common service area,
  Smooth translation to co-operative interference mitigations.
  Transparent merging of different BSSs using co-operative interference mitigations.
Weimin Xing, ZTE Corp.

## Slide 9: Channel Operation Solutions
Requirements
  Meet objectives of proposed channel access.
  Efficiently fulfills the requirements for co-operative interference mitigations in densely populated environments.
  Efficiently handle OBSS mitigations.
A general channel operation solution was proposed in next few slides.
NOTE, the details of the general channel operation solution is not yet completed and we call for interested parties to contribute.
Weimin Xing, ZTE Corp.

## Slide 10: Proposed solution (2/4)
The primary channel of a 1.08 GHz channel is predefined, e.g., Channel 2 is the primary channel within Channel 1
If a PCP/AP intends to start its BSS in a free 540 MHz channel, it selects the primary channel as the first option to transmit its beacon/notification frames. If occupied, it selects the secondary channel.
If both 540 MHz channels are occupied but no PCP/AP operates in this 1.08 GHz channel, a PCP/AP may select either primary or secondary channel to start its BSS.
If both 540 MHz channels are occupied and there exists at least one PCP/AP operates in this 1.08 GHz channel, a PCP/AP must select the primary channel to start its BSS.
Weimin Xing, ZTE Corp.

## Slide 11: Proposed solution (2/4)
If a PCP/AP intends to start its BSS in a free 1.08 GHz channel, it will transmit beacon/notification frames in the primary channel only.
If no 1.08 GHz channel is free, a PCP/AP select the 1.08 GHz operating channel based on the following priority orders:
  The secondary channel is free.
  All the existing PCPs/APs operate in the primary channel only.
  All the existing PCPs/APs either operate in the primary channel or operate in the secondary channel.
Weimin Xing, ZTE Corp.

## Slide 12: Proposed solution (3/4)
Suppose that a PCP/AP 1 operates in a 1.08 GHz Channel, e.g., Channel 1, with transmitting beacon/notification frames in a predefined or selected primary channel only, e.g., Channel 2.
  Another PCP/AP 2 that intends to operate in 1.08 GHz channel must also transmit beacon/notification frames in Channel 2.
  Another PCP/AP 3 that intend to operate in 540 GHz channel can start in Channel 2 only.
  Switch to another unoccupied channel
Weimin Xing, ZTE Corp.

## Slide 13: Proposed solution (4/4)
Suppose that PCP/AP 1 operates in a 540 GHz Channel.
  Another PCP/AP 2 that intends to operate in 1.08 GHz channel must transmit beacon/notification frames in the predefined or selected primary channel, e.g., Channel 2.
    If PCP/AP 1 was operating in Channel 3, PCP/AP 2 must notify the PCP/AP 1 to switch its BSS to Channel 2 or at least transmit beacon/notification frames in Channel 2. (How to notify is TBD.)
  Another PCP/AP 3 that intend to operate in 540 GHz channel may select either Channel 2 or Channel 3 to start if no PCP/AP operates in Channel 1 now; otherwise, it can only start in Channel 2.
  Switch to another unoccupied channel.
Movement of PCPs/APs is TBD.
Weimin Xing, ZTE Corp.

## Slide 14
45 GHz Channel Access
Weimin Xing, ZTE Corp.

## Slide 15
Scope of Channel Access
Channel Access:
    Channel access mechanisms: contention based access, contention free access
    Dynamic allocations of channel resources.
    Multi-bandwidth: dynamic bandwidth negotiation
Weimin Xing, ZTE Corp.

## Slide 16
Channel Access mechanisms
Supports reservation based allocations as well as contention based allocations
    Allocate SPs for devices so that the quality of service (QoS) is guaranteed when required.
    Allocate CBAPs for contention based access to cater to intermittent channel access.
Weimin Xing, ZTE Corp.

## Slide 17
Dynamic allocation
Supports dynamic allocate/truncate/extend SPs or CBAPs
    Dynamic allocation of channel resources is employed to allocate channel time during scheduled allocations.
    A STA truncates an allocation to release the remaining time in the allocation.
    Dynamic extension of allocation to extend the allocated time in the current allocation. The additional time can be used to support variable bit rate traffic, for retransmissions or for other purposes.
Weimin Xing, ZTE Corp.

## Slide 18
Dynamic bandwidth operation
Dynamic bandwidth negotiation:
Dynamic bandwidth operation is needed when multi-bandwidth is introduced to 45GHz
    Dynamic bandwidth operation is proposed in IEEE 802.11ac, which allows narrower bandwidth transmission if one or more secondary channels are sensed busy.
    The RTS/CTS exchange is used to negotiate a potentially channel width for subsequent transmissions within the current TXOP.
Weimin Xing, ZTE Corp.

## Slide 19
Dynamic Bandwidth Operation for 45GHz
  Dynamic bandwidth operation:
    With dynamic bandwidth subfield set to 1, RTS in duplicate format is transmitted over 1080 MHz channel that is sensed free at the initiator.
    If network allocation vector(NAV) indicates idle at the responder:
      If clear channel assessment(CCA) on the secondary channel has been idle for a point coordination function interframe space(PIFS) period prior to the start of the RTS frame, CTS frame in duplicate format is sent over the 1080 MHz channel.
      Otherwise, CTS is sent only on the primary 540 MHz channel.
    If NAV indicates busy at the responder, no CTS is responded.
    Initiator transmits data only over channel indicated free by CTS.

## Slide 20
Static Bandwidth Operation for 45GHz
  Static bandwidth operation :
    With dynamic bandwidth subfield set to 0, RTS in duplicate format is transmitted over 1080 MHz channel that is sensed free at the initiator.
    If NAV indicates free at the responder and CCA on the secondary channel has been idle for a PIFS period prior to the start of the RTS frame , CTS frame in duplicate format is sent over the 1080 MHz channel.
    If the secondary channel has been sensed busy at the responder, the initiator will not receive CTS and then it shall invoke the back-off procedure to retransfer the RTS.

## Slide 21
The Flowchart of Dynamic Bandwidth
Dynamic bandwidth operation for IEEE 802.11aj is illustrated in the flowchart.

## Slide 22
Allow STAs that are not targeted by the AP to enter doze state until the end of the TXOP：
  On receipt of a PPDU, the STA determines that the COLOR in the RXVECTOR parameter does not match the COLOR indicated by the AP to which the STA
  is associated.
  With the matching COLOR, the RXVECTOR parameter PARTIAL_AID is not equal to 0 nor does it match the STA’s partial AID.
  With the matching partial AID, the RA in the MAC header of the corresponding frame that is received correctly does not match the MAC address of the STA.
  540 MHz STAs receive a Beacon frame or a Set PCO frame that contains the PCO Phase field equal to 1.
  In a received PSMP frame, the STA finds that the STA_AID field is not its AID nor does the PSMP Group Address ID match its Group Address .
  The STA receives a frame intended for it with the More Data field equal to 0 and the Ack Policy subfield in the QoS Control field is equal to No Ack or sends an acknowledgment if Ack Policy subfield is not equal to No Ack.
TXOP Power Save

## Slide 23: Proposed changes
Base on Draft P802.11REVmc D4.0, we proposed to add/modify the following subclauses in the complete proposal of 802.11aj (45GHz)
9.xx QMG channel access
  9.xx.1 General
  9.xx.2 Access period within a BI
  ......
  9.xx.a CBAP transmission
  9.xx.b SP transmission
  9.xx.c Dynamic bandwidth negotiation
  …….
10.xx QMG BSS Operation
  10.xx.1 Basic QMG BSS functionality
  10.xx.2 Channel selection methods for a QMG BSS
  10.xx.3 Scanning requirements for QMG STA
  ……
  10.xx.a 540/1080MHz QMG BSS operation
  10.xx.b Channel switching methods for a QMG BSS
  10.xx.c Communicating 540/1080MHz BSS coexistence information

## Slide 24: Conclusion
We propose a framework for the BSS operation and channel access in China 45 GHz, which include:
BSS operation:
  One 540 MHz channel is defined for each 1080 MHz channel, e.g. Channel 1/3/5/7/9 are defined as primary channel;
  A PCP/AP working on 540 MHz channel shall transmit beacon on its working channel;
  A PCP/AP working on 1080 MHz channel shall transmit beacon on the primary 540 MHz channel of its working channel
  Some compliance mechanisms may be employed to immigrate the interference from a BSS on the secondary 540 MHz channel to a 1080 MHz BSS
Channel access:
  Supports reservation based allocations as well as contention based allocations
  Allow dynamic allocate channel time for data transfer
  Supports dynamic bandwidth operation like 802.11ac

## Slide 25: Reference
IEEE 802.11-13/1365r2 45 GHz Spectrum Allocation in China
Weimin Xing, ZTE Corp.

## Slide 26
Thank YOU
Weimin Xing, ZTE Corp.

## Slide 27
Appendix: Channel setup scenairos
Weimin Xing, ZTE Corp.

## Slide 28: Channel Setup Scenario 1
Pre-requisite
  No BSS established within a 1080 MHz channel, Channel 1 (as illustrated).
Possible channel setup choices for incoming PCP/AP
  Operate within either of the 540 MHz channels (Channel 2 or Channel 3).
  Operate in the 1080 MHz bandwidth channel, Channel 1.
    Option 1: Use of fixed primary channel (i.e. Channel 2) for BSS control.
    Option 2: PCP/AP dynamically choose between Channel 2 or Channel 3 as the primary channel.
Weimin Xing, ZTE Corp.

## Slide 29: Channel Setup Scenario 2
Pre-requisite:
  One BSS established within either Channel 2 or Channel 3.
Possible channel setup choices for incoming PCP/AP
  Operate within the free 540 MHz channel.
  Search for a free 1080 MHz bandwidth channel (i.e. Channel 4, 7… etc) if so desired.
  Operate within the 1.08GHz channel and share the spectrum with existing 540MHz BSS.
Weimin Xing, ZTE Corp.

## Slide 30: Channel Setup Scenario 3 (1/3)
Pre-requisite:
  All possible channels are occupied.
Possible channel setup choices for incoming PCP/AP
  Operate within any 540MHz channel and share the spectrum with existing 540/1080MHz BSS
  Operate within any 1.08GHz channel and share the spectrum with existing 540/1080MHz BSS
Weimin Xing, ZTE Corp.

## Slide 31: Channel Setup Scenario 3 (2/3)
Some considerations for spectrum sharing method in Scenario 3
  For easy interference mitigations.
  Guaranteed QoS requirements
  Protected transmission period for network co-ordination.
  Fairness among different BSSs.
    Splitting of 1080 MHz channel to two 540 MHz channels.
    Interleaved time block sharing of spectrum resources through coordination between PCP/APs.
    Clustering mechanism with interleaved protected period for different BSSs.
Weimin Xing, ZTE Corp.

## Slide 32: Channel Setup Scenario 3 (3/3)
Weimin Xing, ZTE Corp.