## Slide 1: Multi-STA BA for SU Transmissions
Date: 2015-05-10
Authors:

## Slide 2
Abstract
In this contribution we evaluate the potential MAC efficiency gain when using multi-STA BA to acknowledge UL SU transmissions.

## Slide 3: Table of Contents
Introduction
Legacy BA/ACK
Multi-STA BA for SU Transmissions
MAC Efficiency Analysis Results
Conclusions

## Slide 4: Introduction
A HE STA may send SU transmissions, particularly, in the uplink direction
  HE STAs may have many packets buffered
  HE STAs may not be capable of UL MU transmissions, e.g., a HE STA may be capable of receiving DL MU-MIMO frames, but not capable of transmitting UL MU-MIMO frames
BA/ACK for each individual STA causes high overhead
Multi-STA BA may be used to provide higher MAC efficiency for SU transmissions
  Multi-STA BA has been accepted into SFD [1]
  Proposed in [2] for acknowledging UL MU transmissions

## Slide 5
Legacy ACK:
  ACK sent SIFS after each packet
HT-Immediate BA
  BA sent SIFS after A-MPDU
Legacy Immediate SU BA/ACKs
STA1
Data
ACK
STA2
Data
ACK
STA1
A-MPDU
BA
STA2
A-MPDU
BA

## Slide 6
HT-Delayed BA:
  BAR included in A-MPDU
  BA sent with unspecified delay
ACK/BA to individual STAs still represent significant overhead
May be optimized for higher MAC efficiency
Legacy Delayed SU BA
STA1
A-MPDU
BA
BA
BAR
STA2
A-MPDU
BAR
ACK
ACK

## Slide 7
Multi-STA BA has been introduced to acknowledge UL MU transmissions [2]
The same multi-STA BA may be used to acknowledge UL SU transmissions to provide higher MAC efficiency
When compared to Legacy Delayed SU BA, multi-STA BA is more efficient due to
  Less inter frame spaces
  Less medium access contention
  More compact frame design
Multi-STA BA for SU Transmissions
STA1
A-MPDU
Multi-STA
ACK/BA
STA2
A-MPDU
STA3
A-MPDU
STA4
A-MPDU

## Slide 8
MAC Efficiency for Multi-STA BA
MAC efficiency gain (G) in percentage for Multi-STA BA over legacy BA is defined as:
( - 1) x 100
T_Legacy_BA: total time consumed to transmit data and BA when legacy BA is used, namely HT-Immediate BA and HT-Delayed BA(shown on Slide 5 and 6)
  T_Imm_BA = (DIFS + BO + Data + SIFS + BA) x N
  T_Delayed_BA = (DIFS + BO + A-(Data+BAR) + DIFS + BO + BA +SIFS + ACK) x N
T_Multi_STA_BA: total time consumed to transmit data and BA when Multi-STA BA is used (shown on Slide 7)
    T_Multi_STA_BA = (DIFS + BO + Data)*N + (DIFS + BO + MU_BA)

## Slide 9
Assumptions for UL SU Data transmissions:
  All the users have the same data packet size and the same amount of data
  All UL SU data transmissions are A-MPDUs
  All the users use the same MCS
  Control frames, i.e., BA, ACK, Multi-STA BA use MCS0
Assumptions for DL BA transmissions:
  Scenario 1: HT-Immediate BA (Slide 5)
  Scenario 2: HT-Delayed BA (Slide 6)
  Scenario 3: Multi-STA BA (Slide 7)
MAC Efficiency Analysis Assumptions

## Slide 10
Description | Value
Contention duration | 27 µs (3 time slots)
Preamble duration | 48 µs
Block ACK duration | 96 µs
# of users | 2, 4 , 6 , 8
OFDM symbol duration (including CP) | 16 µs
# of data sub carriers | 234
Multi_STA BA duration (2/4/6/8 users) | 112/128/160/192 µs
MAC Efficiency Analysis Assumptions
L-STF | L-LTF | L-SIG | HE-SIG-A | HE-LTF
8µs | 8µs | 4µs | 12µs | 16µs
Preamble duration 48us [1]

## Slide 11
Observations:
MAC efficiency gain (G) increases when a Multi-STA BA is used to acknowledge higher number of SU transmissions
MAC efficiency gain of up to 76% for 8 users compared to legacy HT-Delayed BA, and MAC efficiency gain of up to 39% for 8 users when compared to legacy HT-Immediate BA
MAC efficiency gain (G) for Multi-STA BA over legacy BA
Chart: MSDU size 500 Bytes, MCS7
| 2 | 4 | 6 | 8
T_Imm_BA/T_Mutli_STA_BA | 9.8266 | 29.3984 | 35.8221 | 39.2792
T_Delayed_BA/T_Multi_STA_BA | 39.499 | 64.3587 | 72.5179 | 76.909

## Slide 12
Observations:
MAC efficiency gain (G) for Multi-STA BA decreases when the packet size increases
When Multi-STA BA is used to acknowledge 4 UL SU transmissions, a MAC efficient gain of up to 91% can be achieved when compared to HT-Delayed BA, and a MAC efficiency gain of up to 38% can be achieved when compared to using HT-Immediate BA
MAC efficiency gain (G) for Multi-STA BA over legacy BA
Chart: 4 Users in Multi-STA BA, MCS7
| 100 | 500 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500 | 4000 | 4500 | 5000
T_Imm_BA/T_Multi_STA_BA | 37.5907 | 29.3984 | 22.7792 | 19.4883 | 17.0283 | 14.5751 | 13.1539 | 11.6404 | 10.7158 | 9.6895 | 9.0401
T_Delayed_BA/T_Multi_STA_BA | 91.582 | 64.3587 | 49.8681 | 42.6637 | 41.4859 | 31.9077 | 28.7963 | 25.4831 | 23.4588 | 21.2121 | 19.7906

## Slide 13: Other Design Considerations
Multi-STA BA may cause higher delay
  Evaluation may depend on the types of delay
    PHY Delay
    MAC Delay/Queueing delay
    End-to-End delay

## Slide 14: Conclusion
Using Multi-STA BA to acknowledge UL SU transmission can significantly improve MAC efficiency
Trade off may be needed between MAC efficiency gain and delay in designing such a Multi-STA BA algorithm

## Slide 15
References
11-15/0132r4, Specification Framework for Tgax
11-15/0366r2, Multi-STA Acknowledgement