## Slide 1: Inefficiency of 256-FFT per 20MHz
Date: 2015-05-10
Authors:

## Slide 2: Background
According to SFD [1], data symbols in an HE PPDU shall use a DFT period of 12.8 µs and subcarrier spacing of 78.125 kHz.
  256 subcarriers are defined in 20MHz bandwidth.
The longer symbol duration can cause excessive padding in the last OFDM symbol.
  Especially when sending short packets, transmission efficiency drops due to padding
  In STBC cases, the padding overhead becomes larger.
Heejung Yu, Yeungnam Univ./NEWRACOM

## Slide 3: Padding inefficiency
In 11ac, EOF padding in MAC layer and PHY padding was used to fill all data tones in the last OFDM symbol.
When an OFDM symbol contains more data tones (roughly x4), more redundant padding bits may be needed.
  In 80MHz BW, several hundreds redundant data tones can be transmitted to send few bits in the last symbol.
Especially in a short packet case, MAC throughput loss cannot be avoided.
In a STBC case, the last two OFDM symbols have such inefficiency.

## Slide 4: Ratio btw padding bits and data bits (1)
Channel BW = 80MHz
  980 data tones assumed
MCS
  MCS0
  MCS8
MIMO scheme
  1STS
  1STS + STBC
  2STS

## Slide 5: Ratio btw padding bits and data bits (2)
MCS8
1STS
MCS8
2STS
8
8

## Slide 6: Ratio btw padding bits and data bits (3)
MCS0
1STS
MCS0
1STS+STBC
8
8

## Slide 7: Ratio btw padding bits and data bits (3)
To send 1000 bytes data payload in 80MHz BW,
  MCS0 with STBC : 10.25% padding is needed (100 bytes)
  MCS8 with Nsts = 1 : 47% padding is needed (470 bytes)
Large padding bits are needed by when using 12.8us OFDM symbol duration.
As shown in the appendix, MAC throughput can drop significantly due to variation of padding bits.

## Slide 8: Ratio btw padding bits and data bits (4)
 | 40 +44bytes1 | 576+44bytes2 | 1500+44bytes3
MCS0 (80MHz, NSTS = 1) | 45.8% | 8.67% | 3.14%
MCS1 (80MHz, NSTS = 1) | 45.8% | 18.6% | 3.14%
MCS2 (80MHz, NSTS = 1) | 119% | 18.6% | 7.11%
MCS3 (80MHz, NSTS = 1) | 192% | 18.6% | 11.1%
MCS4 (80MHz, NSTS = 1) | 338% | 18.6% | 19.0%
MCS5 (80MHz, NSTS = 1) | 483% | 58.1% | 26.9%
MCS6 (80MHz, NSTS = 1) | 556% | 77.8% | 7.11%
MCS7 (80MHz, NSTS = 1) | 629% | 97.6% | 19.0%
MCS8 (80MHz, NSTS = 1) | 775% | 18.6% | 42.8%
1 IPv4 TCP/IP ACK (without option) : 40 bytes + 4 bytes (A-MPDU header) + 32 bytes (MAC header + FCS) + 3 bytes (LLC header) + 5 bytes (SNAP extension LLC header)
2 Minimum IPv4 datagram size : 567 bytes + 44 (MAC & LLC overhead)
3 Ethernet MTU : 1500 bytes + 44 bytes (MAC & LLC overehead)
Padding bits with typical packets

## Slide 9: Conclusions
12.8us OFDM symbol duration can cause excessive padding and result in throughput loss.
  Especially for OFDM transmission with wide BW, high MCS, and many STSs.

## Slide 10: Straw Poll #1
Do you support the concept
  HE shall include mechanisms to enhance the MAC/PHY padding efficiency for OFDM transmissions using symbol duration of 12.8usec.

## Slide 11: Reference
[1] 11-15-0132-04-00ax-Specification Framework for Tgax
[2] 11-15-0330-01-00ax-OFDMA-numerology-and-structure

## Slide 12: Appendix

## Slide 13: Numerical evaluation: Padding inefficiency
11ac : current frame structure with 0.8us CP
11ax : 12.8us OFDM symbol duration plus 3.2us CP
BW = 20MHz 80MHz
  11ac : 52 data tones 234 data tones
  11ax : 234 data tones 980 data tones
L-STF
8us
L-LTF
8us
L-SIG
4us
HE-SIGA
8us
HE-STF
4us
HE-LTF
16us*Nss
HE-SIG B
16us
HE-DATA
16us * N OFDM symbol

## Slide 14: MCS0, Nsts =1, 80MHz
STBC off STBC on
8
8

## Slide 15: MCS8, 80MHz
Nsts = 1 Nsts = 2
8
8

## Slide 16: MCS8, 20MHz
STBC off STBC on