## Slide 1
SIG Structure for UL PPDU
Date: 2015-05-11
Authors:

## Slide 2: Background
In this contribution, we analyze issues for UL transmission (SU and MU) and propose SIG field structures.

## Slide 3: Background
11ax has added basic SIG field structure in SFD [1]:
  An HE PPDU shall include the legacy preamble (L-STF, L-LTF and L-SIG), duplicated on each 20 MHz, for backward compatibility with legacy devices.
  HE-SIG-A (using a DFT period of 3.2 µs and subcarrier spacing of 312.5 kHz) is duplicated on each 20 MHz after the legacy preamble to indicate common control information.
  Downlink HE MU PPDU shall include HE-SIG-B field, and the number of OFDM symbols of HE-SIG-B field is variable.
Also, 11ax has added UL MU PPDU transmission sequence [1]:
  An UL MU PPDU is sent as an immediate response (IFS TBD) to a Trigger frame (format TBD) sent by the AP.
  HE-PPDU for UL-OFDMA shall support UL data transmission below 20 MHz for an HE STA.
  The amendment shall define a mechanism for multiplexing DL acknowledgements sent in response to UL MU transmissions.

## Slide 4: SIG Field Information
Common control information
  Information needed not only for target receiver but also 3rd party STAs and common information to all scheduled STAs, such as
    Allocated bandwidth
    Packet duration/GI/N_LTF
    COLOR/PAID/GID/TXOP_PS
  May be included in L-SIG and HE-SIG-A fields.
Resource allocation information
  Required only for MU transmission or partial band transmission such as
    Resource allocation structure (map)
    Which STA is scheduled in which subband/spatial_stream
  May be included in either HE-SIG-A or HE-SIG-B field.
User-specific information
  Information for each STA to decode the payload, such as
    MCS/NSTS
    STBC/Beamformed
  May be included in HE-SIG-B field.

## Slide 5: SIG Field for UL MU Transmission
Multiple scheduled STAs shall:
  Set the fields that are RF-combined to the same values.
  Transmits their payloads at a designated resource (frequency subband or spatial stream) only.
For this purpose, the Trigger frame shall indicate at least:
  Common control information
  Resource allocation information
However, depending on SIG-field structure, user-specific information may or may not be included in the Trigger frame.
  If user-specific information is RF-combined in the SIG field, it has to be preset by the serving AP.
  If user-specific information is indicated in orthogonal SIG field, each participating STA can choose based on its preference.

## Slide 6: User-Specific-Information: RF-Combined
HE-SIG-B field is encoded either for each 20MHz, or for whole transmission bandwidth.
A single HE-SIG-B field may include every allocated STA’s user-specific information.
  Serving AP has to indicate every scheduled STA’s user-specific information such that every scheduled STA can encode HE-SIG-B properly.
As HE-SIG-B information in UL MU transmission is preset by the AP, the receiver (AP) already knows this information.
  It implies that not the transmitter but the receiver (AP) determines the MCS and NSTS of the frame, and the transmitter cannot adjust these values.

## Slide 7: User-Specific-Information: RF-Combined
MCS/NSTS decision by an AP
  As the receiver can identify better channel information such as received signal power, channel correlation, it is better for a receiver to decide the MCS/NSTS.
  In case there was no prior packet exchange within reasonable time duration, it’s hard for the receiver to figure out the right MCS/NSTS value.
HE-SIG-B field design
  As the target receiver (AP) knows all HE-SIG-B information, HE-SIG-B field can be omitted.
  If HE-SIG-B field is omitted, 3rd party STAs cannot decode the payload correctly.
    Still all required common control information can be identified by decoding HE-SIG-A field.
  3rd party STAs cannot identify up-to-date NAV (Duration) information.
    If 3rd party STAs decoded Trigger frame correctly, this issue can be resolved.
    Or, HE-SIG-A for UL MU transmission may include these information.
Pros
  HE-SIG-B field can be omitted, which can reduce the signaling overhead.
Cons
  MCS/NSTS decision may not be optimized if there’s no prior packet exchange.

## Slide 8: User Specific information: Separate Encoding
HE-SIG-B occupies the same subband that payload occupies using 12.8usec OFDM symbol (excluding GI).
  Each allocated subband has its own HE-SIG-B field.
As HE-SIG-B occupies orthogonal resource, each transmitter can choose its own preferred user-specific values for transmission.
  Still every participating STA shall follow basic resource allocation structure that is indicated by the Trigger frame.
  AP may indicate the preferred MCS/NSTS in the Trigger frame for reference, but the participating STA may adjust based on its own decision as long as the payload fits in the allocated resource.

## Slide 9: User Specific information: Separate Encoding
MCS/NSTS decision by the STA
  Each STA can utilize channel reciprocity in estimating the UL channel quality.
    Interference level at the AP cannot be estimated correctly.
  Each STA can utilize the up-to-date channel information (Trigger frame reception) for UL transmission
    But, hard to get information for NSTS > 1.
  However, as resource allocation and packet duration is already preset by the AP based on its own knowledge and there’s no room for each participating STA to modify/adjust this, gain by adjusting the MCS from the transmitter is not high.
Pros
  Can utilize up-to-date channel information for MCS selection.
Cons
  As each HE-SIG-B block requires basic overhead (such as Tail bits and CRC), overall HE-SIG-B overhead is higher.

## Slide 10: Proposals
Comparing the two possible structures for HE-SIG-B for UL MU transmission, our observation is
  Allowing each scheduled STA to choose its own user-specific parameters does not give meaningful gain considering restrictions in UL MU transmission.
  Rather not including HE-SIG-B in UL MU transmission will improve overall system efficiency.
Therefore, we propose:
  AP decides user-specific information and indicates in the Trigger frame.
  HE-SIG-B field is not included in the UL MU PPDU.

## Slide 11: SIG Field for UL SU Transmission
UL SU transmission can happen without a Trigger frame.
Two possible cases for UL SU transmission:
  Full band transmission
    PSDU occupies entire transmission bandwidth.
  Partial band transmission
    Legacy preamble occupies entire transmission bandwidth.
    PSDU occupies only part of the transmission bandwidth
Full band transmission
Partial band transmission

## Slide 12: SIG Field for UL SU Transmission
Full band transmission
  As every resource is occupied by a single STA, there’s no need to indicate additional resource allocation information.
  HE-SIG-A may be enough to indicate common control and user-specific information similar to 11ac.
Partial band transmission
  As not all resource is occupied by the transmitter, resource allocation information is needed for the receiver to properly decode the payload.
  HE-SIG-A alone is not enough to indicate all common control, resource allocation, and user-specific information.
  Use of MU PPDU frame format may be a better-fit (with single STA allocation).

## Slide 13: Proposals
For UL SU transmission,
  HE-SIG-B is not required if PSDU occupies entire transmission bandwidth.
  HE-SIG-B is needed if PSDU does not occupy entire transmission bandwidth to indicate allocated resource.

## Slide 14: SP 1
Do you agree to add to the TG Specific Framework:
  3.y.z UL MU PPDU shall not include HE-SIG-B field if it is sent as an immediate response to a Trigger frame sent by an AP.

## Slide 15: SP 2
Do you agree to add to the TG Specific Framework:
  3.y.z UL SU PPDU shall not include HE-SIG-B field.

## Slide 16: SP 3
Do you agree to add to the TG Specific Framework:
  3.y.z UL MU PPDU may include HE-SIG-B field if it is not an immediate response to a Trigger frame and sent by a single STA.

## Slide 17: References
[1] 11-15/0132r4, “Specification Framework for TGax”.