## Slide 1
Considerations on LTF Sequence Design
Date: 2015-05-10
Authors:

## Slide 2: Introduction
LTF-related decisions made in previous meetings
  The HE-LTF shall adopt a structure of using P matrix in the data tones as in 11ac. In the data tones, every space-time stream is spread over all HE-LTF symbols by one row of the P matrix as defined in 11ac. Different space-time streams use different rows in P matrix.
  The HE PPDU shall support the following LTF modes:
    HE-LTF symbol duration of 6.4us excluding GI
      Equivalent to modulating every other tone in an OFDM symbol of 12.8 µs excluding GI, and then removing the second half of the OFDM symbol in time domain
    HE-LTF symbol duration of 12.8 µs excluding GI

## Slide 3: Considerations in PAPR
Peak-to-Average Power Ratio (PAPR)
  PAPR affects cost of Tx Power Amplifier (PA) and Rx receiver dynamic range related function blocks
  With a lower PAPR in LTF, a transmitter can acquire more room for power boosting
  It is known to be especially high if sequence is repeated in frequency domain and that a part of a base sequence has completely a different PAPR from the base one
Accompanying signals’ PAPRs as a reference
  HE LTF is transmitted with a single RF chain of legacy preambles and data
  Therefore, PAPRs of HE LTF should be designed to be comparable with those of L-STF, L-LTF, and L-SIG, and the design should consider statistic PAPRs of HE data portion

## Slide 4: Considerations in PAPR (cont’d)
Observations in PAPRs of legacy and 12.8us OFDM symbol data
  L-STF and L-LTF have good PAPRs for 20MHz and 80MHz, but the phase rotation with two phases doesn’t provide much gain, as shown in 40MHz
  Considering PAPRs of legacy and data, it seems reasonable to design LTF sequences to have near the minimum PAPR of data, which is comparable to PAPRs of L-LTF
    At least, less than the median PAPR of data
Bandwidth | L-STF [dB] | L-LTF [dB]
20 MHz [ 1 ] | 2.2394 | 3.2245
40 MHz [1 +j] | 5.2497 | 5.8208
80 MHz [1 -1 -1 -1] | 4.3480 | 5.3827
Note: the values in square brackets “[ ]” are phase rotation values used to reduce the overall PAPR
PAPR of Legacy
PAPR of Data

## Slide 5: Considerations in Sequence Design
OFDMA
  More sizes, especially small sizes of LTF sequences are needed for OFDMA
Wider bandwidth
  New sequences should be designed for 40, 80, and 160MHz in 256-FFT
Compressed LTF (2xLTF)
  A set of half-sized LTF sequences are required

## Slide 6: LTF Transmissions in OFDMA
Transmission only in the allocated subband in UL OFDMA
  In downlink, AP may transmit LTF in the whole operating bandwidth, i.e., 20MHz, 40MHz, or 80MHz
  However, in uplink, it’s natural that each STA transmits LTF only in the allocated subbands
From STA1
To STA1
To STA2
To STAn
…
20MHz
DL OFDMA PPDU transmitted in AP
…
From STA1
From STA2
From STAn
…
20MHz
UL OFDMA PPUD received in AP
…
Data multiplexed in frequency
From STA2
From STAn
LTFs
LTFs multiplexed
in frequency
Data multiplexed in frequency

## Slide 7: Design for OFDMA (cont’d)
Full-band design
  Design a LTF sequence in 20, 40, or 80MHz, and chop it up depending on the STA’s allocated subband
  Less sets of LTF sequences and simple LTF receiving procedure
  But, not optimized PAPR for subband in UL OFDMA
Per-subband design
  LTF sequence design for each subband size, e.g., 2.5MHz, 5MHz
  More optimized PAPR performance in subband
The per-subband design seems to be natural, which is a similar way to HT and VHT designs
1, -1, 1, ..0, 0, 0, …,1, -1,1
A LTF sequence designed in 20MHz
1,.,1
1, …,1
1,.,1
2.5MHz
Seq.
2.5MHz
Seq.
5MHz
Seq.
Same length but different sequence, i.e., different PAPRs
1,.,1
1, …,1
1, -1, …,-1, 1
1, -1, 1, ..0, 0, 0, …,1, -1,1
7.5MHz Seq.
5MHz Seq.
2.5MHz Seq.
10MHz Seq.
LTF sequences designed for every possible subband sizes
Chop up the base seq. depending on a subband size and position
Choose one depending on a subband size

## Slide 8: Design For Wider Bandwidths
LTF sequences for 40, 80, and 160MHz
  Concatenation of 20MHz LTF sequences with the optimal missing tone-fillings and phase rotations can be applied similar to previous 11’s
Filling for missing tones
  If there are some leftover tones, optimal fillings are needed
  TBD for tone-filling
Size of phase rotation
  No gains in the concatenation of two identical sequence blocks with two different phases
    For example, all possible combinations of two phases, i.e., [1, -1], [1, j], and etc, do not provide any benefit in PAPR, e.g., 40MHz in HT and VHT
  Therefore, smaller size of phase rotation than 20MHz can be considered
  TBD for size of phase rotation

## Slide 9: Design for Compressed LTF (2xLTF)
Reuse of uncompressed LTF (4xLTF) sequence
  If only every other tone in the design LTF is transmitted, the designed PAPR is destroyed
  However, if a designed half-sized sequence exists, it could be reused for 2xLTF, which guarantees the same PAPR as designed
  Therefore, it’s reasonable that 2xLTF sequence can reuse designed 4xLTF sequences
Additional considerations
  Even though reusing 4xLTF sequences, it is necessary to design additional 2xLTF sequence for the smallest subband
  The center band can have a different size with others, depending on 2x tone mapping
-08 -07 -06 -05 -04 -03 -02 -01 0 +01 +02 +03 +04 +05 +06 +07 +08
…
Odd index mapping: # of 2xLTF tones is (14/2 -1) = 6
For example, a given subband block size of 14-tones (excluding DC tones)
DC tone
Even index mapping: # of 2xLTF tones is (14/2 +1) = 8

## Slide 10: Conclusions
For a given subband, the PAPR of HE LTF should be comparable to those of legacy preambles and at least less than the median PAPR of 256-FFT data
In UL OFDMA, a STA transmits HE LTF only in the allocated subbands, while an AP transmits HE LTF in the whole operating bandwidth in DL OFDMA
For subbands less than 20MHz, the per-subband design can be considered to optimize PAPR in UL OFDMA
LTF sequences for 40, 80, and 160MHz is designed from the concatenation of the 20MHz LTF sequence with some phase rotations
In a given subband size, a compressed LTF reuses a half-sized uncompressed LTF sequence for a simple design

## Slide 11: Straw Poll #1
Do you agree the following sentence to be adopted in SFD?
  3.y.z. A STA shall transmit HE LTF only in the allocated subbands in UL OFDMA.
    Y/N/A:

## Slide 12: Straw Poll #2
Do you agree the following sentences to be adopted in SFD?
  3.y.z. A HE LTF sequence for 40, 80, and 160MHz shall be made from concatenations of the HE LTF sequence for 20MHz with phase rotations and filling of missing tones.
    Detailed phase rotations and filling of missing tones are TBD.
Y/N/A:

## Slide 13: Straw Poll #3
Do you agree the following sentences to be adopted in SFD?
  3.y.z. A HE 2xLTF shall reuse the 4xLTF sequence defined for the half-sized subband
    TBD for 2xLTF sequences for the smallest subband and the center band
    Y/N/A:
    Note: 2xLTF and 4xLTF stand for HE LTFs which have symbol durations of 6.4us and 12.8 µs, respectively, excluding GI

## Slide 14: References
[1] Robert Stacey, Specification Framework for Tgax, 11-15/0132r3, March 2015.
[2] Daewon Lee, et. al., PAPR reduction of Legacy portion of VHT PLCP Preamble, 11-10/0795r2, July 2010.
[3] Sameer Vermani, et.al., VHT-LTF sequence for 80 MHz, 11-10/0802r0, July 2010