## Slide 1: Uplink ACK and BA Multiplexing
Date: 2015-05-10
Authors:
Name | Affiliations | Address | Phone | email
Reza Hedayat Young Hoon Kwon Yongho Seok Vida Ferdowsi | Newracom | 9008 Research Drive, Irvine, CA 92618 |  | reza.hedayat at newracom.com younghoon.kwon at newracom.com yongho.seok at newracom.com vida.ferdowsi at newracom.com
Reza Hedayat, Newracom

## Slide 2: Background
TGax adopted DL OFDMA and along with DL MU MIMO, there are now two DL MU mechanisms
The efficiency of DL OFDMA is enhanced significantly if multiple ACK/BAs are multiplexed in response to a DL OFDMA PPDU
  ACK/BA multiplexing also enhances DL MU MIMO efficiency
Based on this 11ax SFD has adopted that “The amendment shall include a mechanism to multiplex BA/ACK responses to DL MU transmission. ”
In this contribution some details on how ACK/BA frames could be multiplexed in response to a DL MU MIMO are presented

## Slide 3: ACK/BA Frame Attributes in Legacy Designs
Content of L-SIG, SIG-A and SIG-B
  In legacy amendments, these fields are decided by each STA as specified by the spec
ACK/BA frame size
  ACK: 14B
  Compressed BA: 32B
  Multi-TID BA: 22B + 12B per each TID
MCS and NSS
  Under current rules and designs MCS and NSS are selected by the STA
Guard Interval (GI)
  Under current rules and designs GI is selected by the STA: 0.8us or 0.4us

## Slide 4: UL ACK/BA Multiplexing
PHY/MAC attributes of each ACK/BA frame in an UL OFDMA frame
Content of L-SIG, SIG-A and SIG-B
  Need to be set by all STAs with the same values; either by AP’s explicit indication in the preceding DL MU PPDU, or as spec defines.
Sub-band assignment
  Assignments for the sub-band of each ACK/BA frame need to be given (next slide)
MCS and NSS
  Could be decided by each STA as currently done, or
  AP could require all STAs to use robust MCS and NSS choices
GI, LTF compression, …
  AP need to mandate that all STAs use the same values for these parameters

## Slide 5: Sub-band Assignment for ACK/BA Multiplexing
It is expected that the transmission bandwidth of the multiplexed ACK/BA to be the same or less than the transmission bandwidth of the preceding DL MU frame and AP need to indicate this to the STAs
  If the bandwidth of the multiplexed ACK/BA frame is less that the bandwidth of the preceding DL MU MIMO, then the bandwidth of possible subsequent frames in a TXOP would be same or les than the bandwidth of the last frame
Depending on the bandwidth of the preceding DL MU frame bandwidth, the number of available sub-bands for multiplexing ACK/BA frames vary
Considering 2MHz and 4MHz sub-bands, possibly up to nine ACK and BA frames could be multiplexed in a 20MHz PPDU

## Slide 6: Sub-band Assignment for ACK/BA Multiplexing
Bandwidth of assigned sub-band for each ACK/BA
  DL payloads in a DL OFDMA could vary a lot, therefore assigned sub-bands in a DL OFDMA PPDU could vary a lot
  But ACK/BA sizes do not vary as much, hence less variance in assigned sub-bands for each ACK/BA frame is expected, and an more equal assignments might be more fitting
Depending on the bandwidth of the preceding DL MU frame bandwidth, the number of available sub-bands vary
Considering 2 and 4MHz sub-bands, possibly up to nine ACK and BA frames could be multiplexed in a 20MHz PPDU

## Slide 7: Sub-band Assignment for ACK/BA Multiplexing
Explicit sub-band assignment
  In each DL OFDMA PPDU, AP can explicitly indicate what sub-band to be used by the STA for placing the ACK/BA
  If the ACK Policy subfield of QoS Control is set to “No ACK”, then the AP does not assign any sub-band to the STA
  Explicit assignment allows the AP to assign best/better sub-bands for each STA
Implicit sub-band assignment
  STAs might pick up a sub-band (from the set of the sub-bands) based on some order
  For instance, based on the same order that their DL assignment appears in the preceding DL OFDMA PPDU, or the same order as in the GID of the preceding DL MU MIMO PPDU
  For this case, the bandwidth of sub-bands used for ACK/BA need to be known to STAs e.g. be pre-announced in the preceding DL OFDMA frame etc

## Slide 8: Trigger Frame for UL MU Transmission
For UL MU operation, TGax has adopted a new frame called Trigger frame where it triggers the simultaneous transmission of individual frames by several STAs
Trigger frame may appear in several forms. For instance:
  New frame type of Trigger frame sent to specific STAs where it includes the necessary scheduling details for the STAs
  New frame type of Trigger frame broadcasted to a set of STAs or all STAs, where a STA can grab a sub-band to send a data, control, or management frame in a scheduled or non-scheduled (random access) manner
  DL MU PPDU where the AP expects two or more ACK or BA frames from the STAs addressed in the DL MU PPDU
  Or a DL MU PPDU where it triggers a combination of above items such as ACK/BA frames from the addressed STAs and other frames from other/all STAs

## Slide 9: Conclusion
This contribution discusses some details regarding how ACK and BA frames should be multiplex in response to a DL MU PPDU
Along with the TGax SFD inclusion of Trigger frame, a DL MU PPDU may act as a Trigger frame for the ACK and BA frames that follow after the DL MU PPDU
There are implicit and explicit options for the AP to specify the sub-bands that each STA uses to place its ACK/BA frame

## Slide 10: Strawpoll 1
Do you agree to add the following to 11ax SFD:
  “ DL MU PPDU may act as Trigger frame for the multiplexed AC/BA frame that follows the DL MU frame.”
  Y/N/A:

## Slide 11: Strawpoll 2
Do you agree to add the following to 11ax SFD:
  “A DL MU PPDU shall not signal explicitly the resource assignment for ACK or BA frames that follow the DL MU frame.”
  Y/N/A: