## Slide 1: More Power Save Calibration Results
Date: 2015-05-10
Authors:

## Slide 2: Abstract
The contributions [1]-[3] described one or more of the 3 existing power save mechanisms in 802.11-2012 [4] as baseline for energy efficiency evaluation in simulation scenario [5] and evaluation methodology documents [6] for TGax
  Power save mode (PSM)
  Power save polling (PSP)
  Unscheduled automatic power save delivery (U-APSD)
For this activity, a MAC calibration test for power save is defined in [5] for others to calibrate their MAC system simulators
  Results have been presented so far for PSM [8, 10, 11], PSP [11], and U-APSD [7, 8, 9].
This contribution presents power save calibration test results for PSP and U-APSD

## Slide 3: Calibration Test Setup
Scenario
  Simulation Run Time = 9000 seconds
  802.11n PHY, 20 MHz bandwidth, 5 GHz band
  PER = 0
  No A-MPDU aggregation
Output
  Percentage of time spent in each power state over simulation run
  Average power consumed for each power state over simulation run
AP
STA
Power Save Test Parameters
  MSDU length for PSP: 1500 bytes with CWmin=15 downlink every 200 ms
  MSDU length for U-APSD: 120 bytes with CWmin=15 (once every 40 ms) for both uplink and downlink
  RTS/CTS [ OFF ]
  AIFS=DIFS=34us
  PIFS=25us
  MCS = [ 0 ]
  DTIM = [ 3 ]

## Slide 4: Summary of Parameters for PSM and U-APSD
Mechanism | Parameter | Definition/Values | Suggested Set of Simulation Values **
Power save polling (PSP) | Beacon Interval (BI) | 100 TU | 100 TU
 | DTIM | Integer in unit of BI | { 1, 3 }
 | Pre-Target Beacon Transmission Time (TBTT) | Length of time before a STA wakes before Beacon | { 0 } ms
 | Beacon timeout | Length of time after TBTT | { 5 } ms
Unscheduled automatic power save delivery (U-APSD) | Beacon Interval (BI) | 100 TU | 100 TU
 | DTIM | Integer in unit of BI | { 1, 3 }
 | Max SP Length | Indicate the maximum number of buffered MSDUs, A-MSDUs, and MMPDUs that AP may deliver per SP | { 2, 4, 6, ∞ }
 | AC | Access Category | All ACs are both delivery and trigger enabled
 | Pre-Target Beacon Transmission Time (TBTT) | Length of time before a STA wakes before Beacon | { 0 } ms
 | Beacon timeout | Length of time after TBTT | { 5 } ms
 | Probe delay | Delay (in microseconds) to be used prior to transmitting when changing from Doze to Awake, if no frame sequence is detected by which the NAV can be set. | { 0 } ms

## Slide 5: Example of PSP Operation
AP buffers this frame since this STA is in power save mode
AP
STA
ACK
PS-Poll
Beacon
MPDU
Beacon
STA starts CCA for PS-Poll
DATA
AP starts EDCA for downlink one MPDU
ACK
Since DTIM=3, STA continues in Doze state during this Beacon
STA exits power save mode and is Awake for DTIM Beacon, i.e. DtimCount=0; STA skips other Beacons that are not DTIM Beacons
STA return to Doze, and AP resumes buffering traffic for this STA
DtimCount=0
DtimCount=2

## Slide 6
Simulation Results for PSP
Percentage of Time Spent in Each Power State over Simulation Run
Power Save Polling (PSP) |  | STA (% of Total Simulation Time) |  |  |  | AP (% of Total Simulation Time) |  |  | 
Enabled? | DTIM Period (BI) | Listen | RX | TX | Sleep | Listen | RX | TX | Sleep
No | - | 98.0645 | 1.9055 | 0.0300 | 0 | 98.0645 | 0.0300 | 1.9055 | 0
Yes | 1 | 0.1418 | 1.9355 | 0.0620 | 97.8607 | 98.0025 | 0.0620 | 1.9355 | 0
Yes | 3 | 0.0847 | 0.9623 | 0.0404 | 98.9127 | 98.3724 | 0.0404 | 1.5872 | 0

## Slide 7
Power Save Polling (PSP) |  | STA (Average Power, mW) |  |  |  |  | AP (Average Power, mW) |  |  |  | 
Enabled? | DTIM Period (BI) | Listen | RX | TX | Sleep | Total Average Power | Listen | RX | TX | Sleep | Total Average Power
No | - | 53.9355 | 2.0961 | 0.0924 | 0 | 56.1239 | 53.9355 | 0.0330 | 5.8690 | 0 | 59.8374
Yes | 1 | 0.0780 | 2.1291 | 0.1910 | 0.0032 | 2.4012 | 53.9014 | 0.0682 | 5.9614 | 0 | 59.9309
Yes | 3 | 0.0466 | 1.0585 | 0.1243 | 0.0033 | 1.2326 | 54.1048 | 0.0444 | 4.8887 | 0 | 59.0379
Based average current consumption values @ 1.1V in [5], i.e. TX = 280 mA, RX = 100 mA, Listen = 50 mA, Sleep = 0.003 mA;
Simulation Results for PSP
Average Power Consumed for Each Power State over Simulation Run

## Slide 8: Example of U-APSD Operation
AP buffers this frame since this STA is in power save mode
AP
STA
Beacon
A-MPDU
STA starts aProbeDelay then CCA for trigger frame, i.e. QoS (Null) frame
DATA
BA
STA return to Doze, and AP resumes buffering traffic for this STA
STA exits power save mode and is Awake for DTIM Beacon, i.e. DtimCount=0; STA skips other Beacons that are not DTIM Beacons
AP is aware STA is Awake, starts EDCA, and send frames to STA until there are no more data frames for this AC or AP has reached Max SP Length
A-MPDU
BA
EOSP=1
Service Period
MPDU
ACK
Beacon
EOSP=0
DtimCount=0
DtimCount=2

## Slide 9
Simulation Results for U-APSD
Percentage of Time Spent in Each Power State over Simulation Run
U-APSD |  | STA (% of Total Simulation Time) |  |  |  | AP (% of Total Simulation Time) |  |  | 
Enabled? | aProbeDelay (us) | Listen | RX | TX | Sleep | Listen | RX | TX | Sleep
No | - | 98.5198 | 0.7401 | 0.7400 | 0 | 98.5198 | 0.7400 | 0.7401 | 0
Yes | 0 | 0.5877 | 0.7401 | 0.7400 | 97.9322 | 98.5199 | 0.7400 | 0.7401 | 0
Yes | 100 | 0.8377 | 0.7401 | 0.7400 | 97.6822 | 98.5199 | 0.7400 | 0.7401 | 0

## Slide 10
U-APSD |  | STA (Average Power, mW) |  |  |  |  | AP (Average Power, mW) |  |  |  | 
Enabled? | aProbeDelay (us) | Listen | RX | TX | Sleep | Total Average Power | Listen | RX | TX | Sleep | Total Average Power
No | - | 54.1859 | 0.8141 | 2.2793 | 0 | 57.2794 | 54.1859 | 0.8140 | 2.2796 | 0 | 57.2796
Yes | 0 | 0.3232 | 0.8140 | 2.2793 | 0.0032 | 3.4198 | 54.1859 | 0.8140 | 2.2796 | 0 | 57.2795
Yes | 100 | 0.4608 | 0.8140 | 2.2793 | 0.0032 | 3.5573 | 54.1859 | 0.8140 | 2.2796 | 0 | 57.2795
Based average current consumption values @ 1.1V in [5], i.e. TX = 280 mA, RX = 100 mA, Listen = 50 mA, Sleep = 0.003 mA;
Simulation Results for U-APSD
Average Power Consumed for Each Power State over Simulation Run

## Slide 11: Beyond Calibration Discussion
A STA that sends a PS-Poll to retrieve any BUs from AP shall continue to stay awake for MPDU from AP; if STA fails to receive the MPDU, then STA will continue to stay awake until the next Beacon and check TIM again
  If TIM bit is set, then STA shall send PS-Poll
  If TIM bit is not set, then STA return back to Doze
If AP has more BUs for this PS STA, then AP may set the More Data bit to 1 in the DL MPDU
  STA may send another PS-Poll within the same Beacon Interval to retrieve additional BUs
A PS STA operating in U-APSD may trigger a service period either using
  An UL DATA MPDU
  QoS NULL frame after observing the TIM is set in Beacon

## Slide 12: Conclusion
This contribution presents and discusses power save calibration test results for PSP and U-APSD

## Slide 13: References
E. Wong et al, “Energy efficiency evaluation methodology,” IEEE 11-14-827r3 July 2014
E. Wong et al, “Energy efficiency evaluation methodology follow up”, IEEE 11-14-1162r1, Sept 2014
E. Wong et al, “Parameters for power save mechanisms,” IEEE 11-14-1161r3, Sept 2014
IEEE 802.11-2012
S. Merlin et al, “TGax Simulation Scenarios,” IEEE 11-14-980r6, Jan 2015
R. Porat et al, “11ax Evaluation Methodology,” IEEE 11-14-571r7, Jan 2015
J. Kneckt et al, “Power save calibration results,” IEEE 11-14-1495r0, Nov 2014
J. Kneckt et al, “Power save calibration,” IEEE 11-15-0103r0, Jan 2015
Y. Li et al, “U-APSD power saving-calibration-results,” IEEE 11-15-0072r0, Jan 2015
E. Wong et al, “Power save calibration results, “IEEE 11-15-306r3, March 2015
H. Choi et al, “Power save calibration,” IEEE 11-15-316r5, March 2015