## Slide 1: Beamformed HE PPDU
Date: 2015-05-13
Authors:

## Slide 2: Beamformed HE PPDU
In 802.11ac,
  For a VHT SU PPDU, a beamforming steering matrix can be applied to the waveform
  For a VHT MU PPDU, a beamforming steering matrix is always applied to the waveform
  If the beamforming steering matrix is applied, a smoothing is not recommended
In 802.11ax MIMO-OFDMA, a beamforming should be allowed as a user-specific value

## Slide 3: HE Sounding Protocol for Beamformed HE PPDU
HE sounding protocol can reuse 11ac VHT sounding protocol
  A HE beamformer may initiate a sounding feedback sequence by transmitting a HE NDP Announcement (NDPA) frame followed by a HE NDP
  HE beamformees sequentially report a HE Compressed Beamforming feedback after receiving a HE NDPA frame or Beamforming Report Poll frame from the HE beamformer

## Slide 4: HE Sounding Protocol for Beamformed HE PPDU
Additionally, in 802.11ax, HE beamformees can simultaneously report a HE Compressed Beamforming feedback in UL MU transmission mode
  NDPA and Trigger frames can be integrated
  Beamforming Report Poll and Trigger frames can be integrated

## Slide 5: Beamformed DL HE PPDU Exchange Sequence
The AP transmits a beamformed DL HE PPDU
A beamformed parameter of each receiving STAs should be encoded in SIG field of a DL HE PPDU
Smoothing is not recommended when the beamformed parameter of the received DL HE PPDU is set to true

## Slide 6: Beamformed DL HE PPDU Exchange Sequence
When multiple PSDUs on a sub-channel are destined to different STAs, encoding a beamformed parameter of each sub-channels is more efficient
Also, in the case of the DL HE MU-MIMO, encoding a beamformed parameter is not needed like 802.11ac

## Slide 7: Beamformed UL HE PPDU Exchange Sequence
The HE AP transmits a trigger frame to initiate the beamformed UL HE MU PPDU transmission
HE STAs transmit a beamformed UL HE PPDU SIFS after receiving the trigger

## Slide 8: Beamformed UL HE PPDU Exchange Sequence
A beamformed parameter of each receiving STAs can be encoded in SIG field of an UL HE PPDU
  But, if SIG contents of UL HE PPDUs are common, encoding the beamforming parameter in the UL HE PPDU is not needed because AP already knows it
    Remind that AP determines the beamformed parameter of the UL HE PPDU and signaled to all transmitters of UL HE PPDU
  Encoding the beamforming parameter in the UL HE PPDU is meaningful only if SIG contents of UL HE PPDU is not common
    Not preferable because of the protocol overhead

## Slide 9: Beamformed UL HE PPDU Exchange Sequence
Alternative proposal is that a beamformed parameter of each receiving STAs is not encoded in any SIG fields of an UL HE PPDU
  A trigger frame can have a smoothing bit for indicating whether the AP may perform the smoothing mechanism on the received UL HE PPDU
    When the smoothing bit in the trigger frame is set to true, Uplink HE PPDU should be in non-beamformed. Otherwise, Uplink HE PPDU can be in either beamformed or non-beamformed.

## Slide 10: Beamformed UL HE PPDU Exchange Sequence
Discussion on beamforming parts of UL HE PPDU
  Option1) After HE-SIG-A, only HE-STF, HE-LTF and PSDU can be beamformed
    Pros: Legacy STA can decode the length from legacy preamble
    Cons: Loss of beamforming gain on the legacy preamble and HE-SIG-A

## Slide 11: Beamformed UL HE PPDU Exchange Sequence
Discussion on beamforming parts of UL HE PPDU
  Option2) All UL HE PPDU parts including legacy preamble and HE-SIG-A can be beamformed
    Pros: Beamforming gain on the legacy preamble and HE-SIG-A
    Cons: Legacy STA can not decode the legacy preamble

## Slide 12: Conclusion
In order to fully utilize the OFDMA technical advantage, the efficient beamforming and sounding protocol should be designed with an optimized but minimized implementation complexity

## Slide 13: Straw Poll 1
Do you agree to add the TGax Specification Framework:
  4 Multi-user (MU) features
  The amendment shall define a sounding procedure for reporting DL CSI feedback using UL MU mode