## Slide 1: Non-Uniform Constellations for 64-QAM
Date: 2015/05/11
Authors:

## Slide 2: Motivation
Higher order QAMs discussed in e.g. [1]-[4] as potential technology for 802.11ay
  OFDM: 128-QAM, 256-QAM (up to 64-QAM in ad)
  SC: 64-QAM (up to 16-QAM in ad)
Non-uniform constellations (NUCs) provide increased performance compared to uniform constellations (UCs) [3]-[4]
  Especially for higher order QAMs [3]
    Gain up to 0.7dB for 256-QAM (OFDM)
  APSK for 64-QAM (SC) [4]
  Moderate (2D NUC) or no (1D NUC) increase in demapper complexity
1-D NUC: 16-QAM
2-D NUC: 16-QAM

## Slide 3: Outline
NUCs for 64-QAM and single carrier (SC) modulation
Performance results
  AWGN channel with and without phase noise

## Slide 4: NUCs for 64-QAM
2-dimenionsal (2D) NUCs
  Improved performance compared to 1D NUCs
  Reasonably demapper complexity (especially for < 256-QAM)
  Quadrant symmetry
Different NUCs for each code rate
  Optimized for operating point of FEC with specific code rate
Bit labeling optimized
  Matches optimally to existing .11 WLAN system
    No changes at FEC or other blocks required
    No need for a dedicated bit interleaver

## Slide 5: 64-QAM NUCs
CR=1/2
CR=5/8
CR=3/4
CR=13/16
Details of
constellation
points and
bit labeling
see Appendix
Bit labeling: :
See Appendix

## Slide 6: Simulations Parameters
Regular UCs and NUCs
Single carrier modulation
Focus on 64-QAM
Message Length: 1000bytes
Channel: AWGN
  AWGN (channel is very close to AWGN in the LOS case)
With and without phase noise
  Phase noise model according to .11ad evaluation methodology [5]
Gain compared to UC evaluated at FER=10-2
modulation | bit/symbol | coderate
64-QAM | 6 | 1/2
64-QAM | 6 | 5/8
64-QAM | 6 | 3/4
64-QAM | 6 | 13/16

## Slide 7: Simulation Results: without phase noise
Up to 0.4dB gain

## Slide 8: Simulation Results: with phase noise (PN)
Different demappers
  Regular demapper
  Demapper which takes PN into account
without PN
with PN
No influence
of PN aware
demapper
NUC gain

## Slide 9: Simulation Results: with phase noise (PN)
Increased NUC gain in the presence of phase noise

## Slide 10: Conclusions
Investigation of non-uniform constellation for 64-QAM
  ~0.4dB gain compared to uniform constellations
Simulations in the presence of phase noise
  NUC gain is maintained or even increased
  ~0.5dB gain compared to uniform constellations
Optimization of QAM promising technology for .11ay
  Improved performance
  Moderate complexity increase
Next steps: further optimizations of NUCs

## Slide 11: References
11-14-1378-00-ng60 PHY rate for NG60
11-14-0652-00-0wng-wng Next Generation 802.11ad
11-15-0096-01-ng60 Non-uniform Constellations for higher Order QAMs
11-15-0339-00-ng60 SC-64APSK for 11ay
11-09-0296-16-00ad Evaluation Methodology

## Slide 12: Appendix

## Slide 13: NUC: 1-D vs 2D
1-D NUC
  I/Q symmetry
  1-D demapping as for uniform constellations (UC), i.e. same demapping complexity as for regular QAMs
2-D NUC
  Symmetric quadrants
  Higher gain compared to 1-D NUC
  2-D demapping required
1-D NUC: 16-QAM
2-D NUC: 16-QAM

## Slide 14: 64-QAM NUC Definition Code rate 1/2

## Slide 15: 64-QAM NUC Definition Code rate 5/8

## Slide 16: 64-QAM NUC Definition Code rate 3/4

## Slide 17: 64-QAM NUC Definition Code rate 13/16