## Slide 1
Name | Affiliations | Address | Phone | email
Vida Ferdowsi Daewon Lee Reza Hedayat | Newracom | 9008 Research Drive, Irvine, CA 92618 |  | Vida.Ferdowsi at newracom.com Daewon.lee at newracom.com Reza.Hedayat at newracom.com
Authors:
Simulation Results for Box 5 Calibration
Date: 2015-05-10

## Slide 2: Summary
This presentation shows simulation results for Box 5 calibration based on the agreements in [1].

## Slide 3: Calibration Scenario - 11ac Scenario 6 [2]
AP A | (0,0)
AP B | (40,20)
AP C | (-40,-20)
STA3 | (7.5+xb, ‑9.5+yb)
STA9 | (7+xb, -7.5+yb)
STA15 | (3+xb, -0.5+yb)
STA21 | (-6.5+xb, -3+yb)
STA27 | (‑6+xb, 2.5+yb)
STA6 | (-5.5+xc,4.5+yc)
STA12 | (7+xc,7+yc)
STA18 | (10+xc,0.5+yc)
STA24 | (3+xc,2.5+yc)
STA30 | (9.5+xc,3.5+yc)
STA1 | (5,-9.5)
STA2 | (3.5,7.5)
STA4 | (-4.5,0.5)
STA5 | (-1.5,6)
STA7 | (-9,-5)
STA8 | (-8.5,8.5)
STA10 | (-3,0.5)
STA11 | (-0.5,8)
STA13 | (-4,-4)
STA14 | (7.5,-1)
STA16 | (8,-6)
STA17 | (0,-7.5)
STA19 | (-2.5,-4.5)
STA20 | (0.5,-2)
STA22 | (0,-4.5)
STA23 | (-1.5,7)
STA25 | (3.5,-5)
STA26 | (9,9.5)
STA28 | (-8,-5.5)
STA29 | (1.5,3.5)
Fixed Location and Association

## Slide 4: PHY Parameters
PHY parameters | 
BW | All BSSs at 5GHz [80 MHz, no dynamic bandwidth]
Channel model | TGac D NLOS per link
Shadow fading | iid log-normal shadowing (5 dB standard deviation) per link
Data Preamble Type | [5GHz, 11ac], duration is considered.
STA TX Power | 15 dBm per antenna
AP TX Power | 20 dBm per antenna
AP number of TX/RX antennas | 1/1
STA number of TX /RX antennas | 1/1
AP antenna gain | 0 dBi
STA antenna gain | -2 dBi
Noise Figure | 7dB
CCA threshold | -70dBm/80MHz (measured after large-scale fading)
Rx sensitivity | -82dBm/80MHz (a packet with lower rx power is dropped)
Link Adaption | Fixed MCS =7
Channel estimation | ideal
PHY abstraction | RBIR, BCC [3, 4]
Channel correlation | Same as defined in the used channel model

## Slide 5: MAC Parameters
MAC parameters | 
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=3 ]
Queue length | A single queue for each traffic link is set inside AP/STA sized of 2000 packets
Traffic type | UDP CBR with rate 10^8bps
MPDU size | 1540 Bytes (1472 Data + 28 IP header + 40 MAC header)
Aggregation | [A-MPDU / max aggregation size / BA window size, No A-MSDU, with immediate BA], Max aggregation: 64 MPDUs with 4-byte MPDU delimiter
Max number of retries | 10
Beacon | Disabled
RTS/CTS | OFF
Traffic direction | DL Only, UL only
Throughput metric | Histogram of per non-AP STA throughput (received bits/overall simulation time)
Note: In the subsequent reported results, A-MSDU of up to 64 MSDUs is used.

## Slide 6: Single-BSS Test
Upright corner BSS B (STAs 3, 9 ,15, 21, 27)
  DL only & UL only (STA rate in Mbps)
  The same traffic is attached to each STA

## Slide 7: Single-BSS Test: DL Only
Chart: 
| 3 | 9 | 15 | 21 | 27
NEWRACOM | 50.81 | 50.82 | 50.7 | 50.71 | 50.76
Huawei | 51.09 | 51.55 | 51.05 | 51.42 | 51.37
LG | 51.05 | 50.97 | 51.11 | 50.7 | 51.1
MRVL | 52 | 52.68 | 52.68 | 52.51 | 52.81
NTT | 49.92 | 50.08 | 49.95 | 50.04 | 50.24
ZTE | 50.75 | 49.77 | 49.31 | 50.81 | 48.47
Data shows the similar trends with other companies results.

## Slide 8: Single-BSS Test: UL Only
Chart: 
| 3 | 9 | 15 | 21 | 27
NEWRACOM | 43.25 | 33.6 | 53.53 | 42.23 | 39.42
Huawei | 40.83 | 45.4 | 48.49 | 43.29 | 44.06
LG | 36.83 | 39.86 | 48.95 | 42 | 39.01
MRVL | 37.74 | 41.15 | 51.52 | 46.6 | 44.83
NTT | 42.79 | 44.86 | 48.92 | 40.4 | 42.21
ZTE | 40.92 | 39.97 | 51.61 | 44.67 | 44.85

## Slide 9: Simulation results for UP. 2-STA and 3-STA subsets Note: MCS5. PER is calculated in UDP layer and incudes packet drops.
 |  | Throughput [Mbps] | PER
2 STAs | STA 3, STA 9 | STA3: 95.84 STA9: 97.28 | STA3: 0.16 STA9: 0.15
 | STA 3, STA 27 | STA3: 95.10 STA 27: 95.53 | STA3: 0.17 STA 27: 0.16
 | STA 3, STA 15 | STA 3: 95.77 STA 15: 97.23 | STA 3: 0.16 STA 15: 0.15
3 STAs | STA 3, STA 9, STA 27 | STA 3: 67.07 STA 9: 65.46 STA 27: 52.25 | STA 3: 0.41 STA 9: 0.57 STA 27: 0.54
 | STA 3, STA 9, STA 27 | STA 3: 59.89 STA 9: 58.95 STA 27: 65.52 | STA 3: 0.47 STA 9: 0.48 STA 27: 0.45

## Slide 10: References
[1] 11-14/1523r4 Offline Discussion Minutes of SLS Calibration
[2] 11-09/0451r16 TGac Functional Requirements and Evaluation Methodology
[3] 11-14/0571r6 Evaluation Methodology
[4] 11-14/1176r0 PHY Abstraction Tables for 11ax System Level Simulation
[5] 11-15/51r0 Box5 Calibration Results
[6] 11-15/53r1 Box5 Results of 11ac SS6