## Slide 1: Multi Channel Availability for UL-OFDMA
Date: 2015-05-12
Authors:

## Slide 2: Introduction
In dense BSS environment, STAs in the same BSS might be influenced by transmissions from different OBSSs[1], [2]
Considering wider band operation, STAs might belong to radio ranges of different OBSS STAs and see channel (idle/busy) differently (different channel availability)
UL-OFDMA procedure might suffer from the different channel availability between AP and UL-STAs

## Slide 3: Hidden node & Channel availability
STA1(CH1, 2) & STA4(CH3, 4) are transmitting data
  Since STA1 and STA4 is hidden from AP, AP sees channel 1 to 4 idle.
  STA2 sees CH1, 2 busy and (STA3-> CH3, 4)
STA1,2 and AP have different channel availability(CA)

## Slide 4: MU-UL motion in the previous meeting
The spec shall define the following mode of operation: An UL MU PPDU (MU-MIMO or OFDMA) is sent as an immediate response (IFS TBD) to a Trigger frame (format TBD) sent by the AP. [3]
UL STAs have to transmit UL data immediately after the trigger frame
  Every control information for UL data transmission must be delivered to UL-STAs within the trigger frame

## Slide 5: UL-OFDMA procedure
Considering UL-OFDMA with multiple channels
  AP must decide which STAs to participate on which channels
  AP requires STAs’ buffer status and CA
  Buffer status information might be gathered periodically or implicitly within ongoing transmissions
  CA cannot be obtained with the same manner
    much more sensitive to time
    CA of past time is not valid for current transmission
AP might assign (sub-)channels to UL-STAs with trigger frame
  There have been no considerations on CA yet
  AP will assign STAs to its available channels based on its discretion
    Simply using previous CSI or random assignment

## Slide 6: Necessity of channel availability on UL-OFDMA procedure (1)
4 channels are idle on AP side
AP assigns 4 UL STAs
Two nodes of different OBSSs, close to STA1 and STA4, were transmitting data (hidden from AP)

## Slide 7: Necessity of channel availability on UL-OFDMA procedure (2)
STA2 receives TF well from primary or secondary 1
  Successful UL transmission occurs
  TF structure on multiple channel(duplicate or not) and STAs channel sensing policy (full channel or just primary) need to be defined
STA1 cannot transmit UL data as it couldn’t hear the trigger frame
  AP didn’t notice that the primary channel was busy for STA1
  Assigned channel will be wasted

## Slide 8: Necessity of channel availability on UL-OFDMA procedure (3)
STA4 could hear the trigger frame
  In 802.11, It is generally assumed that STAs are sensing only primary channel before they transmit data
  STA4 might hear the trigger frame from the primary channel
The length of xIFS might influence the following behavior of STA4
  Assuming xIFS less than PIFS
  Since STA4 is not possible to measure CCA within the xIFS duration, it must transmit UL-data regardless of the CA
  UL data of STA4 might cause interference to ongoing transmissions of OBSS STAs

## Slide 9: Necessity of channel availability on UL-OFDMA procedure (4)
With increased xIFS (up to PIFS), it is possible for UL STAs to measure CCA before they transmit UL data
  Assigned STAs(STA4) may decide not to participate UL-transmission
  STA4 won’t make any interference to OBSS, but assigned channel will still be wasted
PIFS sensing for secondary channels may collide with existing PIFS based mechanism (e.g., beacon)

## Slide 10: Necessity of channel availability on UL-OFDMA procedure (5)
If AP could exploit channel availability of STAs
  Avoiding selecting inappropriate UL STAs
    STA1 and STA4 might interfere OBSS transmission or not transmit any UL data
  Assigning other STAs without CA issues
    STA5, STA6 don’t belong to OBSS interference range
    Assigning more channels to STA2, STA3
  Overall contention isolation gain or channel utility can be maintained

## Slide 11: Hidden node protection with existing RTS/CTS
Using RTS/CTS for multiple STAs
  RTS/CTS are supposed to reserve and protect channel from hidden nodes
  For UL-OFDMA case, each UL-STA might have different hidden node
  RTS/CTS must be exchanged on by one for each UL STA
  CTS can be regarded as CA feedback
RTS/CTS is not apt for solving CA problem
  Overhead of multiple STAs RTS/CTS is too large
  Other potential problems exist (backup slides)
Advanced channel availability feedback or channel protection mechanism is required

## Slide 12: Conclusion
In dense BSS and STA environment, STAs in the same BSS might have different channel availability due to ongoing transmissions of OBSSs
Channel availability might not only reduce the channel utility and contention isolation gain of UL-OFDMA but also interfere ongoing transmissions of OBSSs
It is necessary to take the effect of channel availability into account for developing the procedure of UL-OFDMA
  Advanced sensing or channel reservation mechanism
  Channel availability feedback
  Relevant channel protection mechanism

## Slide 13: References
[1] 11-15-0091-01-00ax-ul-ofdma-procedure-in-ieee-802-11ax
[2] 11-15-0378-02-00ax-channel-sensing-in-ul-ofdma
[3] 11-15-0365-00-00ax-ul-mu-procedure

## Slide 14: Strawpoll
UL-OFDMA procedure should consider the effect of different channel availability between AP and UL STAs
Y:
N:
A:

## Slide 15: Hidden node protection with existing RTS/CTS - backup
Channel will be over protected
  STAs don’t know which channel will be assigned
  STAs will send CTS for every available channel
  Secondary 1~3 didn’t have to be protected for STA1
  OBSS STAs of STA1 side have to defer for unused channels
For OBSS STAs only exposed to specific UL-STA, RTS/CTS duration could be seen idle
  OBSS STAs may start transmission during RTS/CTS period

## Slide 16: Hidden node protection with existing RTS/CTS - backup
Assuming the channel allocation is performed prior to the trigger
  RTS/CTS will be exchanged only on the assigned channel for each UL-STA
  Channel overprotection problem is no longer exist
  OBSS STAs may start transmission during RTS/CTS period still
  Overall UL-OFDMA procedure might become heavier due to channel allocation