## Slide 1: Design Principles for HE Preamble
Date: 2015-05-13
Authors:

## Slide 2: Background
TGax adopted HE preamble structure as follows [1]
  L-STF/L-LTF/L-SIG
    An HE PPDU shall include the legacy preamble (L-STF, L-LTF and L-SIG), duplicated on each 20 MHz, for backward compatibility with legacy devices.
  HE-SIG-A
    HE-SIG-A (using a DFT period of 3.2 µs and subcarrier spacing of 312.5 kHz) is duplicated on each 20 MHz after the legacy preamble to indicate common control information.
  HE-SIG-B
    Downlink HE MU PPDU shall include HE-SIG-B field, and the number of OFDM symbols of HE-SIG-B field is variable.
      NOTE—The HE-SIG-B field includes information required to interpret HE MU PPDU, and detail is TBD.
In this contribution, we discuss design principles for HE preamble, such as HE-SIG-B’s location, information division between HE-SIG-A/B, and HE-SIG-B’s multi-channel transmission.

## Slide 3: Introduction
A. HE-SIG-B’s location
  HE-SIG-A is after the legacy preamble
  TGax needs study for HE-SIG-B’s possible location within a HE preamble
B. SIG information division between HE-SIG-A/B
  HE-SIG-A indicates common control information
  HE-SIG-B includes information to interpret HE MU PPDU
  TGax needs study for how to divide SIG information between HE-SIG-A/B
C. HE-SIG-B’s transmission in multi 20MHz channels
  HE-SIG-A is duplicated on each 20MHz
  TGax needs study for HE-SIG-B’s transmission in multi 20MHz channels

## Slide 4: A. HE-SIG-B’s location
64 FFT
256 FFT
L-Part
HE Data
HE-
LTF
1
HE-
STF
HE-
SIG-A
HE-
LTF
n
...
HE-
SIG-B
variable
64 FFT
256 FFT
L-Part
HE Data
HE-
LTF
HE-
STF
HE-
SIG-A
HE-
LTF
...
HE-
SIG-B
variable
[A-1] SIG-B is in the 256FFT OFDM part
  Same as the current VHT-SIG-B’s position
  Can be beam-formed, divided by sub-bands
  (Pros) Efficient when MU-MIMO
  (Cons) NSTS, PAID information should be known prior to decode HE-LTFs
  (Cons) Inefficient minimum granularity (4X Sym.)
[A-2] SIG-B is in the 64FFT OFDM part
  Reside as the variable-length extension of SIG-A
  (Pros) Efficient minimum granularity (1X Sym.)
  (Cons) No MU-MIMO efficiency
Proposal: [A-2] SIG-B is in the 64FFT OFDM part
  Better to have HE-SIG-B in the 64FFT OFDM part as the variable-length extension of HE-SIG-A while having the efficient minimum granularity, also it does not impose ambiguity for decoding 256FFT part
HE-SIG-B’s exact location within a HE preamble is not defined

## Slide 5: Possible Signaling Information for 11ax
Partial AID
(9b)
SHORT GI
GI NYSM
Coding
LDPC extra
Beamformed
MCS
(4b)
Tail
(6b)
BW
(2b)
Group ID
(6b)
NSTS
(3b)
STBC
CRC
(8b)
SHORT GI
GI NSYM
LDPC extra
Tail
(6b)
BW
(2b)
Group ID
(6b)
NSTS
[0]
(3b)
STBC
CRC
(8b)
NSTS
[1]
(3b)
NSTS
[2]
(3b)
NSTS
[3]
(3b)
TXOP_PS
TXOP_PS
Coding [1]
Coding [2]
Coding [3]
SU
MU
VHT-SIG-A
VHT-SIGB
Coding [0]
Common Info (HE-SIG-A)
  BW (2b for 20/40/80/160MHz)
  GI (2b for 0.8/1.6/3.2us)
  Power Save (1b, TBD)
  LTF (1b for 6.4/12.8us)
  SU/MU indicator (1b, TBD)
  BSS color (TBD)
  HE-SIG-B Length (TBD)
  others (TBD)
Tail
(6b)
Length
(17b)
Tail
(6b)
Length
(16b)
MCS
(4b)
Single User Info (HE-SIG-A or B ?)
  PAID (9b), NSTS (3b), MCS (4b), STBC (1b), Coding (1~2b)
  Beamformed (1b)
  Length (can be indicated from L-SIG Length)
  others (TBD)
Multi User Info (HE-SIG-B)
  PAID (9b) (or GID), NSTS (3b), MCS (4b), Coding (1b)
  Length (16b)
  others (TBD)
Resource Allocation Info (HE-SIG-A or B?)
  Resource Allocation (TBD)
  others (TBD)
SU
MU
Based on VHT-SIG, SFD [1], and previous discussions in TGax, possible signaling information for HE Preamble can be classified as follows (preliminary results).

## Slide 6: B. Information Division between HE-SIG-A and B
SU
Info
SU
Info
variable
[B-1] SIG-A contains Common Control Info only
  DL/UL MU and UL SU PPDU require SIG-B
  UL MU PPDU may not require SIG-B
  (Cons) Inefficient from individual CRC/Tail fields on both HE-SIG-A and B for SU PPDU
[B-2] SIG-A contains Common Control Info and SU Info (or Resource Allocation Info)
  DL MU PPDU requires SIG-B
  DL/UL SU and UL MU PPDU may not require SIG-B
  SU specific info can be replaced by Resource Allocation Info when MU PPDU
  Additional Resource Allocation Info may reside in HE-SIG-B as well
Proposal: [B-2]
  Better to have HE-SIG-A for signaling SU PPDU without additional HE-SIG-B
Based on the previous slide, there are possible options for allocating the resource allocation information between HE-SIG-A and B
HE-SIG-A
HE-SIG-A
HE-SIG-B
HE-SIG-B
Resource
Alloc.
Info
variable
...
MU
Info
[n-1]
MU
Info
[0]
Resource
Alloc.
Info
...
MU
Info
[n-1]
MU
Info
[0]
SU
MU
Common
Control
Info
Common
Control
Info
SU
MU
Common
Control
Info
Common
Control
Info
CRC
/Tail
CRC
/Tail
CRC
/Tail
CRC
/Tail
CRC
/Tail
CRC
/Tail
CRC
/Tail
Additional
Resource
Alloc.
Info

## Slide 7: C. SIG-B transmission in multi 20MHz channels (1)
64 FFT
256 FFT
HE-
SIG-A
...
HE-
SIG-B
variable
Dup.
HE-
SIG-A
Dup.
HE-
SIG-B
L-Part
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-
SIG-B
Dup.
HE-
SIG-A
Dup.
HE-
SIG-B
Dup.
L-Part
Dup.
L-Part
[C-1] Duplicated HE-SIG-B per 20MHz
  (Pros) Most robust & flexible HE-SIG-B decoding
  (Cons) Longer preamble time with many STAs signaling
  (Cons) Inefficient resource usage when multi-channel
[C-2] Non-duplicated HE-SIG-B per 20MHz
  (Pros) Efficient with multi-channel
  (Cons) Dependent on multi-channel RX implementations
  (Cons) Inefficient from HE-SIG-B’s individual CRC/Tail per 20MHz
64 FFT
256 FFT
HE-
SIG-A
...
HE-
SIG-B
1
variable
Dup.
HE-
SIG-A
HE-
SIG-B
2
L-Part
Dup.
L-Part
Dup.
HE-
SIG-A
HE-
SIG-B
3
Dup.
HE-
SIG-A
HE-
SIG-B
4
Dup.
L-Part
Dup.
L-Part
Primary
20MHz
Primary
20MHz

## Slide 8: C. SIG-B transmission in multi 20MHz channels (2)
64 FFT
256 FFT
HE-
SIG-A
...
variable
Dup.
HE-
SIG-A
L-Part
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-
SIG-A
Dup.
L-Part
Dup.
L-Part
HE-
SIG-B
S
T
F
L
T
F
[C-3] Entire-channel HE-SIG-B without dedicated STF/LTF
  (Pros) Efficient multi-channel utilization
  (Cons) Without dedicated entire channel STF/LTF, AGC and channel estimation are challenging
  (Cons) May require new numerology design for HE-SIG-B
TGax requires further study for how to transmit HE-SIG-B in multi 20MHz channels in terms of preamble overhead and SIG-B decoding performances.
[C-4] Entire-channel HE-SIG-B with dedicated STF/LTF
  (Pros) Efficient multi-channel utilization
  (Cons) Require dedicated STF/LTF for HE-SIG-B
64 FFT
256 FFT
HE-
SIG-A
...
variable
Dup.
HE-
SIG-A
L-Part
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-
SIG-A
Dup.
L-Part
Dup.
L-Part
HE-
SIG-B
Primary
20MHz
Primary
20MHz

## Slide 9: Conclusions
We discussed possible design options for HE Preamble
  HE-SIG-B’s location
    We propose to locate HE-SIG-B in 64FFT OFDM part
    Has efficient min. granularity, and eliminates ambiguity by providing resource allocation information early
  Information division between HE-SIG-A and B
    We propose for HE-SIG-A to have Common Control Info and SU specific Info for HE SU PPDU
    Efficiently contains all SU information in SIG-A only
  HE-SIG-B transmissions in multi 20MHz channels
    We propose TGax to study further how to transmit HE-SIG-B in multi 20MHz channels in terms of preamble overhead and SIG-B decoding performances.

## Slide 10: Straw poll - 1
  Do you agree to add the following text into 11ax SFD ?
  3.2.z HE-SIG-B shall use a DFT period of 3.2us and subcarrier spacing of 312.5kHz.
  Y
  N
  A

## Slide 11: Straw poll - 2
  Do you agree to add the following text into 11ax SFD ?
  3.2.z For HE SU PPDU, HE-SIG-A field shall include common control information and user specific information.
  Y
  N
  A

## Slide 12: Straw poll - 3
  For transmission of HE-SIG-B field per 20MHz, which option do you prefer ?
  [C-1] HE-SIG-B duplicate per 20MHz
  [C-2] HE-SIG-B non-duplicated per 20MHz, individual information per 20MHz
  [C-3] HE-SIG-B encoding in the entire PPDU bandwidth
  [C-4] HE-SIG-B encoding in the entire PPDU bandwidth, prepended with dedicated STF/LTF in the entire PPDU bandwidth

## Slide 13: References
[1] 15/0132r4 Spec framework