## Slide 1: Further consideration on Multi-STA Block ACK
Date: 2015-05-11
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Wookbong Lee |  |  |  | wookbong.lee@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Hyeyoung Choi |  |  |  | hy0117.choi@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Tu Nguyen |  |  |  | 
Vinko Erceg |  |  |  | 
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Mingguan Xu |  |  |  | mxu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Jie Huang |  |  |  | jiehuang@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 9: Introduction
In legacy system[3], ACK is sent for single MPDU and BA is sent for A-MPDU with multiple MPDUs
Multi-STA Block Ack (M-BA) frame can be used for acknowledging for UL MU frames [1][2]
  Add an indication that the frame is a multi-STA BA (TBD)
  ……
  If B11 in the per-TID info field is set, then the BlockAck bitmap and the SC subfields in the BA Info field are not present and this BA Info field indicates an ACK for the STA with AID indicated in the per-TID info field
B0-B10= AID
B11= ACK/BA
B0-B10= AID
B11= ACK/BA

## Slide 10: Motivation
The current M-BA frame is used to convey the Block ACKs of multiple STAs in response to UL MU frames
M-BA overhead will be increased according to increasing the number of STAs which sent UL MU frames
Duration of M-BA frame will exceed the EIFS duration very often and long M-BA frame will degrade the UL MU performance
This contribution propose an approach to reduce the M-BA frame overhead
# of STAs | 2 | 4 | 8 | 16
M-BA duration (us) | 88 | 120 | 184 | 312
Assumptions: 11a PPDU format(20us preamble), MCS0, Service field (2bytes), Tail (6bits)

## Slide 11: Proposal
AP can correctly receive all MPDUs in an A-MPDU sent by a STA among UL MU PPDUs
  In this case (i.e., STA2), B11 bit in the Per TID Info field is set to 1 to indicate it
  SC subfield and BA bitmap are not present.
If a STA that sent an A-MPDU receives an M-BA with B11 set to 1 in the BA Information pertaining to it, the STA operates as if it had received an immediate BA acknowledging all the MPDUs sent in the A-MPDU
Such an M-BA can be used if there are any other unacknowledged MPDUs from an earlier A-MPDU, but does not acknowledge those.
Trigger frame
AP
STA1
STA2
MPDU (SN =3)
Ack_Policy=00
MPDU
(SN =4)
MPDU
(SN =5)
MPDU (SN =7)
Ack_Policy=00
MPDU
(SN =8)
MPDU
(SN =9)
M-BA
(STA1: B11=0, AID, SSC, bitmap)
(STA2: B11=1, AID)
UL MU frames
MPDU
(SN =4)

## Slide 12: Overhead comparison
How much gain?
Assumptions: 11a PPDU format(20us preamble), MCS0, Service field (2bytes), Tail (6bits)
Overhead reduction gain: 58.7% (108us) for 8 ACK STAs among 8 STAs
Total # of STAs (8)
Number of STAs with ACK among 8 STAs
Number of STAs with ACK among 16 STAs
Overhead reduction gain: 69.2% (216us) for 16 ACK STAs among 16 STAs
Total # of STAs (16)
Chart: Duration of M-BA frame(us)
| 2 | 4 | 6 | 8
M-BA (BA for all 8 STAs) | 184 | 184 | 184 | 184
M-BA (BA for some STAs) | 156 | 128 | 104 | 76
Chart: Duration of M-BA frame(us)
| 6 | 10 | 14 | 16
M-BA (BA for all 16 STAs) | 312 | 312 | 312 | 312
M-BA (BA for some STAs) | 232 | 176 | 124 | 96
The number of STAs with ACK A-MPDU depends on the channel environment

## Slide 13: Discussions
UL MU TXs are initiated by trigger frame (AP) and will be protected by trigger frame
  i.e., A-MPDU TXs with partial error (i.e., BA) will hardly happen in UL MU and the probability for ACK A-MPDUs will be much more than that of partial ACK A-MPDUs, especially in RTS/CTS exchange for UL MU
In case of multiple UL MU frames in a TXOP, multiple M-BA frames are sent and we can save more M-BA duration
  E.g.,) If 108/216us (8/16 STAs, MCS0) per a M-BA is saved, we can save up to 648/1296 us totally for 6 M-BA frames
The saved time duration by reduced M-BA frame will be used for triggering other UL frame (e.g., buffer status request (BSR) , additional UL data, etc.) or for DL frame transmission (e.g., data, management, etc.)

## Slide 14: Conclusion
  Multi- STA Block ACK(M-BA) frame size needs to be minimized because the long M-BA will decrease the UL MU performance and the long M-BA duration can exceed the EIFS duration often
In UL MU procedure, the number of A-MPDUs with all ACK MPDUs will be much more than that of A-MPDU with partial ACK MPDUs
  because most of A-MPDUs sent by STAs can be protected by trigger frame
We propose to use B11 bit in per-TID Info field in order to indicate the ACK of an A-MPDU sent by a STA during UL MU procedure (i.e., M-BA overhead reduction)

## Slide 15: References
[1] 11-15-0132-04-00ax-spec-framework
[2] 11-15-0366-02-00ax-multi-sta-ba
[3] P802.11 REVmc_D4.0

## Slide 16: Straw Poll
Do you agree to modify the sub-clause 7.2 in 11ax SFD as follows?
  7.2 Multi-STA BA
  …..
  If B11 in the per-TID info field is set, then the BlockAck bitmap and the SC subfields in the BA Info field are not present and this BA Info field indicates an ACK for of either single MPDU or all MPDUs carried in the eliciting PPDU that was transmitted by the STA whose the STA with AID is indicated in the per-TID info field