## Slide 1: Additional NGP Use Cases (with some updates to the Use Case Template)
Date: 2015-05-12
Authors:

## Slide 2: Background
This document proposes a concrete definition of accuracy (potentially usable in the PAR/CSD) and a set of attributes that reflect the requirements of specific Use Cases

## Slide 3: Definition of Accuracy
<tbd-1>% of the set of computed estimates from uniformly distributed test locations (covering regions of interest) over a fixed test duration per test location are within <tbd-2>
  E.g. 90% of the set of computed estimates from uniformly distributed test locations over a fixed test duration per test location are within one meter
  Stated as <tbd-2>@<tbd-1> or less than <tbd-2>@<tbd_1> in the Use Case
Discussion
  What would be a good value for the number of “uniformly distributed test locations” in order to render the corresponding accuracy statistically significant? TBD

## Slide 4: Key Performance Requirement
Expected Horizontal Accuracy
  e.g., <1m@90%
Expected Vertical Accuracy
  e.g., <0.5m@90%
Angular accuracy:
  Applies only for Use Cases that require AoA (e.g., cars in a toll plaza, peer to peer, exhibits in a museum, etc)
  e.g., less than <AoA-tbd> degrees @90%

## Slide 5: Attributes to be identified in Use Case description
Latency: Expected time taken to obtain an location estimate. The process begins with initiating a location request, then computing location, and ends with returning the computed location. E.g. 10 ms latency would indicate that it takes 10 ms to transmit the request, gather measurements, compute an estimate, and transfer the computed estimate
Refresh Rate: This defines how frequently is the computation expected when client moving. E.g. a refresh rate of 10 locations per second would indicate that location needs to be refreshed 10 times in a second
Number of simultaneous users
Power-Location Service Tradeoff – location estimation is more important than power (e.g., user walking with a smartphone) versus power conservation is more important than location estimation (e.g., tags) -- "power at the mobile device participating in location est"
Usage duration – how long does the device capable of operating at the power consumption profile hours vs. minutes
Impact on Network Bandwidth (PAR.CSD uses Medium Usage, keep it consistent)
Ganesh Venkatesan (Intel Corporation)

## Slide 6: 1. Micro location in store
User: Person with a smartphone which has the store app installed
Environment: A store has APs for 802.11 coverage. The store may have APs at the store entrance. The expected AP density is about 1 AP per 4000 sq. ft. with APs supporting HT, VHT and NGP
Use case:
  The user enters the store with their phone
  As soon as user enters, the phone notifies the user about the store promotions
  The user can query details about a product on the app
  The app and smartphone can then help the user navigate to the particular shelf containing the product (foreground acitivity)
  The user stands in queue and as they reach the checkout counter, their loyalty number is brought up on the system (background activity)
Key Performance and Attributes:
  Horizontal accuracy: <0.5 m@90%, vertical accuracy: same floor@99%
  Latency: <500ms
  Refresh Rate: > 1 location/sec
  Number of simultaneous users – depends on the size of the store (a few to as many as 100s)
  Power-Location Estimate Tradeoff – navigation and promotions (location estimate); loyalty number (power)
  Usage Duration – depends on shopping habit (a few minutes to a few hours)
  Impact on Network Bandwidth -- < 3 additional frames per second/device/estimate
Ganesh Venkatesan (Intel Corporation)

## Slide 7: 2. Museum Exhibit Guide
User: Person with a smartphone which has the museum app installed.
Environment: A museum has APs and 802.11 based “Location Beacons” (e.g. Wi-Fi Aware) like STAs. The store may have APs and non AP STAs at the store entrance. The expected infrastructure density is about 1: per TBD sq. ft. and also specially located infrastructure devices in aisles on the celling for LOS or near LOS supporting HT, VHT, DMG and NGP.
Use case:
  The User enters the store with their phone and the app pops up.
  The app shows identifies exhibits at the museum that are of interest to the User (based on a prior input to the app by the User). The location of the identified exhibits at the museum are also presented to the User (either on the smartphone display or on a wearable (e.g. glasses).
  The User selects an exhibit and the smartphone app then helps with guiding the User to the exhibit.
  Once the User arrives at the area where exhibit is, the app displays information on the selected exhibit. The app also displays a map of other exhibits in the same area and when the User selects one or more from the display, the app guides the User toward the selected exhibits and display additional pertinent information
Ganesh Venkatesan (Intel Corporation)

## Slide 8: Museum Exhibit Guide (cont’d)
Key Performance and Attributes:
  Horizontal accuracy: <0.5 m@90%, vertical accuracy: same floor@99%
  Latency: <500ms
  Refresh Rate: > 1 location/sec (slower once the exhibit is reached)
  Number of simultaneous users – depends on the size/popularity of the museum (a few to as many as 100s)
  Power-Location Estimate Tradeoff – navigation to the exhibit (location estimate); other exhibits in the same area (power)
  Usage Duration – depends on the size of the museum (a few hours)
  Impact on Network Bandwidth -- < 3 additional frames per second/device/estimate

## Slide 9: 3. Grocery list in-store guidance
User: Person with a smartphone which has the supermarket app installed.
Environment: The supermarket has APs and 802.11 based “Location Beacon” (e.g. Wi-Fi Aware) like STAs. The store have both APs and non AP STAs at the store entrance and deployed all over the store. The expected AP density is about 1 infrastructure STA / per TBD sq. ft. and also specially located infrastructure devices in aisles on the celling for LOS or near LOS supporting HT, VHT, DMG and NGP.
Use case:
  User populates a grocery list as and when he/she realizes the need for an/a set of item(s). This list and updates to the list as it happens is sent to the grocery store server. Some items in the list could be qualified as ‘needed only if it is on sale’.
  User enters the store with their smartphone and the app pops up.
  The app guides the user navigate to store in order to shop for the items in the list. The navigation can be using the smartphone’s display or via a wearable device like glasses. Along the path through the store, the app also highlights specials/offers on other items that are stocked along/near the item of interest to the user.
  As the user enters the checkout counter, the app reviews items in the list against items in the shopping cart (based on user input to the app during the course of shopping)
Ganesh Venkatesan (Intel Corporation)

## Slide 10: 3. Grocery list in-store guidance (cont’d)
Key Performance and Attributes:
  Horizontal accuracy: <0.5m@99%, vertical accuracy: same 0.5m@99%
  Latency: <500ms
  Refresh Rate: > 1 location/sec
  Number of simultaneous users –a few 10s (could be more on special days like before a holiday or weekends; or time of day)
  Power-Location Estimate Tradeoff – navigation to the items in the list (location estimate); offers/promotion for other items in the same area (power)
  Usage Duration – depends on the size of the museum (a few minutes)
  Impact on Network Bandwidth -- < 3 additional frames per second/device/estimate
Ganesh Venkatesan (Intel Corporation)

## Slide 11: 4. Toll Booth with Video Kiosk
User: User selects a subset of movies from a list which gets downloaded as the vehicle driven by the User passes through a Toll Booth
Environment: A Toll Booth also provides for download of preselected (prior to entering the toll booth) video content. The selection is limited to what could be downloaded within the duration that the user is expected spend in the toll booth. The user could change lanes between selecting the video content and entry into the toll booth. More than 1 person may be pre-selecting or downloading video content simultaneously. STA is VHT and DMG capable.
Use case:
  As the User nears the toll booth (< a mile) a list of available video content (for download) is displayed to the User.
  The User makes selects a subset from the display.
  As the user passes through the toll booth, video content corresponding to the selection is downloaded
Ganesh Venkatesan (Intel Corporation)

## Slide 12: 4. Toll Booth with Video Kiosk (cont’d)
Key Performance and Attributes:
  Horizontal accuracy: <0.5m@99%, vertical accuracy: same 0.5m@99%; Angular Accuracy <5 degrees@99%
  Latency: <500ms
  Refresh Rate: > 1 location/sec
  Number of simultaneous users –a few 10s (those queued up prior to entering the toll booth including those that change lanes)
  Power-Location Estimate Tradeoff – tracking the vehicle and matching it with the selection made (location estimate)
  Usage Duration – depends on the size of the museum (a few seconds)
  Impact on Network Bandwidth -- < an additional frame per second/device/estimate

## Slide 13: References
11-07-2988-04-0000-liaison-from-wi-fi-alliance-to-802-11-regarding-wfa-vht-study-group-consolidation-of-usage-models.ppt
11-14-1464-02-0wng-ng-positioning-overview-and-chalanges.pptx
11-15-0388-00-0ngp-ng-NGP Use Case Template .pptx
Ganesh Venkatesan (Intel Corporation)