## Slide 1: A View on IEEE 802.11ay
Date: 2015-05-11
Authors:

## Slide 2: Motivation
To promote TGay documents development, we’d like to share our view on 802.11ay, especially for (1) what type of new functional features we need to concentrate on to enable the pre-discussed NG60 use cases and (2) what kind of technical aspects we need to consider to establish functional requirements from the key features.

## Slide 3: Use Case Observation (1/2)
Use Case (in 15/0328r4) |  | Range | Throughput | Channel
Ultra Short Range Communication |  | < 10 cm | 10 Gbps | 
4k/8k UHD Transmission |  | < 5 m | < 28 Gbps | Indoor
VR |  | < 10 m | ~20 Gbps | Indoor, LOS
Data Center |  | < 1.5 m | ~40 Gbps | Indoor, Mostly LOS
Video/Mass-data Distribution, VOD |  | < 100 m |  | LOS/NLOS
Mobile Offloading & Multiband Operation |  | < 100 m | ~20 Gbps | Indoor + Outdoor, LOS/NLOS
Mobile Fronthauling |  | < 200 m | ~20 Gbps | Outdoor LOS
Wireless Backhauling | w/ Single Hop | < 1000 m | ~20 Gbps | Outdoor LOS
 | w/ Multi-hop | < 150 m | ~2 Gbps per Link | Outdoor LOS
For the use case in 15/0328r4, ‘Tens of Gbps’, ‘Mobile’, and ‘Outdoor’ are beyond the scope of the IEEE 802.11ad specification.

## Slide 4: Use Case Observation (2/2)
To draw a market impact of the next generation 60 GHz technology, the IEEE 802.11ay specification needs to enable the attractive usage scenarios in the previous slide.
In regards of our gap analysis, the IEEE 802.11ad specification is lack of consideration of ‘Tens of Gbps’, ‘Mobile’, and ‘Outdoor’.
Also, in a market perspective, it would be important to fulfill the needs for a higher data-rate, mobile support, and outdoor support.

## Slide 5: New Functional Features for 802.11ay
Channel
Model
Backward Compatibility
&
Coexistence
Higher Data-rate Support
Outdoor
Support
Mobility
Support
We consider ‘higher data-rate support’, ‘mobility support’, and ‘outdoor support’ as important functional features in 802.11ay.
To integrate those features in the 802.11ay spec, functional requirements can be developed with the constraint of channel characteristics, as well as backward compatibility.

## Slide 6: Functional Feature vs. Tech Items
Higher Data Rate Support
Outdoor
Support
Mobility
Support
MIMO Capability
Overlapping/Clustered-BSS Support
BF Training Enhancement
Large Bandwidth Support
QoS (Quality-of-Service) Support
Coverage Extension
Multi-user Support
Spectral Efficiency Enhancement
MAC Enhancement

## Slide 7: Higher Data-rate Support
The following tech items can be considered to achieve ‘higher data-rate support’:
  MIMO Capability (e.g., spatial or polarization diversity/multiplexing)
  Large Bandwidth Support (e.g., channel bonding)
  Spectral Efficiency Enhancement (e.g., modulation and coding schemes)
  Multi-user Support (e.g., DL MU-MIMO)
  MAC Enhancement
  BF Training Enhancement
  QoS Support
Functional requirements for the tech items can be developed with the constraint of channel characteristics, backward compatibility, as well as power consumption budget (power saving).

## Slide 8: Mobility Support
There are 3 types of time-variance in a radio channel:
  Position of the radio varies over time (i.e., mobility)
  Orientation of the radio varies over time
  Object’s mobility in an environment changes scattering or blockage pattern.
To reflect the ‘mobility support’ in a developed channel model, the following tech items can be considered:
  MAC Enhancement
  BF Training Enhancement
  QoS Support
  Coverage Extension

## Slide 9: Outdoor Support
The following tech items can be considered to achieve ‘outdoor support’ in outdoor access and backhaul:
  BF Training Enhancement
  Large Bandwidth Support
  QoS Support
  Coverage Extension
  Overlapping/Clustered-BSS Support
Functional requirements for the tech items can be developed with the constraint of channel characteristics, backward compatibility, as well as power consumption budget (power saving).

## Slide 10: Conclusion
We have listed the primary functional features in 802.11ay as follows:
  Higher Data-rate Support
  Mobility Support
  Outdoor Support
We’d like to discuss about the technical aspects in 802.11ay tech items to achieve the features and to establish functional requirements.

## Slide 11: References
11-15-0328-04-ng60-ng-60-usage-models.pptx
11-14-1151-08-ng60-ng6-proposed-par.docx