## Slide 1
Reference Box5 Calibration Assumptions and Parameters
Date: 2015-05-14
Authors:

## Slide 2
Authors (continued):

## Slide 3: Background
So far we have achieved a lot of agreements with Box5 calibration [1] and the basic procedure of packet reception and preamble detection concluded from [1] has been accepted in the appendix 4 of 11ax EMD [2].
  Also some simplifications of and TBD parameters in appendix 4 [2] were listed in the subsection “Box 5” in section “System Simulation Calibration” in [2].
    One of the most important calibration assumptions there is: the receiver will be locked by the first-arrived packet, and later-arrived packets are considered as interference.
Though11ax scenarios 1 and 4 [3] are required to be used for Box5 calibration, 11ac SS6 [4] was selected offline as an easy-to-start scenario and more and more members have provided individual results for this simple scenario [5-7*].
Along with the calibration progress, there is a need to summarize our calibration assumptions and parameters in one presentation for clear reference so that
  each member does not need to list the detail calibration/simulation setting in individual submission of calibration results or other system performance evaluation such as DSC/CCAC [8].
  * [5-7] could cover all the involved members where [5] & [6] are joint contributions

## Slide 4: PHY Parameters
PHY parameters | 
BW | All BSSs at 5GHz [80 MHz, no dynamic bandwidth]
Primary channel | Aligned primary 20MHz channel for each co-80MHz-channel BSS; The detection of preamble and BA should only focus on primary 20MHz
Channel model | TGac D NLOS per link
Shadow fading | iid log-normal shadowing (5 or 0 dB standard deviation) per link
Preamble Type | Control: legacy 20us; Data: 11ac (20us+20us for 1antenna case)
AP/STA TX Power | 20/15 dBm per antenna
Power Spectral density | Scaled to 80 MHz
number of antennas at AP /STA | 1/1
AP /STA antenna gain | 0/-2 dBi
Noise Figure | 7dB
CCA-ED threshold | -56 dBm (measured across the entire bandwidth after large-scale fading)
Rx sensitivity/CCA-SD | -76 dBm (a packet with lower rx power is dropped)
Link Adaption | Fixed MCS =5 for 11ac SS6 and TBD for 11ax SS1-4
Channel estimation | Ideal unless otherwise specified
PHY abstraction | RBIR, BCC [ 2, 9]
Symbol length | 4us with 800ns GI per OFDM symbol

## Slide 5: MAC Parameters
MAC parameters | 
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=3 ]
Queue length | A single queue for each traffic link is set inside AP/STA sized of 2000 packets
Traffic type | UDP CBR with rate 10^8bps (may not enough to model full buffer) Random start time during a 10ms interval
MPDU size | 1544 Bytes (1472 Data + 28 IP header + 8 LLC header + 30 MAC header + 4 delimiter + 2 padding)
Aggregation | [A-MPDU / max aggregation size / BA window size, No A-MSDU, with immediate BA], Max aggregation: 32 or 64 MPDUs
Max number of retries | 10
Beacon | Disabled unless otherwise specified
RTS/CTS | OFF unless otherwise specified
Running time | >= 10s per drop
Output metric | -CDF or Histogram of per non-AP STA throughput (received bits/overall simulation time) -PER of all AP/STA (1 - # of success subframes / # of transmitted subframes)

## Slide 6: 11ac Scenario 6 – OBSS Enterprise [4]
AP A | (0,0)
AP B | (40,20)
AP C | (-40,-20)
STA3 | (7.5+xb, ‑9.5+yb)
STA9 | (7+xb, -7.5+yb)
STA15 | (3+xb, -0.5+yb)
STA21 | (-6.5+xb, -3+yb)
STA27 | (‑6+xb, 2.5+yb)
STA6 | (-5.5+xc,4.5+yc)
STA12 | (7+xc,7+yc)
STA18 | (10+xc,0.5+yc)
STA24 | (3+xc,2.5+yc)
STA30 | (9.5+xc,3.5+yc)
STA1 | (5,-9.5)
STA2 | (3.5,7.5)
STA4 | (-4.5,0.5)
STA5 | (-1.5,6)
STA7 | (-9,-5)
STA8 | (-8.5,8.5)
STA10 | (-3,0.5)
STA11 | (-0.5,8)
STA13 | (-4,-4)
STA14 | (7.5,-1)
STA16 | (8,-6)
STA17 | (0,-7.5)
STA19 | (-2.5,-4.5)
STA20 | (0.5,-2)
STA22 | (0,-4.5)
STA23 | (-1.5,7)
STA25 | (3.5,-5)
STA26 | (9,9.5)
STA28 | (-8,-5.5)
STA29 | (1.5,3.5)
Fixed Location and Association

## Slide 7: Step-by-Step Calibration of 11ac SS6
1 BSS (upper-right corner BSS B)
  DL only case
  UL only case
    1 STA: each STA-AP
    2 STAs: 3+9, 3+15, 3+27
    3 STAs: 3+9+15, 3+9+27
  DL & UL case
2 BSS (A+B)
  Both DL only
  Both UL only
  A DL and B UL
  B UL and A DL
3 BSS
  DL only
  UL only
  Mixed DL & UL
Note: here no shadowing is assumed and 1 drop is ok to get the result to facilitate the calibration

## Slide 8: Summary
Besides the main agreements in [1,2], detail Box5 calibration parameters were clarified.
We agreed to firstly calibrate 11ac SS6 for Box5 step by step.
We’d like to formally include the contents in this presentation into the SSD 11-14/0980r10 [3] for reference and citing in future calibration and evaluation.

## Slide 9: Straw Poll
Do you agree that the proposed text as per 15/0681r0 for Box5 calibration is added to the Simulation Document 11-14/0980r10 [3]?
Y/N/A

## Slide 10: Reference
[1] 11-14/1523r5 Offline Discussion Minutes of SLS Calibration
[2] 11-14/0571r8 Evaluation Methodology
[3] 11-14/0980r10 Simulation Scenarios
[4] 11-09/0451r16 TGac Functional Requirements and Evaluation Methodology
[5] 11-15/0051r0 Box5 Calibration Results
[6] 11-15/0674r1 Joint submission for Box 5 calibration
[7] 11-15/0623r1 TGax simulation scenario "Box 5" - calibration results
    [8] 11-15/0652r1 Reference Simulation Model for Dynamic CCA / DSC Calibration
    [9] 11-14/1176r1 PHY abstraction tables for 11ax system level simulation
    [10] 11-15/0681r0 Proposed Text additions to 14/980 for Box5 Calibration