## Slide 1: Bandwidth and Packet Type Detection Schemes for 40-50GHz Millimeter Wave Communication Systems
Authors:

## Slide 2: Introduction
In IEEE 802.11aj specifications, there are three PHY types, control PHY, single carrier PHY, and OFDM PHY
Also, transmission bandwidth can be in 540MHz channel or in 1080MHz channel
This proposal proposes a preamble design for auto-detection of bandwidth and packet type

## Slide 3: Motivations
In 45 GHz systems, there are multiple transmission schemes with three different packet formats and two kinds of bandwidth
Why bandwidth auto-detection in preamble?
  RX can perform channel estimation on only the occupied bandwidth other than the maximum transmission bandwidth
  Also, especially for single carrier packets, since there are no other training fields allowing RX to update channel estimation for different bandwidth
Why packet format auto-detection in preamble?
  With packet type knowledge before channel estimation and PHY header decoding, RX does NOT have to perform parallel decoding for multiple possible packet formats

## Slide 4: Preamble Design (1/3)
There are five possible transmission schemes, inlcuding
  Control PHY transmission only uses 540 MHz primary channel for simple interoperability.
  SC and OFDM both can use 540 MHz or 1080 MHz
Utilize different polarizations of ZCZ 256 (Z256) sequences in preamble, RX can do auto-detection of packet types and bandwidth

## Slide 5: Preamble Design (2/3)
Signature symbol sets the boundary for starting BW and packet type detection
At lest two repetitions in CEF for better channel estimation

## Slide 6: Preamble Design (3/3)
The following sign patterns from CE symbols are used for bandwidth and packet type detection
  The first sign pattern
  indicates the BW
  The second and third signs
  indicate the packet type
Pattern | Channel BW | Packet Type
- - + | 540 MHz | Control PHY
- + - | 540 MHz | SC PHY
- + + | 540 MHz | OFDM PHY
+ - + | 1080 MHZ | SC PHY
+ + + | 1080 MHz | OFDM PHY

## Slide 7: Simulations
Correct detection includes
  Signature symbol detection
  Bandwidth detection
  Packet format detection
Simulation setup
  PHY type: Control PHY, SC 540MHz, OFDM 540MHz, SC 1080MHz, OFDM 1080MHz
  Channel: AWGN
  CFO: 0 ppm, +/- 5 ppm, +/- 10 ppm

## Slide 8: AWGN Simulation Results (1/5)
Detection error rate: AWGN & CFO 0 ppm
PHY Type | SNR (dB)
Ctrl | -10.4
SC540 | -10.5
OFDM540 | -10.3
SC1080 | -10.5
OFDM1080 | -10.4
10-3

## Slide 9: AWGN Simulation Results (2/5)
Detection error rate: AWGN & CFO 5 ppm
10-3
PHY Type | SNR (dB)
Ctrl | -9.8
SC540 | -9.6
OFDM540 | -9.7
SC1080 | -9.7
OFDM1080 | -9.7
10-3

## Slide 10: AWGN Simulation Results (3/5)
Detection error rate: AWGN & CFO -5 ppm
10-3
PHY Type | SNR (dB)
Ctrl | -9.6
SC540 | -9.6
OFDM540 | -9.5
SC1080 | -9.5
OFDM1080 | -9.8
10-3

## Slide 11: AWGN Simulation Results (4/5)
Detection error rate: AWGN & CFO 10 ppm
10-3
PHY Type | SNR (dB)
Ctrl | -9.3
SC540 | -9.3
OFDM540 | -9.3
SC1080 | -9.4
OFDM1080 | -9.2
10-3

## Slide 12: AWGN Simulation Results (5/5)
Detection error rate: AWGN & CFO -10 ppm
10-3
PHY Type | SNR (dB)
Ctrl | -9.3
SC540 | -9.3
OFDM540 | -9.4
SC1080 | -9.2
OFDM1080 | -9.3
10-3

## Slide 13: AWGN Performance Summary
Detection SNR @ 10-3 error rate
Comments
  In general, when doing signature symbol detection, CFO has been compensated within 10 ppm or less
  10 ppm CFO only introduces up to 1.3 dB loss
  The detection capability is around -9 dB and fits for current 11aj 45 GHz specs.
 | 0 ppm | 5 ppm | -5 ppm | 10 ppm | -10 ppm
Ctrl | -10.4 | -9.8 | -9.6 | -9.3 | -9.3
SC540 | -10.5 | -9.6 | -9.6 | -9.3 | -9.3
OFDM540 | -10.3 | -9.7 | -9.5 | -9.3 | -9.4
SC1080 | -10.5 | -9.7 | -9.5 | -9.4 | -9.2
OFDM1080 | -10.4 | -9.7 | -9.8 | -9.2 | -9.3

## Slide 14: Summary
A preamble design is proposed for packet type and bandwidth auto-detection
Simulations show that detection performance fits current 11aj specification requirements

## Slide 15: References
[1] 11-14-1363-00-00aj-preamble-sequence-for-802-11aj-45ghz
[2] Complete-specification-proposal-IEEE-802.11aj(45GHz)_v0.1.1
[3] 11-14-0807-01-00aj-ldpc-coding-for-45ghz

## Slide 16
BACKUP
May 2015
Slide 16
Frank Hsu, et. al. (MediaTek)

## Slide 17: AWGN Simulation Results
Detection error rate: AWGN & CFO 20 ppm
10-3
PHY Type | SNR (dB)
Ctrl | -7.8
SC540 | -7.6
OFDM540 | -7.7
SC1080 | -7.7
OFDM1080 | -7.7
10-3

## Slide 18: AWGN Simulation Results
Detection error rate: AWGN & CFO -20 ppm
10-3
PHY Type | SNR (dB)
Ctrl | -7.9
SC540 | -7.7
OFDM540 | -7.9
SC1080 | -7.7
OFDM1080 | -7.8
10-3

## Slide 19: Exp 4ns Simulation Results
Detection error rate: Exp 4ns & CFO 0 ppm
PHY Type | SNR (dB)
Ctrl | -10.7
SC540 | -10.4
OFDM540 | -10.5
SC1080 | -10.6
OFDM1080 | -10.7
10-2

## Slide 20: Exp 10ns Simulation Results
Detection error rate: Exp 10ns & CFO 0 ppm
PHY Type | SNR (dB)
Ctrl | -9.4
SC540 | -9.7
OFDM540 | -9.7
SC1080 | -9.4
OFDM1080 | -9.4
10-2

## Slide 21: Exp 20ns Simulation Results
Detection error rate: Exp 20ns & CFO 0 ppm
PHY Type | SNR (dB)
Ctrl | -8.2
SC540 | -8.3
OFDM540 | -8.2
SC1080 | -7.9
OFDM1080 | -8.5
10-2

## Slide 22: CE Schemes
Five CE schemes
  Colored Z256s are taken to estimate the channel
Scheme | CEF Sign Sequence
1 | +
2 | + -
3 | + +
4 | + +
5 | + + +
May 2015
Slide 22
Frank Hsu, et. al. (MediaTek)

## Slide 23: Simulation Setup
Packet Type/BW: SC 540 MHz
Packet Size: 1050 bytes
MCS: BPSK and LDPC 1/2
Channel: AWGN, Exp 4ns, Exp 10ns
5 CE schemes
May 2015
Slide 23
Frank Hsu, et. al. (MediaTek)

## Slide 24: AWGN
Scheme | SNR @10-1 PER
1 | 1.29
2 | 1.29
3 | 1.29
4 | 1.28
5 | 1.28
May 2015
Slide 24
Frank Hsu, et. al. (MediaTek)

## Slide 25: Exp 4ns
Scheme | SNR @10-1 PER
1 | 3.13
2 | 3.09
3 | 3.07
4 | 3.07
5 | 3.05
May 2015
Slide 25
Frank Hsu, et. al. (MediaTek)

## Slide 26: Exp 10ns
Scheme | SNR @10-1 PER
1 | 3.73
2 | 3.45
3 | 3.41
4 | 3.47
5 | 3.42
May 2015
Slide 26
Frank Hsu, et. al. (MediaTek)

## Slide 27: Comments
For short delay spread channels, AWGN And Exp 4ns, CE of all schemes has enough accuracy (required SNRs are within 0.1 dB difference)
For long delay spread channels, schemes 2 and scheme 3 CE provides enough accuracy, and adding more Z256 sequences provides little performance gain
Sign inversion of Z256 sequences does NOT cause any significant performance loss
May 2015
Slide 27
Frank Hsu, et. al. (MediaTek)