## Slide 1: Complete Proposal for IEEE 802.11aj (45 GHz)
Date: 2015-05-19
Author(s)/Supporter(s): |  |  |  | 
Name | Company | Address | Phone | Email
Shiwen He | SEU |  |  | shiwenhe@seu.edu.cn
Haiming Wang | SEU |  |  | hmwang@seu.edu.cn
Yongming Huang | SEU |  |  | huangym@seu.edu.cn
Wei Hong | SEU |  |  | weihong@seu.edu.cn
Luxi Yang | SEU |  |  | lxyang@seu.edu.cn
Jiang Hua | ZTE |  |  | Jiang.Hua@zte.com.cn
Jun Zhang | ZTE |  |  | zhang.jun7@zte.com.cn
Liguang Li | ZTE |  |  | li.liguang@zte.com.cn
Jun Xu | ZTE |  |  | xu.jun@zte.com.cn
Zhifeng Yuan | ZTE |  |  | yuan.zhifeng@zte.com.cn
Bo Sun | ZTE |  |  | sun.bo1@zte.com.cn
Ke Yao | ZTE |  |  | yao.ke5@zte.com.cn
Kaibo Tian | ZTE |  |  | tian,kaibo@zte.com.cn
Jianhan Liu | Mediatek Inc. |  |  | jianhan.liu@mediatek.com
Frank Hsu | Mediatek Inc. |  |  | frank.hsu@mediatek.com

## Slide 2
Author(s)/Supporter(s): |  |  |  | 
Name | Company | Address | Phone | Email
Xiaoming Peng | I2R |  |  | pengxm@i2r.a-star.edu.sg
Pei Liu | Huawei/Hisilicon |  |  | liupei@hisilicon.com
Jiamin Chen | Huawei |  |  | jiamin.chen@mail01.huawei.com
Dejian Li | Huawei |  |  | lidejian@huawei.com
Yan Li | Gigaray |  |  | yan_li@gigaray.cn
Feng Huang | Gigaray |  |  | feng_huang@gigaray.cn
Xiaohua Jiang | Lenovo |  |  | jiangxh@lenovo.com
Weixia Zou | BUPT |  |  | zwx0218@bupt.edu.cn
Lan Zhu | CESI |  |  | this_zl7812@163.com

## Slide 3: Proposal overview
This presentation is part and in support of the complete proposal described in (slides) and (text) that:
  Supports data transmission rate up to 15 Gbps
  Supplements and extends the 802.11 MAC and is backward compatible with the IEEE 802.11 standard
  Enables both the low power and the high performance devices, guaranteeing interoperability and communication at gigabit rates
  Supports beamforming, enabling robust communication at distance up to 10 meters
  Supports advanced power management
  Supports coexistence with other 45GHz systems
  Supports fast session transfer among 2.4 GHz, 5 GHz and 45 GHz bands

## Slide 4: Proposal presentation plan
ID | Item | Type | Subclauses from 802.11-10/433r2 | Doc#
1 | Complete proposal overview | Complete proposal (CP) | High-level proposal overview | Slides: Text:
2 | MAC (Channel Access & QoS) | New Technique (NT) | 8, 9.3,9.7,9.9-9.16,-9.19, 9.24-9.31, 9.37 | 
3 | MAC (Sync & power saving) | NT | 10 | 
4 | PHY | NT | All in 21, except 21.3.6, 21.5, 21.7 | 

## Slide 5: Additional proposal supporting documents
To meet the TGaj PAR, FRD, EVM and selection procedure requirements, the following additional supporting documents complement this proposal
Therefore, this proposal meets all the requirements in the TGaj selection procedure to be classified as a complete proposal
ID | Item | Doc#
5 | PAR, FRD and EVM declaration | 
6 | PHY simulation results and methodology | 

## Slide 6
Item | This complete proposal | Subclause of
Network architecture | Infra-BSS, IBSS, PBSS | 5.2
Scheduled access | Scheduled Service Periods | 9.23.6
Contention access | EDCA tuned for directional access | 9.2
Dynamic allocation of resources | (Re-)allocation of channel time with support to P2P and directionality | 9.23.7, 9.23.8, 9.23.9
Power save | Non-AP STA and PCP power save | 11.2.3
Measurements | Amendments to 802.11k to support directionality | 11.33
PHY | SC and OFDM, with ZCZ preamble | 26
Beamforming | Unified and flexible beamforming scheme | 9.25
Fast session transfer | Multi-band operation across 2.4GHz, 5GHz and 45 GHz | 11.34
Notable amendments to IEEE 802.11
Slide 6

## Slide 7: MAC/PHY proposal overview
Provides an unified and interoperable MAC/PHY across all mmWave implementations
  Scalable across different usages, devices, and platforms
  Adjustable to meet different power vs. performance trade-offs

## Slide 8: MAC
Reference:
  11-15/0558r0 - 45GHz channel access and BSS operation

## Slide 9
45 GHz BSS Operation

## Slide 10: Some Requirements for 45 GHz
User experience for 45 GHz should be in consistence with that of existing 802.11 systems.
A maximum target PHY transmission rate over Gbps to be met as specified in the FRD.
Operating usages like video streaming, file transfer, internet access etc.

## Slide 11
Scope of BSS Operation (1/2)
Channel Setup
efficiently support 45 GHz channelization
  PCP/AP may select to operate in one of the ten 540 MHz channels or one of the five 1080 MHz channel when it starts.
  PCP/AP may dynamically change its channel number with corresponding change in channel bandwidth.
  For a BSS occupying a 1080 MHz bandwidth channel, data transfer can be through 540 MHz bandwidth or 1080 MHz bandwidth

## Slide 12
Scope of BSS Operation (2/2)
OBSS Mitigation
When two BSSs have devices overlapping in service area, or movement of BSSs to a common service area,
  Smooth translation to co-operative interference mitigations.
  Transparent merging of different BSSs using co-operative interference mitigations.

## Slide 13: Channel Operation Solutions
Requirements
  Meet objectives of proposed channel access.
  Efficiently fulfills the requirements for co-operative interference mitigations in densely populated environments.
  Efficiently handle OBSS mitigations.
A general channel operation solution was proposed in next few slides.
NOTE, the details of the general channel operation solution is not yet completed and we call for interested parties to contribute.

## Slide 14: Proposed solution (2/4)
The primary channel of a 1.08 GHz channel is predefined, e.g., Channel 2 is the primary channel within Channel 1
If a PCP/AP intends to start its BSS in a free 540 MHz channel, it selects the primary channel as the first option to transmit its beacon/notification frames. If occupied, it selects the secondary channel.
If both 540 MHz channels are occupied but no PCP/AP operates in this 1.08 GHz channel, a PCP/AP may select either primary or secondary channel to start its BSS.
If both 540 MHz channels are occupied and there exists at least one PCP/AP operates in this 1.08 GHz channel, a PCP/AP must select the primary channel to start its BSS.

## Slide 15: Proposed solution (2/4)
If a PCP/AP intends to start its BSS in a free 1.08 GHz channel, it will transmit beacon/notification frames in the primary channel only.
If no 1.08 GHz channel is free, a PCP/AP select the 1.08 GHz operating channel based on the following priority orders:
  The secondary channel is free.
  All the existing PCPs/APs operate in the primary channel only.
  All the existing PCPs/APs either operate in the primary channel or operate in the secondary channel.

## Slide 16: Proposed solution (3/4)
Suppose that a PCP/AP 1 operates in a 1.08 GHz Channel, e.g., Channel 1, with transmitting beacon/notification frames in a predefined or selected primary channel only, e.g., Channel 2.
  Another PCP/AP 2 that intends to operate in 1.08 GHz channel must also transmit beacon/notification frames in Channel 2.
  Another PCP/AP 3 that intend to operate in 540 GHz channel can start in Channel 2 only.
  Switch to another unoccupied channel

## Slide 17: Proposed solution (4/4)
Suppose that PCP/AP 1 operates in a 540 GHz Channel.
  Another PCP/AP 2 that intends to operate in 1.08 GHz channel must transmit beacon/notification frames in the predefined or selected primary channel, e.g., Channel 2.
    If PCP/AP 1 was operating in Channel 3, PCP/AP 2 must notify the PCP/AP 1 to switch its BSS to Channel 2 or at least transmit beacon/notification frames in Channel 2. (How to notify is TBD.)
  Another PCP/AP 3 that intend to operate in 540 GHz channel may select either Channel 2 or Channel 3 to start if no PCP/AP operates in Channel 1 now; otherwise, it can only start in Channel 2.
  Switch to another unoccupied channel.
Movement of PCPs/APs is TBD.

## Slide 18
45 GHz Channel Access

## Slide 19
Scope of Channel Access
Channel Access:
    Channel access mechanisms: contention based access, contention free access
    Dynamic allocations of channel resources.
    Multi-bandwidth: dynamic bandwidth negotiation

## Slide 20
Channel Access mechanisms
Supports reservation based allocations as well as contention based allocations
    Allocate SPs for devices so that the quality of service (QoS) is guaranteed when required.
    Allocate CBAPs for contention based access to cater to intermittent channel access.

## Slide 21
Dynamic allocation
Supports dynamic allocate/truncate/extend SPs or CBAPs
    Dynamic allocation of channel resources is employed to allocate channel time during scheduled allocations.
    A STA truncates an allocation to release the remaining time in the allocation.
    Dynamic extension of allocation to extend the allocated time in the current allocation. The additional time can be used to support variable bit rate traffic, for retransmissions or for other purposes.

## Slide 22
Dynamic bandwidth operation
Dynamic bandwidth negotiation:
Dynamic bandwidth operation is needed when multi-bandwidth is introduced to 45GHz
    Dynamic bandwidth operation is proposed in IEEE 802.11ac, which allows narrower bandwidth transmission if one or more secondary channels are sensed busy.
    The RTS/CTS exchange is used to negotiate a potentially channel width for subsequent transmissions within the current TXOP.

## Slide 23
Dynamic Bandwidth Operation for 45 GHz
  Dynamic bandwidth operation:
    With dynamic bandwidth subfield set to 1, RTS in duplicate format is transmitted over 1080 MHz channel that is sensed free at the initiator.
    If network allocation vector(NAV) indicates idle at the responder:
      If clear channel assessment(CCA) on the secondary channel has been idle for a point coordination function interframe space(PIFS) period prior to the start of the RTS frame, CTS frame in duplicate format is sent over the 1080 MHz channel.
      Otherwise, CTS is sent only on the primary 540 MHz channel.
    If NAV indicates busy at the responder, no CTS is responded.
    Initiator transmits data only over channel indicated free by CTS.

## Slide 24
Static Bandwidth Operation for 45 GHz
  Static bandwidth operation :
    With dynamic bandwidth subfield set to 0, RTS in duplicate format is transmitted over 1080 MHz channel that is sensed free at the initiator.
    If NAV indicates free at the responder and CCA on the secondary channel has been idle for a PIFS period prior to the start of the RTS frame , CTS frame in duplicate format is sent over the 1080 MHz channel.
    If the secondary channel has been sensed busy at the responder, the initiator will not receive CTS and then it shall invoke the back-off procedure to retransfer the RTS.

## Slide 25
The Flowchart of Dynamic Bandwidth
Dynamic bandwidth operation for IEEE 802.11aj is illustrated in the flowchart.

## Slide 26
Allow STAs that are not targeted by the AP to enter doze state until the end of the TXOP：
  On receipt of a PPDU, the STA determines that the COLOR in the RXVECTOR parameter does not match the COLOR indicated by the AP to which the STA
  is associated.
  With the matching COLOR, the RXVECTOR parameter PARTIAL_AID is not equal to 0 nor does it match the STA’s partial AID.
  With the matching partial AID, the RA in the MAC header of the corresponding frame that is received correctly does not match the MAC address of the STA.
  540 MHz STAs receive a Beacon frame or a Set PCO frame that contains the PCO Phase field equal to 1.
  In a received PSMP frame, the STA finds that the STA_AID field is not its AID nor does the PSMP Group Address ID match its Group Address .
  The STA receives a frame intended for it with the More Data field equal to 0 and the Ack Policy subfield in the QoS Control field is equal to No Ack or sends an acknowledgment if Ack Policy subfield is not equal to No Ack.
TXOP Power Save

## Slide 27: Proposed changes
Base on Draft P802.11REVmc D4.0, we proposed to add/modify the following subclauses in the complete proposal of 802.11aj (45GHz)
9.xx QMG channel access
  9.xx.1 General
  9.xx.2 Access period within a BI
  ......
  9.xx.a CBAP transmission
  9.xx.b SP transmission
  9.xx.c Dynamic bandwidth negotiation
  …….
10.xx QMG BSS Operation
  10.xx.1 Basic QMG BSS functionality
  10.xx.2 Channel selection methods for a QMG BSS
  10.xx.3 Scanning requirements for QMG STA
  ……
  10.xx.a 540/1080MHz QMG BSS operation
  10.xx.b Channel switching methods for a QMG BSS
  10.xx.c Communicating 540/1080MHz BSS coexistence information

## Slide 28: PHY
Reference:
  11-15/0701r1 - Physical Channel Encoding for 45Ghz
  11-14/0716r4 - PHY-SIG-frame-structure-for-ieee-802.11aj (45GHz)
  11-14/1082r3 - PPDU-format-for-ieee-802.11aj (45GHz)
  11-15/0705r0 - Control PHY Design for 40-50GHz Millimeter Wave Communication Systems
  11-16/0706r0 - Bandwidth and Packet Type Detection Schemes for 40-50GHz Millimeter Wave Communication Systems

## Slide 29: Agenda
Channelization
PHY Overview
  PHY general parameters
Common Preamble Preview
  ZCZ sequences
  Preamble structure
    Short preamble
    CEF
Coding scheme
  LDPC
Single Carrier modulation
  Control MCS
  Single carrier MCS set
OFDM modulation
RF General parameters

## Slide 30: Channelization
CH 1
CH 1
B0 = 1080 MHz
42.66GHz
42.93GHz
B0 = 540 MHz
CH 2
CH 3
CH 4
CH 5
CH 6
CH 7
CH 8
CH 9
CH 10
46.44 GHz
47.52GHz
48.06 GHz
42.3 GHz
47.0 GHz
47.2 GHz
48.4 GHz
CH 2
CH 3
CH 4
CH 5
46.17 GHz
47.79 GHz
B0 = 540 MHz:
B0 = 1080 MHz:
1.08 GHz
1.62 GHz=3*0.54 GHz

## Slide 31: PHY Overview
Unified and interoperable PHY
  Common preamble
  Common MCS
  Common coding
Different MCS sets for different usages: OFDM and SC
  OFDM MCSs for high performance on frequency selective channels up to 64 QAM
  SC modulation for low power/low complexity transceivers
    SC MCS for control signaling (Channel, SNR durability)
    SC Low Power MCS set
      Simpler coding and shorter symbol structure to enable low power implementation

## Slide 32: PHY Parameters

## Slide 33: PHY General parameters
Sampling rate
  SC PHY MCS set Symbol Rate = 440 MHz for 540MHz channel, =880 MHz for 1080MHz channel
  OFDM MCS set Sampling Rate = 660MHz for 540MHz channel, =1320 MHz for 1080 MHz channel
    Sampling Rate is Exactly 1.5x the SC symbol rate
SC block – 256 symbols of which 64 or 32chips GI for 540MHz, 512 symbols of which 128 or 64chips GI for 1080MHz
  OFDM nominal sample rate = 660 MHz for 540 MHz channel, =1320 MHz for 1080MHz channel (1.5 times SC symbol rate)
Common Packet Structure

## Slide 34: Preambles

## Slide 35
Slide 35
Common preamble requirements
Low peak side lobe of periodic auto-correlation and low maximum value of periodic cross-correlation.
  to accurate the timing synchronization
Large zero correlation zone of periodic auto-correlation and periodic cross-correlation.
  11aj maximum multipath delay spread: 100ns
  The time of zero correlation zone should be larger than 100ns to eliminate interference of multipath delay.
The elements of preamble sequence should belong to finite collection of symbols, and have optimized periodic correlator.
  to simplify receiver processing and reduce the power consumption
Preamble sequence set should contain several sequences.
  to implement the MIMO technology
Notes: 35

## Slide 36
Slide 36
Definition of ZCZ sequence set
The sequence set is called Zero Correlation Zone (ZCZ) sequence set when the following formula is satisfied:
where, denotes the periodic correlation between and , denotes the energy of the sequence, denotes the ZCZ length, denotes the number of ZCZ sequences.
Notes: 36

## Slide 37
Generator of ZCZ sequence set
Notes: 37

## Slide 38
Slide 38
Generation parameters of .
Finite collection of symbols:
Initial mutually orthogonal aperiodic sequence sets:
DFT matrix:
Coefficient matrix:
Notes: 38

## Slide 39
Slide 39
Generation parameters of .
Finite collection of symbols:
Initial mutually orthogonal aperiodic sequence sets:
DFT matrix:
Coefficient matrix:
Notes: 39

## Slide 40: Preambles

## Slide 41: LDPC Coding

## Slide 42: LDPC Code Set Overview
Four codes of common codeword length of 672, 2016
Cyclic shifted identity (CSI) construction
Submatrix size 42, 126
Excellent coding gain on realistic channels
Construction supports high throughput implementation
Single construction supports code rates of 1/2, 5/8, 3/4, and 13/16

## Slide 43: LDPC Code Set Implementation
Low complexity / low latency encoding
  Shared terms in systematic product calculation across all codes
  Back substitution for parity calculation
High throughput / low power decoding
  Layer decoding
    Each code matrix H has 4 layers with a single set element per column
    4 clock cycles per decoder iteration
  Fully parallel belief propagation decoding
    Code set super-position matrix has single CSI value per location which minimizes decoder multiplexing and routing
    1 clock cycle per decoder iteration

## Slide 44: LDPC Matrices
-1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | 0 | -1 | -1 | -1 | -1 | -1 | -1 | -1
0 | -1 | -1 | 34 | -1 | 12 | -1 | 36 | 18 | 0 | -1 | -1 | -1 | -1 | -1 | -1
8 | -1 | 0 | -1 | 0 | -1 | 0 | -1 | -1 | 13 | 0 | -1 | -1 | -1 | -1 | -1
-1 | 16 | 40 | -1 | 32 | -1 | 22 | -1 | -1 | -1 | 19 | 0 | -1 | -1 | -1 | -1
-1 | 20 | -1 | 22 | -1 | 2 | -1 | 28 | 32 | -1 | -1 | 21 | 0 | -1 | -1 | -1
30 | -1 | 18 | -1 | -1 | 14 | -1 | 30 | -1 | 37 | -1 | -1 | 31 | 0 | -1 | -1
40 | -1 | 12 | -1 | 38 | -1 | 6 | -1 | -1 | -1 | 26 | -1 | -1 | 13 | 0 | -1
-1 | 24 | -1 | 20 | 10 | -1 | 2 | -1 | -1 | -1 | -1 | 18 | -1 | -1 | 5 | 0
-1 | 0 | -1 | 0 | 0 | 0 | 0 | 0 | 0 | -1 | 0 | -1 | -1 | -1 | -1 | -1
0 | -1 | 0 | -1 | 32 | -1 | 22 | -1 | 18 | 0 | 19 | 0 | -1 | -1 | -1 | -1
8 | 16 | 40 | 34 | -1 | 12 | -1 | 36 | 32 | -1 | -1 | 21 | 0 | -1 | -1 | -1
30 | 20 | 18 | 22 | 38 | -1 | 6 | -1 | -1 | 13 | -1 | -1 | 31 | 0 | -1 | -1
-1 | 24 | -1 | 20 | -1 | 2 | -1 | 28 | 16 | 37 | -1 | -1 | -1 | 13 | 0 | -1
40 | -1 | 12 | -1 | 10 | 14 | 2 | 30 | -1 | 19 | -1 | -1 | -1 | -1 | 5 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -1 | -1 | -1
8 | 16 | 40 | 34 | 32 | 12 | 22 | 36 | 18 | 13 | 19 | 0 | -1 | 0 | -1 | -1
30 | 20 | 18 | 22 | 38 | 2 | 6 | 28 | 32 | 37 | 26 | 21 | 31 | -1 | 0 | -1
40 | 24 | 12 | 20 | 10 | 14 | 2 | 30 | 16 | 19 | 34 | 18 | -1 | 13 | 5 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -1 | -1
30 | 20 | 18 | 22 | 38 | 2 | 6 | 28 | 32 | 37 | 26 | 21 | 34 | -1 | 0 | -1
40 | 24 | 12 | 20 | 10 | 14 | 2 | 30 | 16 | 19 | 34 | 18 | 8 | 13 | 5 | 0

## Slide 45: SC MCS 0: Control MCS

## Slide 46: Control MCS
Very low SNR modem to allow pre-beamforming link
Control MCS based on SC modulation ~11 Mbps
π/2 13/7/4 Bark spreading sequence
Spreading mitigates long channels
A-MPDU aggregation is not allowed using Control MCS
Maximum length is limited to 1024 bytes

## Slide 47: Single Carrier Parameters

## Slide 48: SC Modulation
For 540MHz channel width
256 chips per symbol
GI with 64 or 32 chips
Pi/2 rotation applied to all modulations
  To reduce PAPR for BPSK
  To enable GMSK equivalent modulation

## Slide 49: SC Modulation
For 1080MHz channel width
512 chips per symbol
GI with 128 or 64 chips
Pi/2 rotation applied to all modulations
  To reduce PAPR for BPSK
  To enable GMSK equivalent modulation

## Slide 50: OFDM Parameters

## Slide 51: OFDM Modulation

## Slide 52: General RF parameters

## Slide 53: RF General Parameters
Transmit EVM for all PHYs
Unified mask for all PHYs
Tx RF Delay
Operating Temperature range
Center Frequency leakage
Transmit Ramp up/down
Center Frequency Tolerance
  ±20 ppm
Symbol Clock Tolerance
  ±20ppm locked

## Slide 54: Simulation Analysis

## Slide 55: 1. Performance simulations under ideal conditions (1/14)
1.1. Performance simulations of single carrier (SC)
1.1.1. SC-SISO
Simulation Environment | Tx=1 | Rx=1 | Frame Length=4096 byte | Synchronization: Ideal | IQ Imbalance: 0db, 0°
 | PHY=SC |  | Frame Number=2000 |  | PA Nonlinearity: Ideal
 | AWGN/11aj Channel |  | Channel Estimation: Ideal |  | Sampling Offset 0 PPM
 | BW=540MHz |  | MMSE Equalization |  | Carrier Frequency Offset=0Hz
MCS Index | MCS0 | MCS1 | MCS2 | MCS3 | MCS4 | MCS5 | MCS6 | MCS7
Modulation Code Rate | BPSK 1/2 | QPSK 1/2 | QPSK 3/4 | 16QAM 1/2 | 16QAM 3/4 | 64QAM 5/8 | 64QAM 3/4 | 64QAM 13/16

## Slide 56: 1. Performance simulations under ideal conditions (2/14)
Conclusion: In SC-SISO mode, the performance in 11aj fading channel is much lower than that in AWGN channel due to the lack of diversity. When PER = 10-1, the performance deterioration of high-order MCS is about 10dB, so we need to consider using analog beamforming.
AWGN channel
11aj channel

## Slide 57: 1. Performance simulations under ideal conditions (3/14)
1.1.2. SC 4 ×4 11aj channel
Simulation Environment | Tx=4 | Rx=4 | Frame Length=4096byte | Synchronization: Ideal | IQ Imbalance: 0db, 0°
 | PHY=SC |  | Frame Number=2000 |  | PA Nonlinearity: Ideal
 | 11aj Channel |  | Channel Estimation: Ideal |  | Sampling Offset 0 PPM
 | BW=540MHz |  | MMSE Equalization |  | Carrier Frequency Offset=0Hz
MCS Index | MCS0 | MCS1 | MCS2 | MCS3 | MCS4 | MCS5 | MCS6 | MCS7
Modulation Code Rate | BPSK 1/2 | QPSK 1/2 | QPSK 3/4 | 16QAM 1/2 | 16QAM 3/4 | 64QAM 5/8 | 64QAM 3/4 | 64QAM 13/16

## Slide 58: 1. Performance simulations under ideal conditions (4/14)
CSD mode, Nss=1
CSD mode, Nss=2
When PER = 10-1, the SNR coverage of 8 MCSs is [-6dB, 14dB]
When PER = 10-1, the SNR coverage of 8 MCSs is [-2dB, 19dB]

## Slide 59: 1. Performance simulations under ideal conditions (5/14)
When PER = 10-1, the SNR coverage of 8 MCSs is [-1dB,24dB]
When PER = 10-1, the SNR coverage of 8 MCSs is [2dB,32dB]
CSD mode, Nss=3
CSD mode, Nss=4

## Slide 60: 1. Performance simulations under ideal conditions (6/14)
STBC mode, Nss=1
STBC mode, Nss=2
When PER = 10-1, the SNR coverage of 8 MCSs is [-6dB,13dB]
When PER = 10-1, the SNR coverage of 8 MCSs is [-2dB,18dB]

## Slide 61: 1. Performance simulations under ideal conditions (7/14)
Conclusion:
When SC system is in CSD mode, the demand of SNR increases gradually with the increase of Nss.
When SNR is in [-6dB, 32dB], we can select Nss and MCS to achieve the optimal system throughput.
When Nss is 1 or 2, STBC mode can achieve a performance gain compared to CSD mode and its slope of PER is higher than CSD.

## Slide 62: 1. Performance simulations under ideal conditions (8/14)
1.2. Performance simulations of OFDM
1.2.1. OFDM 1 ×1 AWGN
Simulation Environment | Tx=1 | Rx=1 | Frame Length=4096byte | Synchronization: Ideal | IQ Imbalance: 0db, 0°
 | PHY=OFDM |  | Frame Number=2000 |  | PA Nonlinearity: Ideal
 | AWGN/11aj channel |  | Channel Estimation: Ideal |  | Sampling Offset 0 PPM
 | BW=540MHz |  | MMSE Equalization |  | Carrier Frequency Offset=0Hz
MCS Index | MCS0 | MCS1 | MCS2 | MCS3 | MCS4 | MCS5 | MCS6 | MCS7
Modulation Code Rate | BPSK 1/2 | QPSK 1/2 | QPSK 3/4 | 16QAM 1/2 | 16QAM 3/4 | 64QAM 5/8 | 64QAM 3/4 | 64QAM 13/16

## Slide 63: 1. Performance simulations under ideal conditions (9/14)
Conclusion: In OFDM-SISO mode, the performance in 11aj fading channel is much lower than that in AWGN channel due to the lack of diversity. When PER = 10-1, the performance deterioration of high-order MCS is about 6dB, so we need to consider using MIMO to increase diversity.
AWGN Channel
11aj Channel

## Slide 64: 1. Performance simulations under ideal conditions (10/14)
1.2.2. OFDM 4 ×4 11aj channel
Simulation Environment | Tx=4 | Rx=4 | Frame Length=4096byte | Synchronization: Ideal | IQ Imbalance: 0db, 0°
 | PHY=OFDM |  | Frame Number=2000 |  | PA Nonlinearity: Ideal
 | 11aj Channel |  | Channel Estimation: Ideal |  | Sampling Offset 0 PPM
 | BW=540MHz |  | MMSE Equalization |  | Carrier Frequency Offset=0Hz
MCS Index | MCS0 | MCS1 | MCS2 | MCS3 | MCS4 | MCS5 | MCS6 | MCS7
Modulation Code Rate | BPSK 1/2 | QPSK 1/2 | QPSK 3/4 | 16QAM 1/2 | 16QAM 3/4 | 64QAM 5/8 | 64QAM 3/4 | 64QAM 13/16

## Slide 65: 1. Performance simulations under ideal conditions (11/14)
CSD mode, Nss=1
CSD mode, Nss=2
When PER = 10-1, the SNR coverage of 8 MCSs is [-7dB, 12dB]
When PER = 10-1, the SNR coverage of 8 MCSs is [-3dB, 17dB]

## Slide 66: 1. Performance simulations under ideal conditions (12/14)
CSD mode, Nss=3
CSD mode, Nss=4
When PER = 10-1, the SNR coverage of 8 MCSs is [-1dB,22dB]
When PER = 10-1, the SNR coverage of 8 MCSs is [1dB,31dB]

## Slide 67: 1. Performance simulations under ideal conditions (13/14)
Beamforming mode, Nss=1
Beamforming mode, Nss=2
When PER = 10-1, the SNR coverage of 8 MCSs is [-10dB,8dB]
When PER = 10-1, the SNR coverage of 8 MCSs is [-6dB, 13dB]

## Slide 68: 1. Performance simulations under ideal conditions (14/14)
STBC mode, Nss=2
When PER = 10-1, the SNR coverage of 8 MCSs is[-4dB,16dB]
Conclusion:
When OFDM system is in CSD mode, the demand of SNR increases gradually with the increase of Nss.
When SNR is in [-7dB, 31dB], we can select Nss and MCS to achieve the optimal system throughput.
When Nss is 1 or 2, beamforming mode can achieve 3dB~4dB performance gain compared to CSD mode. When Nss is 2, STBC mode can achieve 1dB performance gain compared to CSD mode.

## Slide 69: 2. Performance simulations under non-ideal conditions (1/14)
2.1. Performance simulations of single carrier (SC)
2.1.1. SC 4 × 4 11aj channel
Simulation Environment | Tx=4 | Rx=4 | PHY=SC | 11aj Channel | Frame Length=4096byte | 
 | MMSE Equalization |  | Channel Estimation: Correlative | Synchronization: Practical | BW=540MHz | 
 | Carrier Frequency Offset=615kHz |  | PA Back-off: 3dB | IQ Imbalance: 1db, 2° |  | Frame Number=2000
MCS Index | MCS0 | MCS1 | MCS2 | MCS3 | MCS4 | MCS5 | MCS6 | MCS7
Modulation Code Rate | BPSK 1/2 | QPSK 1/2 | QPSK 3/4 | 16QAM 1/2 | 16QAM 3/4 | 64QAM 5/8 | 64QAM 3/4 | 64QAM 13/16

## Slide 70: 2. Performance simulations under non-ideal conditions (2/14)
CSD mode, Nss=1
CSD mode, Nss=2
When PER = 10-1, the SNR coverage of 8 MCSs is [-3dB, 22dB]
When PER = 10-1, the SNR coverage of 8 MCSs is [0dB, 27dB]

## Slide 71: 2. Performance simulations under non-ideal conditions (3/14)
CSD mode, Nss=3
CSD mode, Nss=4
When PER = 10-1, the SNR coverage of 8 MCSs is [3dB, 32dB]
When PER = 10-1, the SNR coverage of 8 MCSs is [4dB, 42dB]

## Slide 72: 2. Performance simulations under non-ideal conditions (4/14)
2.1.2. Performance comparison between ideal and non-ideal SC
CSD mode, Nss=4
CSD mode, Nss=2
Conclusion: With the increase of MCS, the gap between practical and ideal performance becomes bigger. PA nonlinear compression and IQ imbalance have remarkable effect on high-order modulations. Owing to that the low-order modulations work at low SNR, timing synchronization and channel estimation errors make a certain gap between practical and ideal performance.

## Slide 73: 2. Performance simulations under non-ideal conditions (5/14)
2.1.3. SC-PAPR
When p=10-5, with the increase of modulation order, PAPR increases gradually.
PAPR(BPSK) = 4.7dB
PAPR(QPSK) = 4.7dB
PAPR(16QAM) = 6.5dB
PAPR(64QAM) = 7dB
Without the shapping filter:
PAPR(BPSK)=0dB
PAPR(QPSK)=0dB
PAPR(16QAM) = 2.7dB
PAPR(64QAM) = 3.8dB

## Slide 74: 2. Performance simulations under non-ideal conditions (6/14)
2.2. Performance simulations of OFDM
2.2.1. OFDM 4 × 4 11aj channel
Simulation Environment | Tx=4 | Rx=4 | Frame Length=4096byte | Synchronization: Practical | IQ Imbalance: 1db, 2°
 | PHY=OFDM |  | Frame Number=2000 |  | PA back-off: 8dB
 | 11aj Channel |  | Channel Estimation: Correlative |  | Sampling Offset 13.675PPM
 | BW=540MHz |  | MMSE Equalization |  | Carrier Frequency Offset=615375Hz
MCS Index | MCS0 | MCS1 | MCS2 | MCS3 | MCS4 | MCS5 | MCS6 | MCS7
Modulation Code Rate | BPSK 1/2 | QPSK 1/2 | QPSK 3/4 | 16QAM 1/2 | 16QAM 3/4 | 64QAM 5/8 | 64QAM 3/4 | 64QAM 13/16

## Slide 75: 2. Performance simulations under non-ideal conditions (7/14)
CSD mode, Nss=1
CSD mode, Nss=2
When PER = 10-1, the SNR coverage of 8 MCSs is [-1dB, 18dB]
When PER = 10-1, the SNR coverage of 8 MCSs is [1dB, 22dB]

## Slide 76: 2. Performance simulations under non-ideal conditions (8/14)
When PER = 10-1, the SNR coverage of 8 MCSs is [3dB, 26dB]
When PER = 10-1, the SNR coverage of 8 MCSs is [5dB,35dB]
CSD mode, Nss=3
CSD mode, Nss=4

## Slide 77: 2. Performance simulations under non-ideal conditions (9/14)
Beamforming mode, Nss=1
Beamforming mode, Nss= 2
When PER = 10-1, the SNR coverage of 8 MCSs is [-3.5dB, 13dB]
When PER = 10-1, the SNR coverage of 8 MCSs is [-0.7dB, 18dB]
量化：[5 3] | 分组：1
Beamforming

## Slide 78: 2. Performance simulations under non-ideal conditions (10/14)
STBC mode, Nss=2
When PER = 10-1, the SNR coverage of 8 MCSs is [-3.5dB, 13dB]

## Slide 79: 2. Performance simulations under non-ideal conditions (11/14)
2.2.2. OFDM CSD BF STBC performance comparison
BF VS CSD, Nss=1
BF VS CSD Nss=2

## Slide 80: 2. Performance simulations under non-ideal conditions (12/14)
STBC VS CSD, Nss=2
Conclusion:
Under non-ideal conditions, when Nss is 1 or 2, beamforming mode has about 2dB performance gain compared to CSD mode with low-order MSC. With the increase of MCS, the performance gain approaches 4~5dB.
When Nss=2, the performance gain of STBC is not remarkable compared to CSD and approaches 0.9dB with the increase of MCS.

## Slide 81: 2. Performance simulations under non-ideal conditions (13/14)
2.2.3. Performance comparison between ideal and non-ideal OFDM
CSD mode, Nss=4
CSD mode, Nss=2
Conclusion: With the increase of MCS, the gap between practical and ideal performance becomes bigger. PA nonlinear compression and IQ imbalance have remarkable effect on high-order modulations. Owing to that the low-order modulations work at low SNR, timing synchronization and channel estimation errors make a certain gap between practical and ideal performance.

## Slide 82: Conclusions

## Slide 83: Conclusions
This complete proposal meets all the requirements of the TGaj PAR and FRD:
  Supports data transmission rate up to 15 Gbps
  Supplements and extends the 802.11 MAC and is backward compatible with the IEEE 802.11 standard
  Enables both the low power and the high performance devices, guaranteeing interoperability and communication at Gbps data rate
  Supports beamforming and MIMO, enabling robust communication
  Supports power management
  Supports fast session transfer among 2.4 GHz, 5 GHz, 45 GHz and 60 GHz

## Slide 84: Strawpoll
Do you support adopting the complete proposal as the first draft specification D0.01 of the TGaj (45 GHz) amendment?
  Y:
  N:
  A:

## Slide 85: Reference
11-15/0558r0 - 45GHz channel access and BSS operation
11-15/0701r1 - Physical Channel Encoding for 45Ghz
11-14/0716r4 - PHY-SIG-frame-structure-for-ieee-802.11aj (45GHz)
11-14/1082r3 - PPDU-format-for-ieee-802.11aj (45GHz)
11-15/0705r0 - Control PHY Design for 40-50GHz Millimeter Wave Communication Systems
11-16/0706r0 - Bandwidth and Packet Type Detection Schemes for 40-50GHz Millimeter Wave Communication Systems
….