## Slide 1: Summary of Power Save Calibration Results
Date: 2015-07-13
Authors:

## Slide 2
Authors:

## Slide 3: Abstract
To evaluate power efficiency in TGax, the simulation scenario [1] and evaluation methodology documents [2] defined three power save mechanisms currently in 802.11-2012 [3]
  Power save mode (PSM)
  Power save polling (PSP)
  Unscheduled automatic power save delivery (U-APSD)
To support this evaluation, a MAC calibration test is defined in [1] and this contribution summarizes results from different companies for each power save mechanism
  Tabulate percentage time spent in each power state (Listen, RX, TX, Sleep) over simulation run

## Slide 4: Power Save Mode (PSM)
Power Save | DTIM (BI) | PSM Timeout (usec) | PHY State | Percentage Time Spent in Each Power State over Simulation Run |  |  | 
 |  |  |  | Nokia | LG |  | Apple
 |  |  |  | without State Transitions | without State Transitions | with State Transitions | without State Transitions
STA - PSM | Off | Off | Listen | 98.463 | 98.842 | 98.829 | 98.065
 |  |  | RX | 1.391 | 1.136 | 1.136 | 1.906
 |  |  | TX | 0.146 | 0.022 | 0.022 | 0.030
 |  |  | Sleep | 0.000 | 0.000 | 0.000 | 0.000
 | 1 | 50 | Listen | 25.139 | 25.128 | 25.094 | 25.064
 |  |  | RX | 1.371 | 1.180 | 1.180 | 1.966
 |  |  | TX | 0.103 | 0.082 | 0.082 | 0.106
 |  |  | Sleep | 73.386 | 73.610 | 72.910 | 72.864
 | 3 | 50 | Listen | 18.590 | 24.721 | 24.695 | 18.268
 |  |  | RX | 1.110 | 1.053 | 1.053 | 1.322
 |  |  | TX | 0.075 | 0.062 | 0.062 | 0.080
 |  |  | Sleep | 80.225 | 74.164 | 73.930 | 80.331
 | 1 | 100 | Listen | 49.823 | 50.031 | 49.984 | 50.130
 |  |  | RX | 1.369 | 1.180 | 1.180 | 1.954
 |  |  | TX | 0.099 | 0.082 | 0.082 | 0.103
 |  |  | Sleep | 48.708 | 48.707 | 48.357 | 47.814
 | 3 | 100 | Listen | 40.825 | 41.353 | 41.327 | 40.228
 |  |  | RX | 1.235 | 1.053 | 1.053 | 1.629
 |  |  | TX | 0.075 | 0.062 | 98.680 | 0.079
 |  |  | Sleep | 57.866 | 57.532 | 57.299 | 58.064
 | 1 | 200 | Listen | 98.648 | 98.801 | 98.788 | 96.670
 |  |  | RX | 1.332 | 1.136 | 1.136 | 1.906
 |  |  | TX | 0.020 | 0.022 | 0.022 | 0.031
 |  |  | Sleep | 0.000 | 0.041 | 0.041 | 1.392
 | 3 | 200 | Listen | 98.648 | 98.884 | 98.872 | 95.965
 |  |  | RX | 1.332 | 1.024 | 1.024 | 1.895
 |  |  | TX | 0.020 | 0.022 | 0.022 | 0.031
 |  |  | Sleep | 0.000 | 0.070 | 0.070 | 2.109

## Slide 5: Power Save Polling (PSP)
Power Save | DTIM (BI) | PHY State | Percentage Time Spent in Each Power State over Simulation Run |  |  |  | 
 |  |  | LG |  | Apple | Intel | 
 |  |  | without State Transitions | with State Transitions | without State Transitions | without State Transitions | with State Transitions
STA - PSP | Off | Listen | 98.842 | 98.829 | 98.065 | 98.820 | 98.820
 |  | RX | 1.136 | 1.136 | 1.906 | 1.120 | 1.123
 |  | TX | 0.022 | 0.022 | 0.030 | 0.020 | 0.020
 |  | Sleep | 0.000 | 0.000 | 0.000 | 0.000 | 0.000
 | 1 | Listen | 0.091 | 0.072 | 0.142 |  | 
 |  | RX | 1.158 | 1.158 | 1.936 |  | 
 |  | TX | 0.048 | 0.048 | 0.062 |  | 
 |  | Sleep | 98.703 | 98.098 | 97.861 |  | 
 | 3 | Listen | 0.074 | 0.055 | 0.085 | 0.090 | 0.087
 |  | RX | 1.046 | 1.046 | 0.962 | 1.030 | 1.027
 |  | TX | 0.048 | 0.048 | 0.040 | 0.040 | 0.040
 |  | Sleep | 98.832 | 98.662 | 98.912 | 98.780 | 98.617
AP - PSP | Off | Listen | 98.759 | 98.728 | 98.065 | 98.860 | 98.843
 |  | RX | 0.022 | 0.022 | 0.030 | 0.020 | 0.020
 |  | TX | 1.136 | 1.136 | 1.906 | 1.120 | 1.123
 |  | Sleep | 0.000 | 0.000 | 0.000 | 0.000 | 0.000
 | 1 | Listen | 98.703 | 98.661 | 98.003 |  | 
 |  | RX | 0.048 | 0.048 | 0.062 |  | 
 |  | TX | 1.158 | 1.158 | 1.936 |  | 
 |  | Sleep | 0.000 | 0.000 | 0.000 |  | 
 | 3 | Listen | 98.703 | 98.661 | 98.372 | 98.800 | 98.787
 |  | RX | 0.048 | 0.048 | 0.040 | 0.040 | 0.040
 |  | TX | 1.158 | 1.158 | 1.587 | 1.140 | 1.137
 |  | Sleep | 0.000 | 0.000 | 0.000 | 0.000 | 0.000

## Slide 6: U-APSD
Power Save | aProbeDelay (us) | PHY State | Percentage Time Spent in Each Power State over Simulation Run |  |  |  |  |  |  |  | 
 |  |  | LG |  | Apple | Intel |  | Sony |  | Nokia | Huawei
 |  |  | without State Transitions | with State Transitions | without State Transitions | without State Transitions | with State Transitions | without State Transitions | with State Transitions | without State Transitions | without State Transitions
STA - UAPSD | Off | Listen | 98.600 | 98.490 | 98.520 | 98.700 | 98.660 | 98.640 | 98.560 | 98.599 | 98.480
 |  | RX | 0.700 | 0.700 | 0.740 | 0.650 | 0.650 | 0.680 | 0.680 | 0.700 | 0.760
 |  | TX | 0.700 | 0.700 | 0.740 | 0.650 | 0.650 | 0.680 | 0.680 | 0.700 | 0.760
 |  | Sleep | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000
 | 100 | Listen | 0.835 | 0.750 | 0.838 | 0.840 | 0.797 | 0.880 | 0.800 | 0.548 | 0.840
 |  | RX | 0.700 | 0.700 | 0.740 | 0.650 | 0.650 | 0.680 | 0.680 | 0.700 | 0.760
 |  | TX | 0.700 | 0.700 | 0.740 | 0.650 | 0.650 | 0.680 | 0.680 | 0.700 | 0.760
 |  | Sleep | 97.765 | 96.490 | 97.682 | 97.850 | 96.573 | 97.760 | 96.480 | 98.051 | 97.640
AP - UAPSD | Off | Listen | 98.268 | 98.158 | 98.520 | 98.700 | 98.660 | 98.640 | 98.530 | 98.599 | 98.480
 |  | RX | 0.700 | 0.700 | 0.740 | 0.650 | 0.650 | 0.680 | 0.680 | 0.700 | 0.760
 |  | TX | 0.700 | 0.700 | 0.740 | 0.650 | 0.650 | 0.680 | 0.680 | 0.701 | 0.760
 |  | Sleep | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000
 | 100 | Listen | 98.269 | 98.159 | 98.520 | 98.690 | 98.647 | 98.640 | 98.530 | 98.600 | 98.480
 |  | RX | 0.700 | 0.700 | 0.740 | 0.650 | 0.650 | 0.680 | 0.680 | 0.700 | 0.760
 |  | TX | 0.700 | 0.700 | 0.740 | 0.650 | 0.650 | 0.680 | 0.680 | 0.700 | 0.760
 |  | Sleep | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000

## Slide 7: Discussions
Next step is to define baseline power save mechanisms (no power save is an acceptable option) for the traffic profiles outlined in each scenario [1]

## Slide 8: Conclusion
This contribution summarizes the MAC calibration data from different companies, for each power save mechanism (PSM, PS-Poll, U-APSD), defined as baseline in the TGax simulation scenarios
The power save calibration results agree well, this provides a baseline to evaluate power efficiency of 802.11ax proposals
Spreadsheet of power save calibration results is uploaded on mentor under document IEEE 11-15-0787r0 [11]

## Slide 9: References
S. Merlin et al, “TGax Simulation Scenarios,” IEEE 11-14-980r12, Jan 2015
R. Porat et al, “11ax Evaluation Methodology,” IEEE 11-14-571r7, Jan 2015
IEEE 802.11-2012
J. Kneckt et al, “Power save calibration results,” IEEE 11-14-1495r0, Nov 2014
J. Kneckt et al, “Power save calibration,” IEEE 11-15-0103r0, Jan 2015
Y. Li et al, “U-APSD power saving-calibration-results,” IEEE 11-15-0072r0, Jan 2015
E. Wong et al, “Power save calibration results,” IEEE 11-15-306r3, March 2015
H. Choi et al, “Power save calibration,” IEEE 11-15-316r5, March 2015
D. Akhmetov et al, “Calibration Results for PSP and U-APSD,” IEEE 11-15-603r0, May 2015
E. Wong et al, “More power save calibration results,” IEEE 11-15-592r0, May 2015
E. Wong et all, “Power save calibration results,” IEEE 11-15-787r0, July 2015