## Slide 1: Proposed changes to Evaluation Methodologies
Date: 2015-07-13
Authors:

## Slide 2: Abstract
The purpose of this presentation is to provide details around suggested changes to the Evaluation Methodologies document (IEEE 802.11-14/0571r9[1]) in Appendix 2 – Traffic model descriptions for the Gaming Traffic Model. These suggested changes will reflect a better model based on the traffic observation of modern FPS games detailed in the FPS Network Traffic Model submission (IEEE 802.11-15/0061r6)

## Slide 3: Proposed Changes to Evaluation Methodologies
Component | Distribution |  | Parameters |  | PDF
 | DL | UL | DL | UL | 
Initial packet arrival (ms) | Uniform | Uniform | a=0, b=40 | a=0, b=40 | 
Packet arrival time (ms) | Largest Extreme Value | Largest Extreme Value | a=50, b=4.5 | a=40, b=6 | 
Packet size (Byte) | Largest Extreme Value | Largest Extreme Value | a=330, b=82 | a=45, b=5.7 | 
Original Distribution proposal from IEEE 802.11-14/0595r0

## Slide 4
Proposed Changes to Evaluation Methodologies
Current Model vs. Observed Distributions (Uplink Arrival)
Chart: FPS3 uplink Packet Arrival Interval

## Slide 5
Proposed Changes to Evaluation Methodologies
Current Model vs. Observed Distributions (Uplink Framelength)
Chart: FPS3 Uplink Packet Size

## Slide 6
Current Model vs. Observed Distributions (Downlink Arrival)
Proposed Changes to Evaluation Methodologies
Chart: FPS3 Downlink Packet Arrival Interval

## Slide 7
Proposed Changes to Evaluation Methodologies
Current Model vs. Observed Distributions (Downlink Framelength)
Chart: FPS3 Downlink Packet Size

## Slide 8: Proposed Changes to Evaluation Methodologies
Component | Distribution |  | Parameters |  | PDF
 | DL | UL | DL | UL | 
Initial packet arrival (ms) | Uniform | Uniform | a=0, b=20 | a=0, b=20 | 
Packet arrival time (ms) | Largest Extreme Value | Largest Extreme Value | a=15, b=7 | a=23.5, b=10.5 | 
Packet size (Byte) | Largest Extreme Value | Largest Extreme Value | a=390 b=89 | a=158, b=26.2 | 
Suggested changes to the table

## Slide 9
Proposed Changes to Evaluation Methodologies
Proposed Model vs. Observed Distributions (Uplink Arrival)
Chart: FPS3 Uplink Packet Arrival Interval

## Slide 10
Proposed Changes to Evaluation Methodologies
Current Model vs. Observed Distributions (Uplink Framelength)
Chart: FPS3 Uplink Packt Size

## Slide 11
Proposed Changes to Evaluation Methodologies
Proposed Model vs. Observed Distributions (Downlink Arrival)
Chart: FPS3 Downlink Packet Arrival Interval

## Slide 12
Proposed Changes to Evaluation Methodologies
Proposed Model vs. Observed Distributions (Downlink Framelength)
Chart: bytes

## Slide 13
Strawpoll:
Do you agree to change the parameters in Appendix 2 Gaming Traffic Model of the Evaluation Methodologies document (IEEE 802.11-14/0571r9) as:
Yes:
No:
Abstain:
Proposed Changes to Evaluation Methodologies
Component | Distribution |  | Parameters |  | PDF
 | DL | UL | DL | UL | 
Initial packet arrival (ms) | Uniform | Uniform | a=0, b=20 | a=0, b=20 | 
Packet arrival time (ms) | Largest Extreme Value | Largest Extreme Value | a=15, b=7 | a=23.5, b=10.5 | 
Packet size (Byte) | Largest Extreme Value | Largest Extreme Value | a=362 b=129 | a=158, b=26.2 | 
Component | Distribution |  | Parameters |  | PDF
 | DL | UL | DL | UL | 
Initial packet arrival (ms) | Uniform | Uniform | a=0, b=20 | a=0, b=20 | 
Packet arrival time (ms) | Largest Extreme Value | Largest Extreme Value | a=15, b=7 | a=23.5, b=10.5 | 
Packet size (Byte) | Largest Extreme Value | Largest Extreme Value | a=390 b=89 | a=158, b=26.2 | 

## Slide 14
Motion:
Do you agree to change the parameters in Appendix 2 Gaming Traffic Model of the Evaluation Methodologies document (IEEE 802.11-14/0571r9) as:
Yes:
No:
Abstain:
Proposed Changes to Evaluation Methodologies
Component | Distribution |  | Parameters |  | PDF
 | DL | UL | DL | UL | 
Initial packet arrival (ms) | Uniform | Uniform | a=0, b=20 | a=0, b=20 | 
Packet arrival time (ms) | Largest Extreme Value | Largest Extreme Value | a=15, b=7 | a=23.5, b=10.5 | 
Packet size (Byte) | Largest Extreme Value | Largest Extreme Value | a=390 b=89 | a=158, b=26.2 | 

## Slide 15: References
[1] 802.11ax Evaluation methodology - IEEE 802.11-14/0571r9 802.11/dcn/14/11-14-0571-08-00ax-evaluation-methodology
[2] FPS Network Traffic Model - IEEE 802.11-15/0061r6 802.11/dcn/15/11-15-0061-06-00ax-fps-network-traffic-model
[3] Edits on Some Traffic Content for HEW SG Simulation Scenarios - IEEE 802.11-14/0595r0 802.11/dcn/14/11-14-0595-00-00ax-edits-on-some-traffic-content-for-hew-sg-simulation-scenarios