## Slide 1: Addressing Simplifications
Date: 2012-07-09
Authors:

## Slide 2: Abstract
Several addressing-related comments want to make changes in how GLK handles frames, in the interest of simplicity. This submission discusses some of these simplifications and attempts to reach consensus before we close out those comments.

## Slide 3: 3 SYNRA formats add complexity
Re: CID210/223
802.11 development has had significant focus on high performance (11n->ac->ax)
  Several chipsets/vendors are adding HW acceleration in DP
  GLK shouldn’t discourage this, or require HW changes as baseline
Variable sized addresses have higher complexity
  SYNRA Types 1&2 are 7-516 bytes long
  These are not well suited to HW acceleration
  These are more appropriate in Control Plane vs Data Plane
This could be a barrier to adoption
  GLK may not be supported if T1&2 require HW changes…
  .. or HW acceleration be globally disabled due to single GLK feature?

## Slide 4: Straw Poll #1
Would you support biasing SYNRA Type 0 more for the typical case?
  Replace 8b with 22b AID bitmap
  No AID offset (limiting to AID 1-22)
  No I/E subfield (only an explicit inclusion list)
  Assumption is most AP would support limited number of GLK Clients, and can assign to lower AID (from a reserved range) at association
Yes:
No:
Abstain:

## Slide 5: Straw Poll #2
Would you support making SYNRA Type 1 & 2 Optional?
  Support for Types 1 & 2 would individually be indicated at association time
  Unsupported types are dropped by receiving Non-AP GLK STA
Yes:
No:
Abstain:

## Slide 6: Straw Poll #3
Would you support dropping SYNRA Type 2?
  Redundant w/ Type 1
  Possibly byte savings for atypical case (sparse matrix, typical is mostly all or exclude 1)
Yes:
No:
Abstain:

## Slide 7: Usage of FromDS/ToDS bits (1 of 2)
Re: CID149/151/218/233
Rational for using all 3 (or 4) combinations of FromDS/ToDS bits is really about saving 6 bytes
  More appropriate in WG focused/limited to lower speed links
  Consider Van Jacobson header compression/etc, for bigger savings
Savings may be naïve assumption
  Many bridges run single IP stack over Bridged Virtual Interface (Cisco) or Bridge Net Device (Linux)
  Which MAC Addr does IP stack use? AP = Ethernet, per Radio, per SSID; Smartphone = WIFI, BlueTooth, Cellular, other;

## Slide 8: Usage of FromDS/ToDS bits (2 of 2)
Bridging is the purpose that 4 address format was designed for
  Where is the DS when we are talking From or To?
802.11 has specific filtering rules for ToDS and FromDS data frames
  Some HW may implement Rx filtering that prohibits a new definition, which GLK makes mandatory

## Slide 9: Straw Poll #4
Would you support limiting GLK to using 4 address format when sending to associated GLK peers?
  Other 3 combinations of ToDS/FromDS prohibited
Yes:
No:
Abstain: