## Slide 1: Feedback of Channel State Information for Hybrid Beamforming in 802.11ay
Date: YYYY-MM-DD
Authors:

## Slide 2: Abstract
Since MIMO is considered for 802.11ay to improve data rates and the link reliability, hybrid beamforming is recommended for practical implementation in 802.11ay [1][2].
This contribution discusses on the feedback of channel state information (CSI) to enable hybrid beamforming in 802.11ay.

## Slide 3: Hybrid Beamforming
System model
  Received signal:
  y = WRx,BBWRx,RFHFTx,RFFTx,BBs + n = WRx,BBHeffFTx,BBs + n
  where Heff = WRx,RFHFTx,RF is the effective channel.
  Optimal RF and digital weights, WRx,BB, WRx,RF, FTx,RF, FTx,BB at AP (Tx) and STA (Rx) are required to be found in terms of SNR.
  Generally, the number of RF chains is less than the number of antennas (NTx,RF<NTx and NRx,RF<NRx).
Heff = WRx,RFHFTx,RF
DAC
DAC
Digital
filter
Digital
Beamforming
WRx,BB
FTx,BB
y
H
NTx,RF RF chains
NRx,RF RF chains
NTx antennas
NRx antennas
ADC
ADC

## Slide 4: Roles of RF and Digital Beamformings
RF beamforming
Increase the link gain
Digital beamforming
Increase the spatial multiplexing gain
AP (or Tx) needs to know the effective channel matrix (or simply CSI) to obtain beamforming gain.

## Slide 5: Difficulty in Estimating Channel Matrix
Effective channel matrix
We need to know the full CSI, that is, H for the calculation of Heff.
However, it is difficult to estimate full CSI in mmWave systems due to the following reasons.
  Usually we have small SNR value before beamforming.
  The large number of antennas causes to require a huge training overhead.
  Even though the full CSI is obtained, developing the efficient feedback scheme of the full CSI is difficult due to the large size of the channel matrix.
So, we estimate the effective channel matrix instead of the full channel matrix once RF beams are determined.
Heff = WRx,RFHFTx,RF

## Slide 6: Contributions
We here want to provide an example of procedure about how to obtain CSI at TX in hybrid beamforming system.

## Slide 7: Procedure for Hybrid Beamforming Design with Effective Channel Information (1/2)
Determination of RF beamforming/filter
Heff = WRx,RFHFTx,RF
Feedback of effective channel information
Design of digital beamforming/filter
1
2
3
AP
STA

## Slide 8: Procedure for Hybrid Beamforming Design with Effective Channel Information (2/2)
Stage 1: Determination of RF beamforming/filter
  Without considering the effect of digital beamforming/filter (WBB =I , FBB = I), RF beamforming/filter are selected based on the beam training algorithms such as SLS, BRP defined in 802.11ad.
Stage 2: Feedback of effective channel information
  AP sends the pilot sequence.
  STA estimates the effective channel (Heff) and feeds back the effective channel information to AP.
Stage 3: Design of digital beamforming/filter
  AP designs its digital beamforming based on the effective channel information.
  STA obtains its digital beamforming based on the estimated effective channel.

## Slide 9: Conclusion
We discussed on the need to feed back the effective channel information in 802.11ay.
We suggested the procedure to design the hybrid beamforming with the effective channel.
Further study on the difference between feedbacks of effective channel information and digital beamforming may be required for 802.11ay.

## Slide 10: References
[1] IEEE 802.11-14/0606r0, “Next Generation 802.11ad: 30+ Gbps WLAN”
[2] IEEE 802.11-14/0431r0, “Shared MIMO Architecture for 802.11ay”