## Slide 1: Multiplexing of Acknowledgements for Multicast Transmission
Date: 2015/07/13
Authors:

## Slide 2: Background
The TGax Spec Framework Document (SFD)[1] includes mention of BA/ACK multiplexing, as follows;
  The amendment shall include a mechanism to multiplex BA/ACK responses to DL MU transmission. [MU Motion #4, March 2015]
The TGax SFD also includes a definition, as follows;
  MU features include UL and DL OFDMA and UL and DL MU-MIMO.
Response Phase
UL multiplexed BA/ACK
BA/ACK
BA/ACK
BA/ACK
AP
STA x
STA y
STA z
Data Transmission Phase
AP
STA x
STA y
STA z
DL MU PPDU
DL MU(OFDMA/MU-MIMO) PPDU

## Slide 3: Merits of Multicast
Multicast is simultaneous same-data transmission to multiple devices.
Compare to unicast transmission, Multicast is more efficient in many use cases.
Multicast
When Multicast carries same data to multiple devices,
Multicast can achieve high TP and low latency
in a similar manner as OFDMA and MU-MIMO.
Unicast
STA 2
STA N-1
STA 1
STA N
AP
Low TP and large latency
DATA
DATA
DATA
DATA
STA 2
STA N-1
STA 1
STA N
AP
DATA

## Slide 4: Existing ACK procedure for Multicast
Some TGax use cases[2] require Multicast(MC) transmission.
  BA/ACK from some of N-STAs are required to ensure QoS (packet loss rate).
802.11aa[3] has introduced GCR procedure.
  This procedure enables exchange of BAR and BA between AP and at least one multicast receiver.
MC with No ACK
Loss packets never recover.
DATA
STA 2
STA N-1
STA 1
STA N
AP
OK
OK
NG
NG
DATA
BA
BA
MC with sufficient GCR BAs (802.11aa)
Sufficient packets can recover.
OK
OK
NG
NG
DATA
OK
OK
OK
OK
High packet loss rate
Low packet loss rate

## Slide 5: Possible measures to minimize overhead
Multiplexing of acknowledgements can be applied for Multicast PPDU.
  BA/ACKs from STAs are required to ensure QoS, but huge number of BA/ACKs can be significant overhead and degrade performance.
Data Transmission Phase
AP
STA x
STA y
STA z
DL MC PPDU
DL MC(Multicast) PPDU
Response Phase
BA/ACK
BA/ACK
AP
STA x
STA y
STA z
BA/ACK
Overhead
UL multiplexed BA/ACK
BA/ACK
BA/ACK
BA/ACK
AP
STA x
STA y
STA z
Multiplexing of acknowledgements
can reduce the overhead

## Slide 6: Performance analysis
Analysis cases
  Case 1 (No BA-multiplexing): One STA sends one acknowledgement for MC PPDU, repeat this sequence until all STAs finish frame exchange.
  Case 2 (BA-multiplexing): Maximum of 4 STAs send multiplexed acknowledgements for MC PPDU, repeat this sequence until all STAs finish frame exchange.
Analysis conditions
  Multiplexing = 4-user MIMO
  Number of STAs = 1 ~ 30
  MSDU size = 100, 1000, 1500, 2000, 4092 [byte]
  Aggregation = 64 packets
  Duration (Details are in appendix)
    Multicast PPDU Duration = 160, 948, 1388, 1824, 3660 [us]
    BA Duration = 68 [us], BAR Duration = 76 [us]
    SIFS = 16[us], AIFS = 34[us], BO average = 67.5[us]

## Slide 7: Performance analysis results
Metrics1: Overhead duration per one MC transmission sequence
  Overhead of Case 2 (Multiplexing) is lower than that of Case 1 (No multiplexing), especially with more STAs.
Lower is better

## Slide 8: Performance analysis results
Metrics2: Total duration efficiency =
  High efficiency means Case2 (BA-multiplexing) works efficiently.
MSDU size
Higher is better
Total duration of Case1 (No multiplexing)
Total duration of Case2 (Multiplexing)
  e.g.
  MSDU =1500, STA =12
  ➔Efficiency =2
  Total duration with BA-multiplexing is half of total duration with No BA-multiplexing.

## Slide 9: Conclusion
This contribution shows multiplexing of acknowledgements can work efficiently for MC(multicast) PPDU in a similar manner as MU (OFDMA, MU-MIMO) PPDU.
Multiplexing of acknowledgements can reduce more overhead duration with more STAs.

## Slide 10: Straw poll
  Do you agree that multiplexing of acknowledgements can work effectively for Multicast PPDU in a similar manner as DL-MU(OFDMA/MU-MIMO) PPDU?
  Yes: /No: /Abstain:

## Slide 11: Reference
[1] 15/0132r05 “Specification Framework for TGax”
[2] 13/0657r6 “Usage models for IEEE 802.11 High Efficiency WLAN study group (HEW SG) –Liaison with WFA.”
[3] IEEE Std. 802.11aa

## Slide 12
Appendix

## Slide 13: Recap of Multicast (Use-case)
Stadium and e-Education use cases[1][2] include simultaneous same-data transmission to multiple devices in dense environment.
  Dense environments are characterized by existence of many APs and non-APs[3].
  Multicast is one of promising technology for such applications.
Video streaming among teacher and students
Teachers/Students demonstrate theirs desktop to others
e-Education
Stadium
Users are receiving VHD video feed highly compressed
Omni-view (point-of-sight selective mobile broadcasting)

## Slide 14: Calculation details (Durations)
Multicast PPDU Duration = 1388 [us] (e.g. MSDU = 1500[bytes])
  MPDU Length = 1464 (App) + 28 (UDP/IP) + 8 (LLC) + 30 (MAC+FCS) + 4 (Delimiter) + 2 (Pad) = 1536 [bytes]
  PSDU Length = MPDU Length * 64 = 98304 [bytes] = 786432 [bits]
  Data Length = Service + PSDU Length + Tail = 16 + 786432 + 6 = 786454 [bits]
  Data Duration = Ceiling(786454 / 585[Mbps](MCS7, 80MHz, Nss2, L-GI), 4) = 1348 [us]
  VHT Preamble Duration (L-STF/L-LTF/L-SIG/VHT-SIG-A/VHT-STF/VHT-LTF/VHT-SIG-B) = 40 [us]
  PPDU Duration = 1348 + 40 = 1388 [us]
BAR Duration = 76 [us]
  MPDU Length = 2 (Frame Control) + 2 (Duration) + 6 (RA) + 6 (TA) + 2 (BAR Control) + 16 (BAR Info) + 4 (FCS) = 38 [bytes] = 304[bit]
  Data Length = Service + PSDU Length + Tail = 16 + 304 + 6 = 326 [bits]
  Data Duration = Ceiling(326 / 6[Mbps](Legacy), 4) = 56 [us]
  PPDU Duration = 56 + 20(Legacy Preamble Duration) = 76 [us]
BA Duration = 68 [us]
  MPDU Length = 2 (Frame Control) + 2 (Duration) + 6 (RA) + 6 (TA) + 2 (BA Control) + 10 (BA Info) + 4 (FCS) = 32 [bytes] = 256[bit]
  Data Length = Service + PSDU Length + Tail = 16 + 256 + 6 = 278 [bits]
  Data Duration = Ceiling(278 / 6[Mbps](Legacy), 4) = 48 [us]
  PPDU Duration = 48 + 20(Legacy Preamble Duration) = 68 [us]
Other
  SIFS = 16[us], AIFS = 34[us], BO average = 67.5[us]
*This calculation is in case of MU-MIMO, In case of 8-user OFDMA,
Data Dutation = Ceiling(278 / (6[Mbps] / 8)) = 372us
BA PPDU Duration = 372 + 20 = 392us
(One extra user out of 8-user OFDMA resource will occupy
only 1 user resource of 8-user OFDMA resource in next allocation,
not occupy full band resource)

## Slide 15: Calculation details (Sequences)
AIFS+BO
SIFS
SIFS
AP
STA 1
BA
DL MC PPDU
STA 4
STA 5
STA 3
BA
BAR
BA
BAR
Total Duration
Overhead Duration
AIFS+BO
STA 2
BA
BA
AIFS+BO
SIFS
AP
STA 1
BA
DL MC PPDU
STA 4
STA 5
STA 3
BAR
BAR
Total Duration
Overhead Duration
AIFS+BO
STA 2
SIFS
BA
BAR
AIFS+BO
SIFS
BA
Case2
Case1

## Slide 16: Performance analysis results
4-user MIMO
8-user MIMO
4-user OFDMA
8-user OFDMA

## Slide 17: Performance analysis results
4-user MIMO
8-user MIMO
4-user OFDMA
8-user OFDMA
MSDU size
MSDU size
MSDU size
MSDU size

## Slide 18: Performance analysis results
Num. of STAs
4-user MIMO
8-user MIMO
4-user OFDMA
8-user OFDMA
Num. of STAs
Num. of STAs
Num. of STAs