## Slide 1: DCCA/DSC Reference Simulation Results
Date: 2015/07/12
Authors:

## Slide 2
Authors (cont’d):

## Slide 3: Abstract
DCCA/DSC reference simulation results (based on 15/0652r1) collected from multiple contributors all show that the system throughput is significantly improved by changing the CCA-SD threshold.
As next steps, we will continue the efforts to further align the reference simulation results, and also run the simulation in more practical scenarios defined in TGax Simulation Scenarios document, 14/0980r12

## Slide 4: DCCA/DSC Reference Scenario from 15/0652r1
30m
3m
3m
AP1
AP2
STA2
STA4
STA1
STA3
CCA-SD threshold is altered between -76, -66, and -56 dBm and throughput is measured at each APs/STAs

## Slide 5: DCCA/DSC Reference Simulation Results
CCA-SD |  |  | Sony* | WILUS* | NTT* | SRTech* | BCM* | LGE* | MTK* | Nokia*
-76 | BSS1 | STA1 | 51.06 | 54.09 | 48.70 | 43.30 | 67.59 | 67.81 | 49.18 | 53.76
 |  | STA2 | 51.74 | 53.00 | 48.80 | 47.00 | 66.42 | 68.99 | 49.53 | 53.29
 |  | Total | 102.80 | 107.09 | 97.50 | 90.30 | 134.01 | 136.80 | 98.71 | 107.05
 | BSS2 | STA3 | 50.53 | 54.51 | 47.80 | 43.30 | 66.53 | 68.46 | 52.01 | 54.63
 |  | STA4 | 51.40 | 54.36 | 48.20 | 43.10 | 68.19 | 68.22 | 53.82 | 54.12
 |  | Total | 101.93 | 108.87 | 96.00 | 86.40 | 134.72 | 136.68 | 105.83 | 108.75
 | BSS1 + BSS2 |  | 204.73 | 215.96 | 193.50 | 176.70 | 268.73 | 273.48 | 204.54 | 215.79
-66 | BSS1 | STA1 | 93.24 | 95.22 | 93.00 | 93.00 | 85.22 | 93.99 | 100.13 | 94.67
 |  | STA2 | 94.28 | 96.31 | 93.50 | 94.00 | 84.33 | 92.27 | 100.51 | 95.22
 |  | Total | 187.52 | 191.53 | 186.50 | 187.00 | 169.55 | 186.26 | 200.64 | 189.89
 | BSS2 | STA3 | 93.03 | 95.12 | 93.60 | 94.40 | 84.77 | 92.83 | 100.75 | 95.19
 |  | STA4 | 93.93 | 95.93 | 93.10 | 92.70 | 85.00 | 91.98 | 100.20 | 95.00
 |  | Total | 186.96 | 191.05 | 186.70 | 187.10 | 169.77 | 184.81 | 200.95 | 190.19
 | BSS1 + BSS2 |  | 374.48 | 382.58 | 373.20 | 374.10 | 339.32 | 371.07 | 401.59 | 380.08
 | Gain |  | 1.83 | 1.77 | 1.93 | 2.12 | 1.26 | 1.36 | 1.96 | 1.76
-56 | BSS1 | STA1 | 95.26 | 95.70 | 93.00 | 93.00 | 87.80 | 94.58 | 100.79 | 94.82
 |  | STA2 | 96.13 | 95.43 | 93.40 | 94.00 | 86.33 | 92.20 | 100.76 | 95.39
 |  | Total | 193.22 | 191.13 | 186.40 | 187.00 | 174.13 | 186.78 | 201.55 | 190.21
 | BSS2 | STA3 | 95.62 | 95.51 | 93.60 | 94.40 | 87.01 | 93.10 | 101.12 | 95.17
 |  | STA4 | 95.54 | 96.71 | 93.10 | 92.70 | 87.37 | 92.33 | 100.68 | 94.97
 |  | Total | 191.16 | 192.22 | 186.70 | 187.10 | 174.38 | 185.43 | 201.80 | 190.14
 | BSS1 + BSS2 |  | 384.38 | 383.35 | 373.10 | 374.10 | 348.51 | 372.21 | 403.35 | 380.35
 | Gain |  | 1.88 | 1.78 | 1.93 | 2.12 | 1.30 | 1.36 | 1.97 | 1.76
26-112% gain by changing the CCA-SD!
* The simulation results are from individual contributors, company names are used only for convenience

## Slide 6: DSC Calibration Next Steps
Efforts for alignment of baseline simulation
  To add metrics (PER, …)
  To check the backoff timer countdown procedure, the behavior when a collision happens, the behavior for CCA-SD, …
Simulation with practical scenario
  To run the simulation with
    TGax Simulation Scenario 1 (residential scenario) and 2 (enterprise scenario) at least
      Many companies ran the simulation with the both scenarios but different assumptions. Better to run with common assumptions
    Combinations of HEW and Non HEW devices
    Various traffic models (UL only, DL only, UL+DL)

## Slide 7: Conclusion
This joint submission provided simulation results for DCCA/DSC calibration (15/0652r1) of each members
  The results show that the system throughput is significantly improved by changing the CCA-SD threshold
Next steps of the DCCA/DSC calibration were presented
  Efforts for alignment of baseline simulation
  Simulation with practical scenarios

## Slide 8: References
14/0571r9 “11ax Evaluation Methodology”
14/0980r12 “TGax Simulation Scenarios”
15/0652r1 “Reference Simulation Model for Dynamic CCA / DSC Calibration”

## Slide 9: Appendix

## Slide 10: Checkpoint 1 PPDU Duration
PPDU Duration = 1,732 [us]
Detail
  MPDU Length = 1,472 (App) + 28 (UDP/IP) + 8 (LLC) + 30 (MAC+FCS) + 4 (Delimiter) + 2 (Pad) = 1,544 [bytes]
  PSDU Length = MPDU Length * 32 = 49,408 [bytes] = 395,264 [bits]
  Data Length = Service + PSDU Length + Tail = 16 + 395,264 + 6 = 395,286 [bits]
  Data Symbols (MCS5) = CEILING (395,286 / 936) = 423 [symbols]
  Data Duration = 423 * 4 = 1,692 [us]
  VHT Preamble Duration (L-STF+L-LTF+L-SIG+VHT-SIG-A+VHT-STF+VHT-LTF+VHT-SIG-B) = 40 [us]
  PPDU Duration = 1,692 + 40 = 1,732 [us]

## Slide 11: Checkpoint 2 RSSI
 |  | Rx |  |  |  |  | 
 |  | AP1 | AP2 | STA1 | STA2 | STA3 | STA4
Tx | AP1 | - | -63.42 | -39.23 | -39.23 | -65.49 | -65.49
 | AP2 | -63.42 | - | -65.49 | -65.49 | -39.23 | -39.23
 | STA1 | -44.23 | -70.49 | - | -51.29 | -72.42 | -72.72
 | STA2 | -44.23 | -70.49 | -51.29 | - | -72.72 | -72.42
 | STA3 | -70.49 | -44.23 | -72.42 | -72.72 | - | -51.29
 | STA4 | -70.49 | -44.23 | -72.72 | -72.42 | -51.29 | -

## Slide 12: Checkpoint 3 Theoretical System Throughput
Theoretical MSDU throughput calculation for MCS 5 (234Mbps), Aggregation size = 32:
Packet time = VHT preamble time + CEILING ((PPDU size x Aggregation size X 8 + service/tail bits)) / date rate, 4)
= 1732 us
Average packet time = Average medium waiting time + Packet time + SIFS + ACK time
= SIFS + AIFSN x slot time + CW/2 x slot time + Packet time + SIFS + ACK time
= 1926.5 us
Theoretical MSDU throughput = (MSDU size – MAC header) x 8 x Aggregation size / Average packet time
~= 202 Mbps

## Slide 13: Reference Traffic Model / MCS Selection
Parameters | Values
Traffic type | 200Mbps / STA; UDP Random start time during a 10ms interval
MPDU size | 1538 Bytes (from SSD) (1544 Bytes in total incl. all overhead) 1544 Bytes (1472 Data + 28 IP header + 8 LLC header + 30 MAC header + 4 delimiter + 2 padding)
Aggregation | Aggregation: 32 MPDUs with 4-byte MPDU delimiter per A-MPDU No A-MSDU Implicit immediate BA
Traffic direction | UL only
PPDU of Data frame | VHT PPDU (MCS 5, fixed),
PPDU of ACK frame | non-HT duplicate PPDU (6Mbps, BPSK(R=1/2), fixed)
Changes from 15/0652r1
A description of “start time” added in Traffic type (copied from Box5 scenario, 1 July 2015)
The description of MPDU size changed (copied from Box5 scenario, 9 July 2015)

## Slide 14: Reference Operational Parameters
Parameters | Values
BW | All BSSs at 5GHz (Ch36, 5180MHz) [80 MHz, no dynamic bandwidth]
Shadow fading | No shadowing
Data Preamble Type | [5GHz, 11ac], duration is considered.
STA TX Power | 15 dBm per antenna
AP TX Power | 20 dBm per antenna
AP / STA number of TX/RX antennas | 1/1
AP / STA antenna height above floor | 3.0m / 1.5m
AP antenna gain | 0 dBi
STA antenna gain | -2 dBi
Guard Interval Symbol length | 4us / symbol, 800ns 4us with 800ns GI per OFDM symbol
Noise Figure | 7dB
CCA-SD threshold | -76/-66/-56 dBm / 80MHz
CCA-ED (for any signal) threshold | -56dBm/80MHz
PHY abstraction | Use PER table from BCC,1458byte in EMD Appendix 3
Pathloss Model | Exponent of 2 up to 10m, exponent of 3.5 beyond (same as SS3)
Changes from 15/0652r1
The description of Guard Interval changed (copied from Box5 scenario, 9 July 2015)

## Slide 15: Reference Operational Parameters (cont’d)
Parameters | Values
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=3 ]
Queue length | A single queue for each traffic link is set inside AP/STA sized of 2000 packets
Max number of retries | 10
Beacon | Disabled
RTS/CTS | OFF
Running time | >= 10s per drop
# of Test Run | 10 times
Throughput metric | Per non-AP STA throughput (received bits/overall simulation time), measured at MAC SAP (MSDU) PER of all STA (1 - # of success subframes / # of transmitted subframes) # of transmitted A-MPDU subframes per second
Output
Changes from 15/0652r1
“Running time” added (copied from Box5 scenario, 1 July 2015)
“# Test Run” added (1 July 2015)
“PER” and “#transmitted frames” added as an output metric (1 July 2015)

## Slide 16: CCA level and Receiver State Machine for calibration
Apply CCA-SD threshold of -76, -66, and -56 dBm to draw throughput graphs
“Packet reception and preamble detection procedure” shall
  Follow Appendix 4 of Evaluation Methodology document [3]
  Set “PPDU capture window” to 0 ns
  Set “preemption window” to 0 ns

## Slide 17: CCA level and Receiver State Machine for calibration (Cont.)
Confirmation about Rx Sensitivity
  Sony assumes “Rx Sensitivity = CCA-SD” in this calibration
    In this calibration scenario, it means that Rx Sensitivity also varies to -76dBm/-66dBm/-56dBm
    The signal that has rx power below CCA-SD simply drops and doesn’t affect receiver state.
Confirmation about the condition of Rx termination
  Sony assumes that the condition for early Rx termination is only for occurring preamble error.
  Except above condition, once signal detected, reception continues to the end of PPDU.
Let us confirm the implementation
of each simulator.
PLCP
PSDU
Arrived PPDU
Detect/Not detect
depend on
Rx sensitivity=CCA-SD
Rx is terminated
only if preamble error
occurs.
Otherwise, Rx continues
to end of PPDU

## Slide 18: TGax SS1 Related Contributions
DCN | Title | Author (Affiliation)
14/0578r0 | Residential Scenario CCA/TPC Simulation Discussion | Joseph Levy (InterDigital)
14/0832r0 | Performance Evaluation of OBSS Densification | Po-Kai Huang (Intel)
14/0833r0 | Residential Scenario Sensitivity and Transmit Power Control Simulation Results | Ron Murias (InterDigital)
14/0846r1 | CCA Study in Residential Scenario | Gwen Barriac (Qualcomm)
14/0861r0 | Impact of CCA adaptation on spatial reuse in dense residential scenario | Sayantan Choudhury (Nokia)
14/0889r3 | Performance Gains from CCA Optimiation | Nihar Jindal (Broadcom)
14/1199r1 | CCA Study in Residential Scenario - Part 2 | Gwen Barriac (Qualcomm)
14/1225r1 | Considerations on CCA for OBSS Opearation in 802.11ax | Jun Luo (Huawei)
14/1427r2 | DSC Performance | Gustav Wikstrom et al. (Ericsson)
14/1443r0 | Adapting CCA and Receiver Sensitivity | Esa Tuomaala (Nokia)
15/0027r1 | Simulation Based Evaluation DSC in residential scenario | M. Shahwaiz Afaqui (UPC)
15/0085r1 | Legacy Fairness Issues of Enhanced CCA | John Son (WILUS Institute)
15/0357r4 | Scenario 1 CCA Simulation | Knut Odman (Broadcom Corporation)
15/0371r2 | Proposal and simulatin based evaluation of DSC-AP Algorithm | Eduard Garcia-Villegas (UPC)
15/0374r1 | Further Considerations on Legacy Fairness with Enhanced CCA | John Son (WILUS Institute)
15/0543r3 | Simulation Scanario changes for Frequency Re-use | Graham Smith (SR Technologies)
15/0544r0 | Proposed text addityions to 14/980 for frequency re-use | Graham Smith (SR Technologies)

## Slide 19: TGax SS2 Related Contributions
DCN | Title | Author (Affiliation)
14/0832r0 | Performance Evaluation of OBSS Densification | Po-Kai Huang (Intel)
14/0868r1 | UL & DL DSC and TPC MAC simulations | Johan Soder (Ericsson)
14/0889r3 | Performance Gains from CCA Optimiation | Nihar Jindal (Broadcom)
14/1426r2 | DSC and legacy coexistence | Gustav Wikstrom et al. (Ericsson)
14/1427r2 | DSC Performance | Gustav Wikstrom et al. (Ericsson)
15/0050r0 | Modeling components impacting throughput gain from CCAT adjustment | Yu Wang (Ericsson AB)
15/0300r0 | Potential of Modified Signal Detection Thresholds | Gustav Wikstrom (Ericsson AB)
15/0543r3 | Simulation Scanario changes for Frequency Re-use | Graham Smith (SR Technologies)
15/0544r0 | Proposed text addityions to 14/980 for frequency re-use | Graham Smith (SR Technologies)
15/0548r0 | Enterprise Scenario and DSC | Graham Smith (SR Technologies)

## Slide 20: TGax SS3 Related Contributions
DCN | Title | Author (Affiliation)
14/0523r0 | MAC simulation results for DSC and TPC | Laurent Cariou (Orange)
14/0779r2 | DSC Practical Usage | Graham Smith (DSP Group)
14/0832r0 | Performance Evaluation of OBSS Densification | Po-Kai Huang (Intel)
14/0889r3 | Performance Gains from CCA Optimiation | Nihar Jindal (Broadcom)
14/1171r1 | DSC Simulation Results for Scenario 3 | Masahito Mori (Sony)
14/1207r1 | OBSS Reuse mechanism which preserves fairness | laurent cariou (Orange)
14/1403r0 | Performance Analysis of BSS Color and DSC | Masahito Mori (Sony)
14/1427r2 | DSC Performance | Gustav Wikstrom et al. (Ericsson)
14/1448r2 | Considerations for Adaptive CCA | Reza Hedayat (Newracom)
15/0045r0 | Performance Analysis of BSS Color and DSC | Masahito Mori (Sony)
15/0319r1 | Impact of TPC coupled to DSC for legacy unfairness issue | Masahito Mori (Sony)
15/0543r3 | Simulation Scanario changes for Frequency Re-use | Graham Smith (SR Technologies)
15/0544r0 | Proposed text addityions to 14/980 for frequency re-use | Graham Smith (SR Technologies)

## Slide 21: TGax SS4 Related Contributions
DCN | Title | Author (Affiliation)
14/1427r2 | DSC Performance | Gustav Wikstrom et al. (Ericsson)
14/1448r2 | Considerations for Adaptive CCA | Reza Hedayat (Newracom)
15/0543r3 | Simulation Scanario changes for Frequency Re-use | Graham Smith (SR Technologies)
15/0544r0 | Proposed text addityions to 14/980 for frequency re-use | Graham Smith (SR Technologies)

## Slide 22: Other DCCA/DSC Contributions
DCN | Title | Author (Affiliation)
14/0628r0 | Measurements on CCA Thresholds in OBSS Environments | John Son (WILUS Institute), Young Doo Kim (SK Telecom)
14/0635r1 | DSC Implementation | Graham Smith (DSP Group)
14/0637r0 | Spatial Reuse and Coexistence with Legacy Devices | James Wang (mediaTek)
14/0847r1 | Further Considerations on Enhanced CCA for 11ax | John Son (WILUS Institute)
14/0854r0 | DSC and Legacy Coexistence | William Carney (SONY)
14/0856r1 | Evaluating Dynamic CCA/Receiver Sensitivity Algorithms | Brian Hart (Cisco Systems)
14/872r0 | A Protocol Framework for Dynamic CCA | Sean Coffey (Realtek)
14/0880r1 | Increased Network Throughput with TX Channel Width Related CCA and Rules | James Wang (Mediatek)
14/1106r1 | WLAN Frame Collision Information | Peng Shao (NEC Communication Systems)
14/1224r0 | Link Aware CCA | Brian Hart (Cisco Systems)
14/1233r2 | Adaptive CCA for 11ax | Reza Hedayat (Newracom)

## Slide 23: Other DCCA/DSC Contributions (Cont’d)
DCN | Title | Author (Affiliation)
14/1416r1 | Observed Protocol Violations Caused by DSC for Roaming STAs | Chuck Lukaszewski (Aruba Networks)
14/1435r0 | Considerations on OBSS Spatial Reuse | Jianhan Liu (Mediatek Inc.)
14/1580r0 | Perspectives on Spatial Reuse in 11ax | Reza Hedayat (Newracom)
15/0025r0 | DSC and Roaming | Graham Smith (SR Technologies)
15/0105r0 | Dynamic CCA Management | Sean Coffey (Realtek)
15/0318r1 | CCA Regime Evaluation Revisited | Amin Jafarian (Newracom Inc.)
15/0338r1 | ssions on the Definition of CCA Threshold | Akira Kishida (NTT)
15/0588r0 | CCA revisit II | Amin Jafarian (Newracom)
15/0595r2 | Discussion on the Receiver Behavior for CCAC DSC with BSS Color | Yasuhiko Inoue (NTT)
15/0652r1 | Reference Simulation Model for Dynamic CCA / DSC Calibration | Masahito Mori (Sony)