## Slide 1: Frame Collision Information Management
Date: 2015-07-14
Authors:

## Slide 2: Abstract
Interference in 11ax scenarios is a severe problem, which is an obstacle to realizing the goals of 11ax.
We proposed that supporting the use of Frame Collision Information(FCI) would be useful for reducing interference by management and control in 11ax.[1]
In this contribution, we propose methods for management of FCI and show examples of use cases.

## Slide 3: Background
In high density scenarios, frame collisions will increase due to many hidden terminals, and many terminals finish backoff at the same time.
Frame Collision Detection (FCD) can be useful for deciding countermeasures to reduce interference, such as for site survey, multi-rate control, DSC.
FCD methods using energy detection were introduced in [1].
  Compare signal power with noise level before and after frame
  Evaluate the power changes during frame
Other FCD methods are also possible
  Detect change of SYNC or BER during reception [2, 3]

## Slide 4: Brush up(1):Examples of FCD[1]
RSSI signal from power signal sensor [4] or spectral scan mode of WLAN card [5]
PHY state signal from WLAN card [6]
RSSI
RSSI
time
time
power
power
Frame-B
Frame-A
Frame-A
Frame-A
Frame-A + Frame-B
No collisions
Collision
time
tx_frame/2
rx_clear
count
Collision

## Slide 5: Brush up(2): Frame Collision Information (FCI)[1]
Frame Collision Information includes information about the timing of the collision.
Timing information can be useful for identifying collision cause, allowing better choice of control countermeasures.
Example of collision type | Collision cause
Type I: | Cause I: transmitter of frame B cannot sense frame A
Type II: | Cause II: transmitters of A and B finish backoff at the same time
Type III: | Cause III: transmitter of frame A cannot sense frame B
A
B
A
B
A
B
A : target frame B : interference frame

## Slide 6: FCI Management
Zones for Collision Detection in frame
B3:Post-Frame Zone
B0:Pre-frame Zone
B1:Frame Start Zone
frame
Header
Payload
B2:Frame Zone

## Slide 7: FCI Management(cont.)
 | Meta-information | FCD result
Proposal for per-packet FCI
  Meta-information:
    indicate the frame zones which were tested
  FCD result:
    indicate the result of each target zone:
      1: interference detected in zone
      0: interference NOT detected in zone

## Slide 8: FCI Management(cont.)
 | Meta-information | FCD result |  |  | 
 | B0, B3 | 0/1(B0) | B1 | B2 | 0/1(B3)
Example: 2-bit FCI
Detection of collisions in 2 zones: Pre-frame and Post-frame zones.
B3:Post-Frame Zone
B0:Pre-frame Zone
frame

## Slide 9: FCI Management(cont.)
Example: 2-bit FCI
Detection of collisions in 2 zones: Pre-frame and Frame zones.
frame
B0:Pre-frame Zone
B2:Frame Zone
 | Meta-information | FCD result |  |  | 
 | B0, B2 | 0/1(B0) | B1 | 0/1(B2) | B3

## Slide 10: FCI management in PHY/MAC layer
Frame transmission/reception uses PHY-SAP and PMD_SAP primitives between sub-layers in PHY/MAC layer.
We propose to add 2 primitives “PHY-FCI” and “PMD-FCI”.
[7]

## Slide 11: Proposal for additional service primitives
“Request/Confirm” primitives should be included for on-demand communication from upper layer and “Indicate” primitive is also included for urgent indication from lower layer
PHY-FCI | X | X | X
[7]
PMD-FCD | X | X | X | -
[7]

## Slide 12: Example for additional service primitives
PMD primitives are used to gather 4 FCD bits from PHY layer
PHY primitives are used to generate 4-bit FCI from 4 FCD bits
B0:Pre-frame Zone B1:Frame Start Zone B2:Frame Zone B3:Post-Frame Zone
MAC
PHY
PLCP
PHY
PMD
frame
B0
B3
PMD_FCD.req/conf
PHY_FCI.confirm
PHY_FCI.request
PMD_FCD.req/conf
frame
B1
B2
Collision Detection during B1 and B2
Energy Detection during
meta-information
4-FCD results from B0, B1, B2 and B3
Energy Detection during

## Slide 13: Add FCI statistics report
For evaluating the network collision status in a certain period, we propose to add “FCI statistics report” to Measurement Report Set in the primitive “MLME-MEASURE.confirm” so SME(Station Management Entity) can access FCI.
[7]

## Slide 14: Add FCI statistics report(Cont.)
FCI statistics report | 13 | Radio Measurement and WNM
…
Add “FCI statistics report”
[7]

## Slide 15: FCI Use Case
Frame collisions caused by hidden terminals.
Identify most likely collision cause from FCI, and decide corresponding countermeasure to achieve higher throughput in collision environment[8].
Collision Type | FCI(*) | Inferred Collision Cause | Effective Countermeasure
Type I: | 0011 | Cause I: transmitter of frame B cannot sense frame A | Increase Tx Power
Type III: | 1111 | Cause III: transmitter of frame A cannot sense frame B | Reduce CCA level
A
B
A
B
A :target frame. B : interference frame
(*) 4-bit FCI indicates the zone where interference is detected

## Slide 16: FCI Use Case (2)
Simulation Scenario
Scenario | Wtx-Ztx Distance[m] | Tx power[dBm] |  | CCA[dBm] | CWmin
 |  | Wtx | Ztx |  | 
1 | 50 | -10~20 | 10 | -80 | 7
2 | 50 | 10 | 0 | -60 ~ -100 | 7
Transmission parameters setting:
Flow W
Flow Z

## Slide 17: FCI Use Case (3)
Scenario 1
Scenario 2
Wtx
Ztx
:Type III
:Type I
Wtx
Ztx
:Type II
Wtx
Ztx
If many type III detected,
then decrease CCA level
If many Type I detected,
then increase Tx power
CONTROL RULE :
Collision Ratio (%)
Collision Ratio (%)
Simulation Result

## Slide 18: Summary
Proposal of management of Frame Collision Information(FCI)
  The format of per-packet FCI
  FCI management in PHY/MAC layer
  Addition of “Service Primitives” and “Statistics Report” for FCI management
Examples of FCI use cases.
  Reduce interference by transmission control depending on detected collision type.

## Slide 19: References
[1] 11-14/1106r1:“WLAN Frame Collision Information”.
[2]K. Whitehouse, “Exploiting the Capture Effect tor Collision Detection and Recovery”, EmNet 2005.
[3]S, Rayanchu, “Diagnosing Wireless Packet Losses in 802.11: Separating Collision from Weak Signal”, ftp://ftp.cs.wisc.edu/pub/techreports/2007/TR1597.pdf
[4] IEICE Technical Report, SIP2012-125, p259-264, March 2014 , P. Shao.
[5]“ath9k spectral scan”, http://wireless.kernel.org/en/users/Drivers/ath9k/spectral_scan/
[6]“Fwd: FW: Channel busy cycles”, ath9k-devel ML, http://article.gmane.org/gmane.linux.drivers. ath9k.devel/9887/
[7]“ IEEE Std 802.11TM-2012, Wireless LAN medium access control (MAC) and physical layer (PHY) specifications”, 2012.
[8]Y. Baba, “Wireless LAN frame collision control using collision type information,” 2015 ICECCT, EC4015, pp. 1361-1367, March, 2015.

## Slide 20: Appendix 1: Simulation Conditions
Simulation conditions in slide 16

## Slide 21: Appendix 2: Example of rx_clear count
Result of CCA
:0
:1
rx_clear count
0
2
4
4
4
4
2
0
time
time
time
power

## Slide 22: Appendix 3 : requesting FCI from MAC and indicating FCI to MAC with Tx frame
PHY_FCI.indication
(4)
(1)
(2)
PHY_FCI.request
(3)
PMD_FCI.req
PHY_FCI.indication
PMD_FCI.conf
PMD_FCI.ind
PHY_FCI.indication
PHY_FCI.confirm
PMD_FCI.ind
PMD_FCI.conf
PMD_FCI.req
(1):Pre-frame Zone (2):Frame Start Zone (3):Frame Zone (4):Post-Frame Zone

## Slide 23: Appendix 4 : indicating FCI to MAC with Rx frame
(1)
(4)
(2)
(3)
PHY_FCI.indication
PHY_FCI.indication
PMD_FCI.req
PMD_FCI.ind
PMD_FCI.ind
PMD_FCI.req
PMD_FCI.conf
PHY_FCI.indication
PHY_FCI.indication
PMD_FCI.conf

## Slide 24: Appendix 5: Adding FCI statistics report to Measurement Report Set
802.11 standards already have various reports in a measurement report set.
We propose to add “FCI statistics report” to Measurement Type definitions.
  Fig. 8-140 shows Measurement Report element format and Table 8-81 shows Measurement Type definitions for measurement reports.
FCI statistics report | 13 | Radio Measurement and WNM
14

## Slide 25: Appendix 6 :Example of FCI Statistics Report
The format of the Measurement Report field corresponding to a “FCI statistics Report” is shown:
Tx Collision Indicator = Integer((Tx collision count/Tx count)×255)
Rx Collision Indicator = Integer((Rx collision count/Rx count)×255)
Channel Number indicates the channel number for which the measurement report applies. Actual Measurement Start Time is set to the value of the measuring STA’s TSF timer at the time the measurement started. Measurement Duration is set to the duration over which the FCI Report was measured, expressed in units of TUs. TU is equal to 1024us.
 | Operating Class | Channel Number | Actual Measurement Start Time | Measurement duration | Tx Count | Rx Count | Tx Collision Indicator during B0
Octets: | 1 | 1 | 8 | 2 | 4 | 4 | 1
 | Tx Collision Indicator during B1 | Tx Collision Indicator during B2 | Tx Collision Indicator during B3 | Rx Collision Indicator during B0 | Rx Collision Indicator during B1 | Rx Collision Indicator during B2 | Rx Collision Indicator during B3
 | 1 | 1 | 1 | 1 | 1 | 1 | 1