## Slide 1: Interleaver and Tone Mapper for OFDMA
Date: 2015-07-12
Authors:
Name | Affiliation | Address | Phone | Email
Yakun Sun | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | yakunsun@marvell.com
Hongyuan Zhang |  |  |  | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvell.com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 2
Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Tu Nguyen |  |  |  | 
Vinko Erceg |  |  |  | 
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com

## Slide 3
Authors (continued)
Name | Affiliation | Address | Phone | Email
Kiseon Ryu | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Hyeyoung Choi |  |  |  | hy0117.choi@lge.com
Jinmin Kim |  |  |  | Jinmin1230.kim@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 4
Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 5
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Authors (continued)

## Slide 6
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Alice Chen |  |  |  | 
Lin Yang |  |  |  | 
Authors (continued)

## Slide 7
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Bo Sun | ZTE | #9 Wuxing duan, Xifeng Rd, Xi’an, China |  | Sub.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | Yao.ke5@zte.com.cn
Weimin Xing |  |  |  | Xing.weimin@zte.com.cn
Authors (continued)

## Slide 8: Overview
11ax OFDMA resource unit (RU) sizes have been agreed to be [1]
  26, 52, 106, 242, 484, 996x1/2 tones
The interleaver (BCC) and tone mapper (LDPC) design for each size of RU is still open.
  Some RU’s tone plan design implies a reuse of existing design.
  The rest RU does not have existing designs to reuse.
  BCC usage has been proposed to be limited to no larger than 20MHz and Nss≤4 [2].
RU (tones) | BCC |  | LDPC | Reuse
 | Ncol | Nrot | DTM | 
26 | 8 | 2 (Nss≤4) | No? | 11ah 1MHz
52 | 16 | ? | ? | 11a 20MHz
106 | ? | ? | ? | 11ac 40MHz?
242 | 26 | 58 (Nss≤4) | 9 | 11ac 80MHz
484 |  |  | ? | 11ac 160MHz?
996 |  |  | ? | N/A
Existing design
Open

## Slide 9: (1) 52-tone RU, Nrot
Simulation Assumptions
  A STA is assigned with a 52-tone block randomly.
  Ncol=16(11a)
  BCC, 8000 bits
  4Tx, Nss=2, 4; 8Tx, Nss=8. No TxBF.
  Nrot is simulated from 1 to 23.
  D-NLOS (CP=0.8us), UMi-NLOS (CP=1.6us)
  Actual channel estimation, no other impairments
Compared SNR(Nrot) – SNR(Nrot_ref) at PER = 10%
  Nrot_ref =11 for Nss<=4
  Negative value  Nrot performs better than Nrot_ref.

## Slide 10: UMi-NLOS, Nss=2
Observations:
MCS0/1/2 has the same trend over different Nrot.
Even Nrot’s have large performance loss, and odd Nrot’s do not impose large loss for MCS0/1/2
Nrot = 11/13 works best over all MCS/subchannels. In the case other Nrot works better, loss is less than 0.3dB.
MCS>2 and Nss>2 cannot make to PER = 10%.
Relative SNR of each Nrot at PER=10% is compared to Nrot=11 for illustration.

## Slide 11: DNLOS, Nss=2/4
Observations:
Low Nrot (<11) clearly has degradation comparing to Nrot=11 for almost all MCSs at Nss=4.
High Nrot (>11) performs different for different MCS for Nss=2, but closely for Nss=4.
Nrot = 11 has loss is mostly less than 0.4dB for any MCS/Nss, and also an existing 11ac design.
Only simulated odd Nrot
MCS>=3 (lower MCS is not important for MIMO)

## Slide 12: Summary of Nrot for 52-tone RU
Nrot = 11 works overall best for Nss≤4.
  Also used for 11n/ac for 20MHz with 52 data tones, very close to 52-tone RU with 48 data tones.
Nrot = 11 is also an existing design to be reused.

## Slide 13: (2) 106-tone RU Interleaver
11ax 106-tone RU has 102 data tones, with a small set of potential Ncol’s:
  2, 3, 6, 17, 34, 51
11ac 40MHz has 108 data ones, and the BCC interleaver uses Ncol=18.
  Cannot be directly reused for 106-tone RU.
Use Ncol = 17 for 106-tone RU
  Very small difference in the number of data tones between 11ac and 106-tone RU  Ncol=17 should work as well as Ncol=18 for 11ac 40MHz.
  Other potential Ncol’s are either too large or too small.
Reuse Nrot = 29 as in 11n/ac for 106-tone RU for the same reason.

## Slide 14: (3) 26/52/106-tone RU, DTM
26-tone RU (24 data tones)
  Potential DTM = 1 (no tone mapping), 2, 3, 4, 6, 8, 12
52-tone RU (48 data tones)
  Potential DTM = 1 (no tone mapping), 2, 3, 4, 6, 8, 12, 16, 24
106-tone RU (102 data tones)
  Potential DTM = 1 (no tone mapping), 2, 3, 6, 17, 34, 51
Note in 11ac DTM is equivalent to as in BCC interleaver for implementation benefit (see Appendix).

## Slide 15: Analysis on Necessity of Tone Mapper
For 26-tone RU:
  NCBPS ≤ 24 * 8 (256QAM) * 8 (Nss) = 1536 < 1 CW (1944)
For 52-tone RU:
  NCBPS ≤ 48 * 8 (256QAM) * 4 (Nss) = 1536 < 1 CW
  NCBPS ≤ 48 * 8 (256QAM) * 8 (Nss) = 3072 ~ 1.5 CW
For 106-tone RU:
  NCBPS ≤ 102 * 8 (256QAM) * 1 (Nss) = 816 < 1 CW
  NCBPS ≤ 102 * 8 (256QAM) * 2 (Nss) = 1632 < 1 CW
  NCBPS ≤ 102 * 8 (256QAM) * 4 (Nss) = 3264 ~ 1.7 CW
  NCBPS ≤ 102 * 8 (256QAM) * 8 (Nss) = 6528 ~ 3.3 CW
Tone mapper may be necessary only for 52-tone with Nss>4, or 106-tone with Nss>2.
  Confirmed by PER simulations later.

## Slide 16: Simulations
Simulation assumptions
  A STA is assigned with a 26/52/106-tone blocks randomly.
  8000 bit per packet.
  D-NLOS (CP=0.8us),
    1x1, Nss=1; 2x2, Nss = 2; 4x4, Nss=4; 8x8, Nss=8. No TxBF.
  UMi-NLOS (CP=1.6us)
    1x1
  Actual channel estimation, no other impairments.
Compared SNR(DTM) – SNR(DTM=1) at PER = 10%
  DTM = 1  no tone mapping.
  If negative value  tone mapping performs better than no tone mapping.

## Slide 17: 26-Tone, Nss=1
Performance with tone mapping and no tone mapping are very close, within +/-0.3dB  tone mapping is not necessary.

## Slide 18: 26-Tone, Nss = 4, 8
Performance of tone mapping for Nss=4 provides less than 0.5dB gain, and less than 1dB for Nss=8.
Tone mapping is not critical.

## Slide 19
52-Tone, Nss=1
Similar to 26-tone RU, performance with tone mapping and no tone mapping are very close, within +/-0.3dB  tone mapping is not necessary.

## Slide 20
52-Tone, Nss = 4, 8
Performance of tone mapping for Nss=4 provides less than 1dB gain, and 1.5~2dB for Nss=8.
DTM = 6 works overall best for Nss>4, and DTM=3 performance is very close.
DTM = 3 is equivalent to Ncol = 16, which is an existing design.

## Slide 21
106-Tone, Nss=1
Tone mapping provides less than 1dB performance gain over no tone mapping  tone mapping is not critical.

## Slide 22
106-Tone, Nss = 2, 4, 8
Performance gain of tone mapping increases to 1 dB for (Nss=2), or 2dB (Nss=4), or 4dB (Nss=8)
DTM=6 provides overall best performance (cross all MCS/Nss).

## Slide 23
Summary of DTM for 26/52/106-tone RU
Performance gain of tone mapping over no tone mapping:
For simplicity, suggest
  No tone mapping for 26-tone RU
  Tone mapping with DTM = 3 for 52-tone RU for close-to-optimal performance and reusing existing design.
  Tone mapping with DTM = 6 for 106-tone RU.
RU (Tones) | Nss = 1 | Nss = 4 | Nss = 8
26 | +/-0.3dB | 0.4dB | 1dB
52 | +/-0.3dB | 1dB | 2dB
106 | <1dB | 2dB | 4dB

## Slide 24
(4) 484-tone RU, DTM
Segment parser is used for 11ac 160MHz, which can be reused here.
Alternative we can remove segment parser and define a new DTM for LDPC.
  Potential DTM = 2, 3, 4, 6, 9, 12, 13, 18, 26, 36, 39, 52, 78, 117, 156, 234.
Simulation assumptions
  A STA is assigned with a 484-tone RU.
  8000 bit per packet.
  D-NLOS (CP=0.8us), UMi-NLOS (CP=1.6us)
  Actual channel estimation, no other impairments.
  Simulated DTM = 13, 18, 26, 36, 39, 52, 78, 117 (without segment parser), and segment parser with DTM = 9 (11ac 160MHz).
  MCS 0, 2, 4, 7 and 9.

## Slide 25
D-NLOS
Segment parser has up to 2dB loss at MCS7-9  better to redefine DTM without segment parser.
DTM = 12 and 13 performs overall best for all MCS’s, although the gain is not significant.
  DTM = 12 is equivalent to Ncol = 39 (which is the best Ncol for 11ac 160MHz w/o segment parsing [3]).

## Slide 26
UMi-NLOS
DTM = 12 and 13 are very close and very marginally better than other options.

## Slide 27
(5) 996-tone RU, DTM
Potential DTM = 2, 4, 5, 7, 10, 14, 20, 28, 35, 49, 70, 98, 140, 196, 245, 490
Simulation assumptions
  A STA is assigned with a 996-tone RU.
  8000 bit per packet.
  D-NLOS (CP=0.8us), UMi-NLOS (CP=1.6us)
  Actual channel estimation, no other impairments.
  Simulated DTM = 10, 14, 20, 28, 35, 49, 70, 98 for MCS0, 2, 4, 7 and 9.

## Slide 28
D-NLOS
DTM = 20 performs best, and DTM=10/14 are marginally worse than DTM = 20.

## Slide 29
UMi-NLOS
Performance of DTM = 10~20 are almost the same, and marginally better than other DTM’s.

## Slide 30
Conclusions
RU (tones) | BCC |  | LDPC
 | Ncol | Nrot | DTM
26 | 8 | 2 (Nss≤4) | 1
52 | 16 | 11 (Nss≤4) | 3
106 | 17 | 29 (Nss≤4) | 6
242 | 26 | 58 (Nss≤4) | 9
484 |  |  | 12
996 |  |  | 20

## Slide 31
Straw Poll #1
Do you support the BCC interleaver and LDPC tone mapper parameters to be defined in the table?
RU (tones) | BCC |  | LDPC
 | Ncol | Nrot | DTM
26 | 8 | 2 | 1
52 | 16 | 11 | 3
106 | 17 | 29 | 6
242 | 26 | 58 | 9
484 |  |  | 12
996 |  |  | 20

## Slide 32
Appendix

## Slide 33
LDPC Tone Mapping as a Special Case of BCC Channel Interleaver
Tone
Intlv
Bit
Intlv
Tone
Rot
QAM
IFFT
Tone
Intlv
QAM
IFFT
BCC
LDPC
LDPC
QAM
IFFT
LDPC Tone
Mapper
W/ modified write sequence

## Slide 34
LDPC Tone Mapping as a Special Case of BCC Channel Interleaver
Excellent compromise
  Each implementation can choose to either
    Make use of existing BCC channel interleaver, or
    Use tone mapping in front of IFFT
  Nrow/Nbpscs = 4/6/9/9 for 20/40/80/160 MHz
    Large enough to satisfy in all cases
      20 MHz, Nss=8, 256-QAM 5/6: 3328 / 1944 = 1.7
      40 MHz, Nss=8, 256-QAM 5/6: 6912 / 1944 = 3.6
      80 MHz, Nss=8, 256-QAM 5/6: 14976 / 1944 = 7.7

## Slide 35: References
[1] 11-15-0132-06-00ax-spec-framework
[2] 11-15-0580-01-00ax-11ax-coding-discussion
    [3] 11-10-1063-01-00ac-160-mhz-tranmission-flow