## Slide 1: HE-SIG-B Structure
Date: 2015-07-11
Authors:
Name | Affiliation | Address | Phone | Email
Joonsuk Kim | Apple | 1 Infinite Loop Cupertino, CA 95014 USA | +1-408-862-3055 | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com

## Slide 2
Name | Affiliation | Address | Phone | Email
Yakun Sun | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | yakunsun@marvell.com
Hongyuan Zhang |  |  |  | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvell..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Authors (continued)

## Slide 3
Name | Affiliation | Address | Phone | Email
Peter Loc | Huawei |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Authors (continued)

## Slide 4
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Authors (continued)

## Slide 5
Authors (continued)
Name | Affiliation | Address | Phone | Email
Kiseon Ryu | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 6
Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 7
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Bo Sun | ZTE | #9 Wuxing duan, Xifeng Rd, Xi’an, China |  | Sub.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | Yao.ke5@zte.com.cn
Weimin Xing |  |  |  | Xing.weimin@zte.com.cn
Authors (continued)

## Slide 8: Discussion on HE-SIG B Structure
The current SFD [1] defines HE-SIG-B as follows:
  Downlink HE MU PPDU shall include HE-SIG-B field, and the number of OFDM symbols of HE-SIG-B field is variable.
    NOTE—The HE-SIG-B field includes information required to interpret HE MU PPDU, and detail is TBD.
  HE-SIG-B shall use a DFT period of 3.2 µs and subcarrier spacing of 312.5 kHz.
Background
  The structure of HE-SIG-B has to be defined with following details
    How to sort the contents in sequence
      Encoding sequence is discussed in another presentation [4]
    For wider bandwidth than 20MHz, how to arrange over frequency bands
    What information to be signaled
  In this presentation, we propose a HE-SIG-B structure

## Slide 9: Topic 1: Duplicate or Non-duplicate
HE SIG-A is proposed to have 2 OFDM symbol [2]
  HE SIG-A is duplicated over operating bandwidth, like 11n/ac
  HE SIG-B exists only for DL-MU
For MU, contents in HE SIG-A and HE SIG-B can be separated as follows:
  HE SIG-A can deliver the information about the PPDU to all STAs
    STAs do not know about the operating bandwidth yet; so better to be duplicated
  HE SIG-B sends the information for designated receiving STAs for MU operation
The remaining question is whether we have duplicated part in HE SIG-B if there is any
  We may not need another duplicated portion in HE SIG-B, given that HE SIG-A has 48~52 information bits
  Unless we are lack of number of bits in HE SIG-A to be fully duplicated, we do not need to duplicate any OFDM symbol of HE SIG-B over full bandwidth

## Slide 10: Topic 2: Common & User-specific
There are some information, which needs to be decoded by a group of STAs, as common information for DL-MU
  For example, Resource Unit (RU) allocation needs to be decoded, not by only one specific STA, but by a group of STAs
  A group includes TBD number of STAs. It can be all or a subset of designated receiving STAs.
  Those information may not be necessary for the other group of STAs when it is signaled for a subset of STAs
Common information for a group of receiving STAs can be signaled at once
  These information may need to be located up front in HE SIG-B, before user-specific information (MCS, Nsts etc. for each user)
  If the group is a subset of STAs, those information is better to be aligned with the designated group of receiving STAs, so that decoding error does not affect for other group of receiving STAs, in terms of sub-bands
    We can minimize the impact of OBSS interference, which may occupy some of sub-bands

## Slide 11: Common Field in SIG-B
The information for non-designated STAs to avoid the further un-necessary decoding process can be included in L-SIG & HE SIG-A
HE SIG-B includes control signaling for recipients of DL-MU PPDU
  The common field in HE SIG-B has the information which is needed for recipients in common
    E.g., RU allocation is common information to all or sub-set of recipients
  The user-specific field in HE SIG-B has the information for a specific user, which is not needed for other users

## Slide 12: User-specific Field in HE SIG-B
User-specific field consists of multiple sub-fields
Per-STA information, one specific subfield may deliver some information for a specific STA, which may not be useful for some other STAs
  i.e., Information is isolated between designated receiving STAs
  The boundary between common & user-specific field is in the bit-level, not OFDM symbol boundary
Common | User 1 | User 2 | … | User K
Common field
User-specific field
Information to be shared between users
No Information to be shared between users

## Slide 13: Logical Flow of Signals in HE SIG-B
Common | User specific
HE-STF | HE-LTF
20 MHz*
Information in SIG-B common field is shared between users within the same sub-band channel
  E.g., Resource Unit Allocation
Common/User specific signaling applies to the same sub-band channel
  In this way, signaling in corrupted sub-band channel does not affect on decoding the PPDU in another sub-band channel
  We can isolate the signaling to operate the OFDMA PPDU, so that partial interference does not corrupt the whole OFDMA PPDU reception
Common | User specific
HE-STF | HE-LTF
Logical Flow
20 MHz*
HE SIG-B
* 20MHz is an example
2nd sub-channel is corrupted due to OBSS
OFDMA Payload

## Slide 14: RU Allocation
In MU (OFDMA or MIMO (SDMA)) operation, there are many combinations of RUs per bandwidth. Possible RUs [3], depending on the size of operating bandwidth, are
  26, 52,106, 242, 484, 996 and 996 x 2 data tones
Receiving STAs need to know which RU needs to be decoded for themselves in HE SIG-B
These RU allocation mapping is better to be up front, at common field, in HE SIG-B, because
  Signaling for RU allocation for all receiving STAs can save the overhead, than individual signaling per STA, and
  Receiver can prepare for decoding accordingly with early identified RU structure
We propose to include RU allocation information in the common field of HE SIG-B
  How to signal RU allocation is TBD

## Slide 15: Summary
We propose the HE signal field structure as follows
  HE SIG-B does not have any OFDM symbol that is fully duplicated over the operating BW
    Some part of an OFDM symbol may be duplicated if necessary
  In HE SIG-B, which exists for DL-MU PPDU
    We need to signal the control information for designated receiving STAs
    For DL-MU, we need following information
      Resource allocation (OFDMA or MU-MIMO)
      Per-STA information, e.g.,
        STA-ID
        MCS
        Nsts
    We propose to have two fields in SIG-B
      Common field, where RU allocation info is included
      User-specific field, where per-STA info belongs to

## Slide 16: Straw poll #1
Do you agree to add to 11ax SFD that HE SIG-B does NOT have any OFDM symbol that carries the same information duplicated in each 20 MHz of the PPDU bandwidth?

## Slide 17: Straw poll #2
Do you agree to add to 11ax SFD that HE SIG-B has the common field followed by the user-specific field, where
  The common field includes the information for all of designated STAs to receive the PPDU in corresponding bandwidth
  The user-specific field consists of multiple sub-fields that do not belong to the common field, where one or multiple of those sub-fields are for each designated receiving STA
  The boundary between the common & the user-specific field is in the bit-level, not the OFDM symbol boundary

## Slide 18: Straw poll #3
Do you agree to add to 11ax SFD that the common field in HE SIG-B contains Resource Unit (RU) allocation?

## Slide 19: Reference
[1] 11-15-0132-06-00ax-spec-framework
[2] 11-15-0822-00-00ax-HE-SIG-A-Structure
[3] 11-15-0330-04-00ax-OFDMA-numerology-and-structure
[4] 11-15-0873-00-00ax-HE-SIG-B-encoding-structure