## Slide 1: Broadcast and Unicast (Trigger) in DL MU
Date: 2015-07-12
Authors:
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Hongyuan Zhang |  |  |  | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Bo Yu |  |  |  | jiehuang@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Andrew Blanksby |  |  |  | 
Matthias Korb |  |  |  | 
Tu Nguyen |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com

## Slide 6: Authors (continued)
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Name | Affiliation | Address | Phone | Email
Hyeyoung Choi | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | hy0117.choi@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 8: Introduction
The following text was included in 11ax SFD [1]
  An UL MU PPDU (MU-MIMO or OFDMA) is sent as an immediate response (IFS TBD) to a Trigger frame (format TBD) sent by the AP
  The amendment shall define a mechanism for multiplexing DL acknowledgments sent in response to UL MU Transmissions
In [2], Trigger frame is defined as MAC frame which is separately transmitted.
It is not clear whether broadcast/multicast frames are allowed in DL MU.
In this presentation we defines
  trigger frame transmitted in DL MU.
  broadcast/multicast frames in DL MU

## Slide 9: Trigger Frame Format in [2]
Trigger information is carried in a control frame which carries the trigger info:
  A new control/extension frame type
    Structure similar to exiting NDPA
  As for any MAC frame, it can be sent in any PHY mode (unless special restrictions are defined)
    11a for legacy compatibility/NAV, HE for outdoor, etc…
  TA = BSSID
  RA = Broadcast if more than one STA Info field is present

## Slide 10: Possible DL/UL OFDMA Frame Exchange
A TXOP may include DL OFDMA and UL OFDMA
  DL OFDMA and UL OFDMA may have different STAs.
  DL OFDMA may include UL resource allocation information.
AP A-MPDU to STA2
BlkAck
BlkAck
BlkAck
DL OFDMA
STA3 A-MPDU to AP
STA2 A-MPDU to AP
STA1 A-MPDU to AP
OFDMA Ack/BA or M-BA
Example of OFDMA Frame Exchange
AP A-MPDU to STA3
AP A-MPDU to STA1
BlkAck
BlkAck
BlkAck
UL OFDMA

## Slide 11: Possible DL/UL OFDMA Frame Exchange
AP A-MPDU to STA2
A Trigger frame in A-MPDU which is transmitted to a single receiver can be used to trigger UL OFDMA/MU-MIMO frame exchange (UL data OFDMA PPDU + DL acknowledge) or UL OFDMA acknowledge from a STA.
TBD IFS after the end of PPDU which carries Trigger, STAs transmit UL OFDMA/MU-MIMO frames.
After receiving UL MU PPDU, the AP acknowledges the received frames by using broadcast acknowledge or OFDMA acknowledge.
BlkAck
BlkAck
BlkAck
DL A-MPDU
Trigger
Trigger
Trigger
STA3 A-MPDU to AP
STA2 A-MPDU to AP
STA1 A-MPDU to AP
OFDMA or broadcast acknowledge
Example of OFDMA Frame Exchange
AP A-MPDU to STA3
AP A-MPDU to STA1
BlkAck
BlkAck
BlkAck
UL A-MPDU

## Slide 12: Combined multicast and unicast transmissions
Multicast frames and unicast frames can be multiplexed together in OFDMA format:
  Provides high efficiency for both multicast and unicast transmissions.
  Reduce the delay of unicast transmission caused by multicast transmissions.

## Slide 13: Broadcast Trigger in DL OFDMA
When a subchannel in DL OFDMA PPDU is used to broadcast Trigger to multiple STAs, UL OFDMA PPDU and DL OFDMA PPDU can have different STAs as the transmitters/receivers.
Unicast Trigger in A-MPDU with data frames has the same receiver as the data frames.
Broadcast Trigger only in a PPDU can be received by multiple STAs.
  The broadcast trigger includes the resource allocation information of the STAs which are not identified by the partial AIDs of the other subchannels of the DL OFDMA.
    With this, a STA doesn’t need to decode two subchanels of DL OFDMA.
TBD IFS after the end of PPDU which carries Trigger, STAs transmit UL OFDMA/MU-MIMO frames.
After receiving UL MU PPDU, the AP acknowledges the received frames by using broadcast acknowledge or OFDMA acknowledge.
AP A-MPDU to STA2
BlkAck
BlkAck
DL A-MPDU
Trigger
Trigger
Trigger
STA3 A-MPDU to AP
STA2 A-MPDU to AP
STA1 A-MPDU to AP
OFDMA or broadcast acknowledge
OFDMA Frame Exchange
AP A-MPDU to STA3
AP A-MPDU to STA1
BlkAck
BlkAck
BlkAck
UL A-MPDU
Trigger
Trigger
AP A-MPDU to STA4
STA5 A-MPDU to AP
STA4 A-MPDU to AP
BlkAck
STA6 A-MPDU to AP
BlkAck
BlkAck
BlkAck
BlkAck

## Slide 14: References
[1] 802.11-15/0132-04-00ax-spec-framework
[2] 802.11-15/0877r0 Trigger Frame Format

## Slide 15: Straw Poll 1
Do you agree to add the following to the SFD?
Unicast trigger frame for a single user may be included within an AMPDU for that user within the DL MU PPDU that precedes the UL MU transmission by TBD IFS.

## Slide 16: Straw Poll 2
Do you agree to add the following to the SFD:
Broadcast trigger transmitted in a subchannel of DL OFDMA shall not include the resource allocation information of the STAs which are recipients of frames in the other subchannels of the DL OFDMA:
  the subchannel of the broadcast trigger frame is identified by TBD signaling.
  the DL OFDMA precedes the UL OFDMA transmission by TBD IFS.