## Slide 1
Calibration Results for PSP and U-APSD for 20MHz, 40MHz and 80 MHz band
Date: 2015-07-07
Authors:
Name | Affiliations | Address | Phone | Email
Dmitry Akhmetov | Intel | 2111 NE 25th AVE, Hillsboro, OR, 97123 | +1-503-264-8081 | dmitry.akhmetov@intel.com
Ghosh Chittabrata | Intel | 2200 Mission College Blvd., Santa Clara, CA, 95054 | +1-415-244-8904 | chittabrata.ghosh@intel.com
Jeonghoon Park | Intel | 2200 Mission College Blvd., Santa Clara, CA, 95054 |  | 

## Slide 2: Abstract
The Simulations Scenario document [1] described 3 existing power save mechanisms in 802.11-2012 as baseline for energy efficiency evaluation in scenarios for TGax
  Power save mode (PSM)
  Power save polling (PSP)
  Unscheduled automatic power save delivery (U-APSD)
In [4] we provided initial power save calibration test results for
  PSP
  U-APSD
This contribution provides extra power save calibration test results for PSP and U-APSD in 40MHz and 80MHz band and comparison with 20MHz presented in [4]

## Slide 3: Various Power States Definition
Power State | Average Current Consumption [mA], 20MHz | Average Current Consumption [mA], 40MHz | Average Current Consumption [mA], 80MHz
Transmit [mA] | 280 | 280 | 280
Receive [mA] | 100 | 140 | 200
Listen [mA] | 50 | 60 | 75
Shallow Sleep [mA] | 0.9 | 0.9 | 0.9
Deep Sleep [mA] | 0.003 | 0.003 | 0.003
Deep Sleep [2] power state is defined as a sleep state with the least (non-zero) power consumed and the longest transition time to Listen state.
Shallow Sleep [2] power state is defined as a sleep state when the STA consumes more power but transitions faster to Listen state when compared to the Deep Sleep power state
Simulation results in this contribution use Shallow Sleep power state as Sleep state
Simulation Scenarios document [1] of IEEE 802.11ax specifies the following common power model parameters for all simulation scenarios

## Slide 4: Common simulation parameters
Simulation Scenarios document [1] of IEEE 802.11ax specifies the following common simulation parameters for all simulation scenarios
Parameters | 
RTS/CTS | OFF
AIFS=DIFS | 34us
Control rate/Data rate for 20/40/80MHz | 6 Mbps/ 6.5Mbps/13.5Mbps/29.3Mbps
MCS | 0
A-MPDU aggregation | No
Simulation time | 300s
BI (PSP only) | 102.4ms
DTIM (PSP only) | 3
Beacon size | 80 bytes
Data frame size (PSP only) | 1500 bytes
Data frame size (U-APSD only) | 120 bytes

## Slide 5: PSP Test
The MSDU 1500 bytes DL traffic transmitted every 200ms
  Beacon transmitted using PIFS
  Regular contention for PS-Poll & DATA
  STA wakes at TBTT boundary
  PS-Poll triggers AP to TX in DL
  STA enter SLEEP after it received DATA with more_frag bit set to zero

## Slide 6: Calibration Test Results for PSP
PSP-Time, % per power state |  |  |  |  |  |  |  |  | 
 |  | Power Save Enabled |  |  |  | Active |  |  | 
 |  | Listen | RX | TX | Sleep | Listen | RX | TX | Sleep
STA | 20MHz | 0.094 | 1.027 | 0.040 | 98.782 | 98.823 | 1.124 | 0.020 | 0.000
 | 40MHz | 0.094 | 0.539 | 0.040 | 99.270 | 99.311 | 0.636 | 0.020 | 0.000
 | 80MHz | 0.094 | 0.296 | 0.040 | 99.513 | 99.555 | 0.392 | 0.020 | 0.000
AP | 20MHz | 98.801 | 0.040 | 1.136 | 0.000 | 98.856 | 0.020 | 1.124 | 0.000
 | 40MHz | 99.288 | 0.040 | 0.649 | 0.000 | 99.344 | 0.020 | 0.636 | 0.000
 | 80MHz | 99.532 | 0.040 | 0.405 | 0.000 | 99.588 | 0.020 | 0.392 | 0.000
PSP-Energy, % per power state |  |  |  |  |  |  |  |  | 
 |  | Power Save Enabled |  |  |  | Active |  |  | 
 |  | Listen | RX | TX | Sleep | Listen | RX | TX | Sleep
STA | 20MHz | 3.974 | 86.464 | 9.313 | 0.249 | 97.668 | 2.222 | 0.111 | 0.000
 | 40MHz | 6.121 | 81.603 | 11.954 | 0.322 | 98.437 | 1.471 | 0.093 | 0.000
 | 80MHz | 9.130 | 76.220 | 14.265 | 0.385 | 98.888 | 1.038 | 0.074 | 0.000
AP | 20MHz | 93.878 | 0.075 | 6.047 | 0.000 | 93.978 | 0.038 | 5.984 | 0.000
 | 40MHz | 96.954 | 0.090 | 2.956 | 0.000 | 97.055 | 0.046 | 2.899 | 0.000
 | 80MHz | 98.401 | 0.104 | 1.494 | 0.000 | 98.500 | 0.053 | 1.447 | 0.000

## Slide 7: U-APDS Test
Bidirectional traffic, MSDU 120 bytes every 40ms
  AP buffer DL traffic while STA is in SLEEP
  STA wakes at UL frame arrival from LLC
  Regular contention for each DATA TX
  STA enter sleep after
    it receive DATA with more_frag bit set to zero
    STA TX buffer is empty

## Slide 8: Calibration Test Results for U-APSD
UAPSD-Time, % per power state |  |  |  |  |  |  |  |  | 
 |  | Power Save Enabled |  |  |  | Active |  |  | 
 |  | Listen | RX | TX | Sleep | Listen | RX | TX | Sleep
STA | 20MHz | 0.837 | 0.650 | 0.650 | 97.850 | 98.700 | 0.650 | 0.650 | 0.000
 | 40MHz | 0.837 | 0.410 | 0.410 | 98.330 | 99.180 | 0.410 | 0.410 | 0.000
 | 80MHz | 0.837 | 0.300 | 0.300 | 98.550 | 99.400 | 0.300 | 0.300 | 0.000
AP | 20MHz | 98.687 | 0.650 | 0.650 | 0.000 | 98.700 | 0.650 | 0.650 | 0.000
 | 40MHz | 99.167 | 0.410 | 0.410 | 0.000 | 99.180 | 0.410 | 0.410 | 0.000
 | 80MHz | 99.387 | 0.300 | 0.300 | 0.000 | 99.400 | 0.300 | 0.300 | 0.000
UAPSD-Energy, % per power state |  |  |  |  |  |  |  |  | 
 |  | Power Save Enabled |  |  |  | Active |  |  | 
 |  | Listen | RX | TX | Sleep | Listen | RX | TX | Sleep
STA | 20MHz | 11.108 | 17.244 | 48.282 | 23.366 | 95.234 | 1.254 | 3.512 | 0.000
 | 40MHz | 16.159 | 18.459 | 36.918 | 28.463 | 97.188 | 0.937 | 1.875 | 0.000
 | 80MHz | 21.254 | 20.303 | 28.425 | 30.017 | 98.105 | 0.790 | 1.105 | 0.000
AP | 20MHz | 95.234 | 1.254 | 3.512 | 0.000 | 95.234 | 1.254 | 3.512 | 0.000
 | 40MHz | 97.188 | 0.937 | 1.875 | 0.000 | 97.188 | 0.937 | 1.875 | 0.000
 | 80MHz | 98.105 | 0.790 | 1.105 | 0.000 | 98.105 | 0.790 | 1.105 | 0.000

## Slide 9: Per state total time comparison 20MHz vs 40MHz vs 80MHz
PSP, Total time per state difference |  |  |  |  | 
 |  | Listen | RX | TX | Sleep
 |  | % diff | % diff | % diff | % diff
STA | 20MHz | 0.00 | 0.00 | 0.00 | 0.00
 | 40MHz | 0.00 | -47.48 | 0.00 | 0.49
 | 80MHz | 0.00 | -71.23 | 0.00 | 0.74
AP | 20MHz | 0.00 | 0.00 | 0.00 | N/A
 | 40MHz | 0.49 | 0.00 | -42.91 | N/A
 | 80MHz | 0.74 | 0.00 | -64.37 | N/A
UAPSD, Total time per state difference |  |  |  |  | 
 |  | Listen | RX | TX | Sleep
 |  | % diff | % diff | % diff | % diff
STA | 20MHz | 0.00 | 0.00 | 0.00 | 0.00
 | 40MHz | 0.00 | -36.92 | -36.92 | 0.49
 | 80MHz | 0.00 | -53.85 | -53.85 | 0.72
AP | 20MHz | 0.00 | 0.00 | 0.00 | N/A
 | 40MHz | 0.49 | -36.92 | -36.92 | N/A
 | 80MHz | 0.71 | -53.85 | -53.85 | N/A
20MHz is taken as 100% for comparison

## Slide 10: Conclusion
In this submission we have provided
  Additional power save calibration test results for 40Mhz and 80Mhz configuration
  We propose to include table from slide 3 to include into Simulation Scenarios Document
Straw poll:
  Do you agree to include table from slide 3 into Simulation Scenarios Document?

## Slide 11: References
[1] S. Merlin et. al., “TGax Simulation Scenarios,” IEEE 11-14-980r6, Jan 2015
[2] C. Ghosh et. al., “Sleep states in-IEEE 802.11ax Simulation Scenarios,” IEEE 11-15-314r2, March 2015
[3] C. Ghosh et. al., “Power Consumption and Latency Values in State Transitions for IEEE 802.11ax Simulation Scenarios,” IEEE 11-15-0576r0, May 2015
[4] D. Akhmetov et. al., “Calibration results for PSP and UAPSD”, IEEE 11-15-0603r0, May 2015