## Slide 1: Cascading Structure
Date: 2015-07-12
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei Technologies | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Wookbong Lee | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | wookbong.lee@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Laurent cariou | Orange |  |  | Laurent.cariou@orange.com
Thomas Derham |  |  |  | thomas.derham@orange.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Tu Nguyen |  |  |  | 
Vinko Erceg |  |  |  | 
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Lei Wang |  |  |  | yakunsun@marvell.com
Jinjing Jiang |  |  |  | Leileiw@marvell.com
Hongyuan Zhang |  |  |  | liwenchu@marvell.com
Yakun Sun |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Jie Huang |  |  |  | jiehuang@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 6
Name | Affiliation | Address | Phone | Email
Simone Merlin | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Santosh Abraham |  | 5775 Morehouse Dr. San Diego, CA, USA |  | sabraham@qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Cherian Gorge |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 1700 Technology Drive San Jose, CA 95110, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 5775 Morehouse Dr. San Diego, CA, USA |  | caldana@qca.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Tevfik Yucek |  | 5775 Morehouse Dr. San Diego, CA, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Authors (continues):

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Joonsuk Kim | Apple | Cupertino, CA | +1-408-974-5967 | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 9: Introduction
DL MU transmission has been defined in 802.11ac
The rules for DL and UL MU transmissions are defined in 11ax SFD [1]
  An UL MU PPDU (MU-MIMO or OFDMA) is sent as an immediate response (IFS TBD) to a Trigger frame (format TBD) sent by the AP
  The amendment shall define a mechanism for multiplexing DL acknowledgments sent in response to UL MU Transmissions
  The amendment shall include a mechanism to multiplex BA/ACK responses to DL MU transmission
In this presentation we define a cascading structure for the frame exchange in DL MU PPDU followed by UL MU PPDU

## Slide 10: Cascading
Cascading is a simple extension to current frame exchange
  The most frequent frame exchange is Data/ACK
  ACK and Data can be aggregated in A-MPDU
  UL MU provides another dimension to multiplex UL ACK and UL data
  So does DL MU
Cascading is DL MU PPDU followed by UL MU PPDU, which can multiplex any type of frames for fast frame exchange
Data
ACK
t
Data
ACK Data
t
Data
Data
t
ACK

## Slide 11: Trigger & Cascading
To support cascading, trigger frame has to be transmitted in DL MU PPDU to trigger the following UL MU PPDU
The definition of trigger frame is:
  The Trigger frame is a MAC frame that includes sufficient information to identify the stations transmitting the UL MU PPDUs and allocating resources for the UL MU PPDUs.
In cascading, trigger frame for the following UL MU PPDU can be
  sent in a dedicated subchannel as a standalone frame to trigger one or multiple STAs that are not in the set of DL MU users (broadcast trigger) or
  sent by aggregating with other MPDU(s) to re-allocate resources for the receiver to send its UL frame in the following UL MU PPDU
DL MU PPDU
UL MU PPDU
t
Preamble

## Slide 12: MU ACK/BA & Cascading
MU ACK/BA can be transmitted in the format of unicast frame in MU PPDU or a broadcast frame for multiple STAs (Multi-STA BA) in DL SU/MU transmission
In cascading, unicast ACK/BA can be multiplexed with other frames in DL MU PPDU or UL MU PPDU
  in frequency domain, or
  in spatial domain
Multi-STA BA can also be multiplexed with other frames in DL MU PPDU
  in frequency domain

## Slide 13: Example of Cascading
Cascading includes the following typical examples:
  Data in DL MU PPDU and its acknowledgement in the following UL MU PPDU
  Trigger in DL MU PPDU and its triggered frames in the following UL MU PPDU
An example of Data/ACK exchange w/o and w/ cascading structure
  w/o cascading
  w/ cascading
Preamble
DL Data (STA 1)
DL Data (STA 2)
DL Data (STA 3)
t
Preamble
UL BA (STA1)
UL BA (STA2)
UL Data
(STA 4)
UL BA (STA3)
Preamble
DL BA (STA 4)
DL Data (STA5)
DL Data (STA6)
…
BAR
Trigger
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
Preamble
DL Data (STA 1)
DL Data (STA 2)
DL Data (STA 3)
t
Preamble
UL BA (STA 1)
UL BA (STA 2)
UL Data (STA 4)
UL BA (STA 3)
Preamble
DL BA (STA 4)
DL Data (STA 5)
DL Data (STA 6)
…
SIFS
SIFS
Trigger (STA 4)

## Slide 14: Multiple Cascading Structures
As shown in the previous pages, cascading structure can be repeated multiple times in a TXOP
DL MU PPDU
UL MU PPDU
t
DL MU BA
DL MU PPDU
UL MU PPDU
…
TXOP

## Slide 15: Flexibility of Cascading Structure
Cascading structure helps to sufficiently utilize the parallel subchannels for simultaneous transmission
  Any types of transmissions (i.e., data frame/control frame/management frame) can be supported by cascading structure
  Frame exchanges are sped up, e.g., accelerates almost any management/control frame exchanges

## Slide 16: Summary of Cascading
As a summary, cascading can be defined as follows:
  a TXOP structure, allowing a sequence of DL MU PPDU followed in the same TXOP by a separate UL MU PPDU, the sequence repeated 0 or more times
    The TXOP sequence has only one DL transmitter
    The TXOP sequence may have different UL transmitters within each UL MU PPDU
    The TXOP sequence may have a different set of transmitters in an UL MU PPDU as compared to the DL MU PPDU that follows the UL MU PPDU within the same TXOP

## Slide 17: Reference
[1] 11-15-0132-06-00ax-spec-framework

## Slide 18: Straw Poll 1
Do you support to add the following to the SFD:
  A TXOP can include both DL MU and UL MU transmissions.

## Slide 19: Straw Poll 2
Do you support to add the following to the SFD:
  The spec shall include the definition of a cascading TXOP structure, allowing a sequence of DL MU PPDU followed in the same TXOP by a separate UL MU PPDU, the sequence repeated 0 or more times
    The TXOP sequence has only one DL transmitter
    The TXOP sequence may have different UL transmitters within each UL MU PPDU
    The TXOP sequence may have a different set of transmitters in an UL MU PPDU as compared to the DL MU PPDU that follows the UL MU PPDU within the same TXOP

## Slide 20: Straw Poll 3
Do you support to add the following to the SFD:
  DL/UL OFDMA can multiplex different type of unicast frames in frequency domain
    Type of frame can be data frame/control frame/management frame
    Different type of frames are to/from different users

## Slide 21: Straw Poll 4
Do you support to add the following to the SFD:
  DL/UL MU-MIMO can multiplex different type of unicast frames in spatial domain
    Type of frame can be data frame/control frame/management frame
    Different type of frames are to/from different users