## Slide 1
Simulation Results for Box5 Calibration
Date: 2015-07-12
Authors:

## Slide 2: Abstract
During IEEE 802.11 May meeting, the agreement on Box5 detail simulation parameters was presented in [1].
Based on the agreed simulation conditions, we provide two sets of test results from the Box5 test cases:
  Results of max 64 MPDU per A-MPDU to be presented in the contribution;
  Results of max 32 MPDU per A-MPDU was combined into the joint-contribution 11-15/0802
Comparison of results with those of partners [2] shows good alignment

## Slide 3: PHY Parameters

## Slide 4: MAC Parameters
MAC parameters | 
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=3 ]
Queue length | A single queue for each traffic link is set inside AP/STA sized of 2000 packets
Traffic type | UDP CBR with rate 10^8bps Random start time during a 10ms interval
MPDU size | 1544 Bytes (1472 Data + 28 IP header + 8 LLC header + 30 MAC header + 4 delimiter + 2 padding)
Aggregation | [A-MPDU / max aggregation size / BA window size, No A-MSDU, immediate BA without explicit request], Max aggregation: 32 or 64 MPDUs
Max number of retries | 10
Beacon | Disabled
RTS/CTS | OFF
Running time | 200s per drop, 30 drops per data
Output metric | -CDF or Histogram of per non-AP STA throughput (received bits/overall simulation time) -PER of all AP/STA (1 - # of success subframes / # of transmitted subframes)

## Slide 5: 11ac Scenario 6 – OBSS Enterprise
AP A | (0,0)
AP B | (40,20)
AP C | (-40,-20)
STA3 | (7.5+xb, ‑9.5+yb)
STA9 | (7+xb, -7.5+yb)
STA15 | (3+xb, -0.5+yb)
STA21 | (-6.5+xb, -3+yb)
STA27 | (‑6+xb, 2.5+yb)
STA6 | (-5.5+xc,4.5+yc)
STA12 | (7+xc,7+yc)
STA18 | (10+xc,0.5+yc)
STA24 | (3+xc,2.5+yc)
STA30 | (9.5+xc,3.5+yc)
STA1 | (5,-9.5)
STA2 | (3.5,7.5)
STA4 | (-4.5,0.5)
STA5 | (-1.5,6)
STA7 | (-9,-5)
STA8 | (-8.5,8.5)
STA10 | (-3,0.5)
STA11 | (-0.5,8)
STA13 | (-4,-4)
STA14 | (7.5,-1)
STA16 | (8,-6)
STA17 | (0,-7.5)
STA19 | (-2.5,-4.5)
STA20 | (0.5,-2)
STA22 | (0,-4.5)
STA23 | (-1.5,7)
STA25 | (3.5,-5)
STA26 | (9,9.5)
STA28 | (-8,-5.5)
STA29 | (1.5,3.5)
Fixed Location and Association

## Slide 6: 11ac SS6 Traffic Flow Model
DL/UL traffic assigned for each STA
STA | DL | UL | STA | DL | UL
STA1 | y | y | STA23 | n | y
STA2 | y | y | STA25 | y | y
STA4 | y | y | STA26 | y | y
STA5 | y | y | STA28 | y | y
STA7 | y | y | STA29 | y | y
STA8 | y | y | STA3 | y | y
STA10 | y | n | STA9 | y | n
STA11 | y | n | STA15 | y | n
STA13 | y | n | STA21 | n | y
STA14 | y | n | STA27 | y | y
STA16 | y | n | STA6 | y | y
STA17 | y | n | STA12 | y | n
STA19 | y | n | STA18 | y | n
STA20 | y | n | STA24 | n | y
STA22 | n | y | STA30 | y | y
“y” means having DL/UL traffic flow; “no” means not having DL/UL traffic flow

## Slide 7: Test Cases for Step-by-Step Calibration of 11ac SS6
1 BSS (upper-right corner BSS B)
  DL only case
  UL only case
    1 STA: each STA-AP
    2 STAs: 3+9, 3+15, 3+27
    3 STAs: 3+9+15, 3+9+27
  DL & UL case
2 BSS (A+B)
  Both DL only
  Both UL only
  A DL and B UL
  B UL and A DL
3 BSS
  DL only
  UL only
  Mixed DL & UL

## Slide 8: Single BSS Simulation Results (max 64 MPDU per A-MPDU)
 | STA#3 |  | STA#9 |  | STA#15 |  | STA#21 |  | STA#27 |  | Sum (Mbps)
 | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | 
DL | 41.12 | 0.00 | 42.03 | 0.00 | 41.16 | 0.00 | 42.05 | 0.00 | 42.03 | 0.00 | 208.39
UL - One STA Only | 99.97 | 0.00 |  |  |  |  |  |  |  |  | 99.97
 |  |  | 99.98 | 0.00 |  |  |  |  |  |  | 99.98
 |  |  |  |  | 99.78 | 0.00 |  |  |  |  | 99.78
 |  |  |  |  |  |  | 97.94 | 0.00 |  |  | 97.94
 |  |  |  |  |  |  |  |  | 99.78 | 0.00 | 99.78
UL - Two STA | 98.64 | 0.10 | 97.38 | 0.11 |  |  |  |  |  |  | 196.02
 | 98.75 | 0.10 |  |  | 97.65 | 0.10 |  |  |  |  | 196.40
 | 98.80 | 0.10 |  |  |  |  |  |  | 97.34 | 0.11 | 196.14
UL - 3 STA | 60.00 | 0.17 | 60.63 | 0.17 | 60.19 | 0.17 |  |  |  |  | 180.82
 | 65.71 | 0.17 | 62.83 | 0.17 |  |  |  |  | 60.23 | 0.18 | 188.77

## Slide 9: 2 BSS (A+B) Simulation Results DL-Only (Max.64 MPDU)
Chart: Throughput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 3.8015 | 5.421 | 5.5914 | 5.8565 | 5.7369 | 5.0447 | 5.4455 | 5.4581 | 5.8885 | 5.3023 | 5.5832 | 5.7196 | 4.6846 | 4.5872 | 4.8941 | 4.259 | 5.3694 | 4.9026 | 5.7243 | 5.6633 | 20.3859 | 20.7335 | 20.5534 | 18.4745 | 20.9635
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.0865 | 0.1037 | 0.0355 | 0.0794 | 0.0555 | 0.0684 | 0.027 | 0.0736 | 0.0222 | 0.087 | 0.0865 | 0.0614 | 0.0418 | 0.0129 | 0.0301 | 0.0503 | 0.0452 | 0.0867 | 0.0398 | 0.0404 | 0.0923 | 0.0772 | 0.026 | 0.0679 | 0.0688

## Slide 10: 2 BSS (A+B) Simulation Results UL-Only(Max.64 MPDU)
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.3919 | 0.3491 | 0.5313 | 0.4292 | 0.4887 | 0.3895 | 0.3818 | 0.3904 | 0.3798 | 0.3912 | 0.4248 | 0.3933 | 0.4424 | 0.3869 | 0.3604 | 0.3561 | 0.4554 | 0.3368 | 0.3022 | 0.3876 | 0.6012 | 0.2856 | 0.2421 | 0.2866 | 0.2482
Chart: Throughput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 6.1882 | 6.8789 | 3.8044 | 6.6454 | 3.5044 | 3.3981 | 4.7517 | 6.4258 | 5.3567 | 6.9773 | 5.8586 | 6.4745 | 4.6294 | 7.8107 | 3.9047 | 6.4658 | 5.3331 | 8.1168 | 10.6558 | 5.8202 | 1.3138 | 5.8505 | 9.3517 | 14.8746 | 10.3731

## Slide 11: 2 BSS (A+B) Simulation Results A-DL / B – UL (Max.64 MPDU)
Chart: Throughput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 1.2537 | 1.72 | 1.5215 | 1.0782 | 1.4753 | 1.8849 | 1.0654 | 1.8312 | 1.2789 | 1.5862 | 1.8033 | 1.871 | 1.5434 | 1.8143 | 1.6213 | 0.8611 | 1.3842 | 1.8825 | 1.7835 | 1.5273 | 27.066 | 30.306 | 30.9663 | 36.2375 | 26.267
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.0974 | 0.1157 | 0.0026 | 0.044 | 0.0594 | 0.1245 | 0.0297 | 0.0969 | 0.0007 | 0.1513 | 0.1055 | 0.0628 | 0.0124 | 0.0298 | 0.0366 | 0.1147 | 0.0566 | 0.1751 | 0.0249 | 0.0774 | 0.2805 | 0.2504 | 0.2388 | 0.2206 | 0.285

## Slide 12: 2 BSS (A+B) Simulation Results A-UL / B - DL(Max.64 MPDU)
Chart: Throughput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 9.7156 | 5.9542 | 4.5627 | 5.8725 | 9.3237 | 11.9791 | 4.6926 | 8.4824 | 6.8449 | 8.2375 | 6.7346 | 10.1448 | 5.5517 | 5.0129 | 7.5777 | 7.7979 | 6.5398 | 9.187 | 6.8897 | 6.0149 | 2.1431 | 1.9439 | 1.7984 | 1.6403 | 2.2348
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.2962 | 0.3849 | 0.4934 | 0.3913 | 0.2912 | 0.2679 | 0.4603 | 0.3374 | 0.4036 | 0.3429 | 0.3428 | 0.3338 | 0.4164 | 0.4479 | 0.3871 | 0.3611 | 0.4017 | 0.3078 | 0.3809 | 0.4102 | 0.1004 | 0.1535 | 0.0224 | 0.1239 | 0.1564

## Slide 13: 3 BSS DL-Only Simulation Results (Max.64 MPDU)
Chart: Throughput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 2.5567 | 2.7754 | 2.2783 | 3.0028 | 2.4571 | 2.6398 | 2.4233 | 2.4337 | 2.7537 | 2.9554 | 2.8232 | 2.9336 | 1.7775 | 2.654 | 2.913 | 2.7131 | 2.7669 | 2.8147 | 15.7863 | 18.3877 | 17.3374 | 18.2098 | 24.5447 | 24.4214 | 21.2226 | 20.4709
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 0.0887 | 0.0662 | 0.0654 | 0.0615 | 0.0961 | 0.1043 | 0.0204 | 0.1178 | 0.0628 | 0.0852 | 0.1478 | 0.0938 | 0.0306 | 0.0271 | 0.0758 | 0.1135 | 0.1041 | 0.0407 | 0.0454 | 0.085 | 0.0261 | 0.0461 | 0.0217 | 0.0592 | 0.0474 | 0.0545

## Slide 14: 3 BSS UL-Only Simulation Results (Max.64 MPDU)
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 0.487 | 0.3297 | 0.3263 | 0.4209 | 0.4797 | 0.3707 | 0.3799 | 0.3698 | 0.3634 | 0.3963 | 0.3515 | 0.4018 | 0.4748 | 0.1773 | 0.1805 | 0.1513 | 0.5126 | 0.1991
Chart: Throughput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 2.5692 | 5.2225 | 9.3174 | 5.5864 | 4.3532 | 6.8856 | 10.4201 | 6.4995 | 1.9538 | 2.327 | 4.96 | 6.1681 | 13.0057 | 41.3708 | 37.3064 | 56.0041 | 6.7443 | 32.8282

## Slide 15: Box5 Test Cases Results Comparison Max.32 vs. Max.64 MPDU Aggregation
Chart: 
| 1Bss-DL | 1Bss-UL-2STAs | 1Bss-UL-3STAs | 2Bss DL-Only | 2Bss UL-Only | 2Bss A-DL/B-UL | 2Bss A-UL/B-DL | 3Bss DL-Only | 3Bss UL-Only
Max.32 MPDU Aggregation | 195.76 | 186.89 | 181.16 | 195.7746 | 153.8699 | 178.4951 | 149.6149 | 196.6513 | 219.9514
Max.64 MPDU Aggregation | 208.39 | 196.02 | 184.82 | 206.445 | 160.7642 | 181.63 | 156.8767 | 208.053 | 253.5223

## Slide 16: Conclusion
Box5 Calibration results (11-15/0802) show good alignment on the condition of Max.32 MPDU aggregation.
However, due to obvious performance gap by MPDU aggregation, Max.64 MPDU aggregation is recommended as default condition for next Box5 calibration.

## Slide 17: Reference
[1] 11-15/0680r2 Reference Box5 Calibration Assumptions and Parameters
[2] 11-15/0802r0 Box5 Calibration Result of SS6

## Slide 18: Backup - Intel Results of max 32 MPDU per A-MPDU

## Slide 19: Single BSS Simulation Results (max 32 MPDU per A-MPDU)
 | STA#3 |  | STA#9 |  | STA#15 |  | STA#21 |  | STA#27 |  | Sum (Mbps)
 | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | 
DL | 39.73 | 0.00 | 38.61 | 0.00 | 39.13 | 0.00 | 38.02 | 0.00 | 40.28 | 0.00 | 195.76
UL - One STA Only | 99.78 | 0.00 |  |  |  |  |  |  |  |  | 99.78
 |  |  | 99.78 | 0.00 |  |  |  |  |  |  | 99.78
 |  |  |  |  | 99.77 | 0.00 |  |  |  |  | 99.77
 |  |  |  |  |  |  | 98.03 | 0.00 |  |  | 98.03
 |  |  |  |  |  |  |  |  | 99.77 | 0.00 | 99.77
UL - Two STA | 93.77 | 0.11 | 93.12 | 0.11 |  |  |  |  |  |  | 186.89
 | 93.13 | 0.11 |  |  | 95.62 | 0.09 |  |  |  |  | 188.75
 | 93.63 | 0.11 |  |  |  |  |  |  | 93.35 | 0.11 | 186.98

## Slide 20: Single BSS Simulation Results (cont.) (max 32 MPDU per A-MPDU)
 | STA#3 |  | STA#9 |  | STA#15 |  | STA#21 |  | STA#27 |  | Sum (Mbps)
 | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | 
UL - 3 STA | 60.46 | 0.17 | 59.23 | 0.17 | 61.47 | 0.16 |  |  |  |  | 181.16
 | 54.62 | 0.17 | 63.26 | 0.17 |  |  |  |  | 63.21 | 0.16 | 181.09

## Slide 21: 2 BSS (A+B) Simulation Results DL-Only (Max.32 MPDU)
Chart: Thoughtput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 4.3654 | 4.728 | 5.0249 | 5.0181 | 5.7784 | 5.0286 | 5.5498 | 4.9123 | 5.2162 | 5.5084 | 4.1471 | 5.4269 | 5.9561 | 5.0966 | 4.6475 | 3.8906 | 4.1763 | 4.4948 | 4.3701 | 4.9613 | 19.2428 | 19.9425 | 18.6107 | 19.3507 | 20.3305
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.0709 | 0.0963 | 0.0322 | 0.0679 | 0.0455 | 0.0899 | 0.0153 | 0.0888 | 0.0174 | 0.0912 | 0.0852 | 0.0676 | 0.039 | 0.0223 | 0.0483 | 0.0714 | 0.0687 | 0.1075 | 0.0609 | 0.0479 | 0.0883 | 0.0627 | 0.0168 | 0.0923 | 0.0953

## Slide 22: 2 BSS (A+B) Simulation Results UL-Only(Max.32 MPDU)
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.3924 | 0.3914 | 0.4437 | 0.4357 | 0.4491 | 0.4047 | 0.3883 | 0.368 | 0.4367 | 0.3877 | 0.3727 | 0.4187 | 0.4339 | 0.4426 | 0.4043 | 0.4161 | 0.3885 | 0.3529 | 0.4198 | 0.3668 | 0.5351 | 0.4348 | 0.2134 | 0.2704 | 0.2795
Chart: Thoughtput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 6.7485 | 6.4227 | 2.8557 | 3.8862 | 2.9077 | 4.641 | 6.5025 | 6.4279 | 4.6724 | 5.2735 | 6.5685 | 5.9308 | 4.072 | 5.0862 | 6.1547 | 5.1601 | 7.0662 | 7.8132 | 4.7314 | 7.7273 | 2.6258 | 4.4643 | 16.0388 | 16.7342 | 13.3583

## Slide 23: 2 BSS (A+B) Simulation Results A-DL / B – UL (Max.32 MPDU)
Chart: Thoughtput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 2.6575 | 2.4434 | 2.3155 | 2.2555 | 2.1297 | 1.7233 | 2.2135 | 2.0597 | 1.9291 | 2.1241 | 1.8077 | 1.9219 | 2.3655 | 2.3789 | 2.2776 | 2.3806 | 2.8449 | 2.1012 | 2.0025 | 2.2224 | 25.0768 | 24.3469 | 28.7782 | 32.1669 | 23.9718
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.113 | 0.0962 | 0.0139 | 0.076 | 0.038 | 0.0781 | 0.0124 | 0.0977 | 0.0135 | 0.1125 | 0.1113 | 0.0595 | 0.0109 | 0.0027 | 0.0092 | 0.0892 | 0.0714 | 0.1818 | 0.038 | 0.0837 | 0.2778 | 0.2812 | 0.2392 | 0.2205 | 0.2702

## Slide 24: 2 BSS (A+B) Simulation Results A-UL / B - DL(Max.32 MPDU)
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.3529 | 0.3772 | 0.4092 | 0.4354 | 0.4269 | 0.4096 | 0.4125 | 0.3867 | 0.4275 | 0.4389 | 0.3609 | 0.3522 | 0.4165 | 0.464 | 0.4102 | 0.3981 | 0.4099 | 0.3776 | 0.4241 | 0.4676 | 0.1529 | 0.1729 | 0.0257 | 0.2806 | 0.1128
Chart: Thoughtput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 8.6849 | 8.3079 | 7.1105 | 5.8768 | 6.3024 | 6.8015 | 6.377 | 7.5445 | 6.3234 | 5.3432 | 8.8186 | 7.5343 | 7.1357 | 5.0529 | 6.4172 | 7.8613 | 5.7698 | 8.1308 | 6.0904 | 5.1276 | 2.5213 | 2.0636 | 3.9354 | 2.5253 | 1.9546

## Slide 25: 3 BSS DL-Only Simulation Results (Max.32 MPDU)
Chart: Thoughtput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 3.3176 | 3.3856 | 3.5366 | 2.9365 | 2.5657 | 3.6503 | 3.4515 | 3.505 | 3.5554 | 3.5554 | 3.0132 | 3.2708 | 3.6273 | 3.1524 | 3.4996 | 2.2911 | 3.1105 | 3.2816 | 14.576 | 19.3549 | 19.2546 | 19.1336 | 18.5144 | 15.418 | 14.5838 | 17.1099
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 0.1023 | 0.1029 | 0.0686 | 0.0709 | 0.079 | 0.1381 | 0.0166 | 0.1096 | 0.0638 | 0.1198 | 0.0779 | 0.0783 | 0.0753 | 0.0246 | 0.1005 | 0.1032 | 0.0722 | 0.0501 | 0.0491 | 0.0744 | 0.0216 | 0.0799 | 0.0415 | 0.0577 | 0.1067 | 0.0847

## Slide 26: 3 BSS UL-Only Simulation Results (Max.32 MPDU)
Chart: Thoughtput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 7.3638 | 4.5858 | 8.4145 | 9.717 | 3.0691 | 5.8898 | 5.2393 | 6.9682 | 7.5678 | 4.1387 | 5.7887 | 7.8612 | 22.3888 | 18.0633 | 30.6298 | 41.1647 | 6.4727 | 24.6282
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 0.3896 | 0.4037 | 0.4437 | 0.357 | 0.5387 | 0.3557 | 0.4262 | 0.4866 | 0.4583 | 0.4435 | 0.4874 | 0.3769 | 0.364 | 0.2992 | 0.2155 | 0.2224 | 0.643 | 0.2587