## Slide 1: HE Trigger Frame Format
Date: 2015-07-13
Authors:

## Slide 2: Introduction
TGax adopted UL MU sequence as follows [1]
  An UL MU PPDU (MU-MIMO or OFDMA) is sent as an immediate response (IFS TBD) to a Trigger frame (format TBD) sent by the AP. [MAC Motion #3, March 2015]
Trigger frame format should be chosen under the following criteria
  Signaling Overhead (amount of airtime it consumes)
  Robust Decoding of Trigger frame (under OBSS interferences or Outdoor environment)
  Protection of UL MU Data reception (against AP-side hidden nodes)
  Protection of DL M-STA BA reception (against STA-side hidden nodes)

## Slide 3: Introduction
Possible HE Trigger Frame Formats
  NDP(Null Data Packet) format: DL MU related signaling design (SIG-A/B) is reused for UL MU signaling (Trigger) as well
  MAC frame format: define a new control frame type called Trigger, can be sent with any PPDU format
Assumptions in this slide
  Additional RTS-CTS negotiations before Trigger frame may be defined in 11ax, but not considered in this slide.
  Legacy(11a/n/ac) STAs will treat HE PPDU as non-HT PPDU.
  L-SIG’s L_LENGTH/L_RATE fields is used to indicate HE PPDU length. (similar to 11ac design)
  HE PPDU can be decoded by STAs in outdoor environments.
DL
Trigger
(format TBD)
UL
MU Data
SIFS
xIFS
OBSS Interferences
Signaling Overhead
DL
M-STA
BA
M-STA BA Max duration
Protection of UL MU Data reception
Protection of DL M-STA BA reception (upto possible max duration)
20/40/80/160
MHz

## Slide 4: Option 1. NDP Trigger frame
Trigger frame is sent as HE NDP format
  HE-SIG-A/B contains UL MU resource allocation information for UL STAs
  If TXOP duration info is contained in SIG-A/B, it can secure TXOP of further sequences from HE STAs
Signaling Overhead
  Very low with L-Preamble & HE-SIG-A/B only
Robust Decoding of Trigger Frame
  Robust decoding from outdoor STAs
  Decoding under secondary channels’ OBSS interferences depends on SIG-B design [2]
Protection of UL MU Data reception
  If TXOP duration is in SIG-A/B, AP-side HE hidden node(H1) can set NAV
  AP-side Legacy hidden node(L1) may interfere to UL MU Data reception at AP
Protection of DL M-STA BA reception
  If TXOP duration is in SIG-A/B, STA-side HE hidden node(H2) can set NAV
  STA-side Legacy hidden node(L2) may interfere to DL M-STA BA reception at UL STA
L-Preamble
Dup.
L-Preamble
UL
MU Data
HE-
Preamble
(64&256FFT)
L-Preamble
Dup.
L-Preamble
XIFS
SIFS
STA
L2
M-STA BA Max duration
H2
DL
M-STA
BA
H2
HE STA
L2
Leg STA
EIFS
H1
HE STA
L1
Leg STA
L-SIG (Trigger)
HE-
Preamble
(64FFT)
(Trigger Info)
OBSS Interferences
AP-side
hidden nodes
STA-side
hidden nodes
HE Preamble Duration ? (UL MU Data)
L-SIG Length (UL MU Data)
AP
40MHz
AP-side hidden nodes
Legacy
HE
Legacy
HE
HE Preamble Duration ? (Trigger)
EIFS
STA-side hidden nodes
NAV setting
collision
L1
H1
STA

## Slide 5: Option 2. MAC Trigger frame (11ax PPDU)
L-Preamble
HE-
Preamble
(64&256FFT)
L-Preamble
UL
MU Data
HE-
Preamble
(64&256FFT)
L-Preamble
L-Preamble
40MHz
XIFS
SIFS
H2
HE STA
L2
Leg STA
L-SIG Length (UL OFDMA)
EIFS
MPDU
(Trigger Info)
OBSS Interferences
H1
HE STA
L1
Leg STA
L-SIG Length (UL OFDMA)
DIFS (EIFS?)
M-STA BA Max duration
DL
M-STA
BA
EIFS
L-SIG Length (Trigger)
Trigger frame is sent as MAC frame in 11ax PPDU format
  MPDU contains UL MU information (field details are TBD)
Signaling Overhead
  Low, can be sent using wide channels and/or high MCS
Robust Decoding of Trigger Frame
  Robust decoding from outdoor STAs
  May not be decodable under secondary channels’ OBSS interferences (dependent on Trigger’s MPDU design)
Protection of UL MU Data reception
  AP-side HE hidden node(H1) can set NAV using MAC Duration field in Trigger
  AP-side Legacy hidden node(L1) may interfere to UL MU Data reception at AP
Protection of DL M-STA BA reception
  STA-side HE hidden node(H2) may not decode MAC Duration field in UL MU Data, thus may interfere to DL M-STA BA reception
  STA-side Legacy hidden node(L2) may interfere to DL M-STA BA reception at UL STA
MAC Duration (Trigger)
AP-side hidden nodes
STA-side hidden nodes
NAV setting
collision

## Slide 6: Option 2. MAC Trigger frame (11a PPDU)
L-Preamble
Dup.
L-Preamble
Dup. MPDU
(Trigger Info)
MPDU
(Trigger Info)
UL MU Data
HE-
Preamble
L-Preamble
Dup.
L-Preamble
XIFS
SIFS
M-STA BA Max duration
M-STA
BA
OBSS Interferences
H2
HE STA
L2
Leg STA
L-SIG Length (UL OFDMA)
MAC Duration (Trigger)
EIFS
H1
HE STA
L1
Leg STA
MAC Duration (Trigger)
L-SIG Length (UL OFDMA)
DIFS (EIFS?)
Trigger frame is sent as MAC frame in 11a PPDU format (non-HT duplicate)
  MPDU contains UL MU information (field details are TBD)
Signaling Overhead
  Low to Middle, no HE-Preamble but MPDU is duplicated per 20MHz
Robust Decoding of Trigger Frame
  May not be decodable from outdoor STAs
  Robust decoding under secondary channels’ OBSS interferences
Protection of UL OFDMA Data reception
  AP-side HE hidden node(H1) & legacy hidden node(L1) can set NAV using MAC Duration field in Trigger
Protection of DL M-STA BA reception
  STA-side HE hidden node(H2) may not decode MAC Duration field in UL MU Data, thus may interfere to DL M-STA BA reception
  STA-side Legacy hidden node(L2) may interfere to DL M-STA BA reception at UL STA
40MHz
AP-side hidden nodes
STA-side hidden nodes
NAV setting

## Slide 7: Trigger Frame Type Comparisons
NDP Trigger frame
  Very low overhead, Robust decoding in outdoor
  Robustness under secondary channels’ interferences and NAV protection for HE/Legacy STAs are very much dependent on SIG-A/B design
  Thus may act as the limiting factors for designing SIG-A/B
MAC Trigger frame
  Has flexibility to choose PPDU format
  11ax PPDU: Low overhead, Robust decoding in outdoor
  11a PPDU: Robust decoding under secondary channels’ interferences, NAV protection for HE/Legacy STAs
Performance Index \ Trigger Format |  | Opt. 1. NDP format | Opt. 2. MAC format | 
 |  |  | sent as 11ax PPDU | sent as 11a PPDU
Trigger Frame Overhead (airtime) |  | Very Low | Low | Low~Mid
Robust Decoding of Trigger Frame | under OBSS interferences @2nd CHs | (dep. on SIG-B design) | X | O
 | under outdoor environments | O | O | X
UL MU Data Protection at AP | against HE hidden nodes | (dep. on SIG-A/B design) | O | O
 | against legacy hidden nodes | X | X | O
DL M-STA BA Protection at UL STAs | against HE hidden nodes | (dep. on SIG-A/B design) | X | X
 | against legacy hidden nodes | X | X | X

## Slide 8: Summary
We propose to choose MAC frame format as the HE Trigger frame format.
  Flexibility to choose PPDU types for different purposes
  Pursue independent & optimal design for SIG-A/B(DL MU) and Trigger(UL MU) respectively
  Among three MAC frame types (Data, Management, and Control), Trigger can be assigned as a new control frame type.
Remaining DL M-STA BA Protection Issues
  Legacy hidden nodes: If DL M-STA BA’s duration exceeds EIFS, it cannot be protected [3]
  HE hidden nodes: UL MU Data’s MPDU may not be decodable by overhearing HE STAs, therefore MAC duration-based protection is not feasible

## Slide 9: Straw poll - 1
  Do you agree to add the following text into 11ax SFD ?
  3.2.z HE Trigger frame shall be defined as a new MAC control frame.
  Y
  N
  A

## Slide 10: References
[1] 15/0132r4 Spec framework
[2] 15/0621r2 Design Principles for HE Preamble
[3] 15/0626r1 Further Considerations on Multi-STA Block Ack