## Slide 1: Extensible Preamble Format Design
Date: 2015-09-13
Authors:

## Slide 2: Summary
Every time there is a new amendment requiring a new PHY preamble format, we always run into the problem of how to do the autodetection against all previous PHY preamble formats.
We propose to create a new preamble format that is efficient and straightforward extensible for future PHY amendments.
There have been a few proposals for the preamble format and its autodetection but they’re extensibility is either uncertain or inefficient [1,2].

## Slide 3: Proposal- Develop an extensible new preamble format
START
STEP 1:
New Format?
11ac Autodetection
Step 2:
11ax and future format detection
N
Y
Step 1: Isolate the New Preamble Format
Step 2: Define an extensible encoding for 11ax
and future extensions

## Slide 4: Step 1: Isolating the new preamble format
BPSK
BPSK
BPSK
1. By using BPSK in the 2 symbols after L-SIG, we quickly narrow down the option to
  11ax+
  Legacy with BPSK modulated data
To rule out Legacy with BPSK, several approaches can be made [1-2].
  CRC check
  Service Field Check
  Additional QBPSK symbol at the end of HE-SIG2
  Special patterns in HE-SIG1 (Repeated L-SIG, Signatures)
HE-SIG2
HE-SIG1
L-STF
L-LTF
L-SIG
TBD

## Slide 5: Step 2: Define an extensible format to separate 11ax+ preamble formats
HE-SIG2
HE-SIG1
L-STF
L-LTF
L-SIG
BPSK
BPSK
BPSK
TBD
TBD (actual 11ax-SIG bits)
11ax indicator
1
Note: 11bx, 11cx, etc. are future extensions
TBD (actual 11bx-SIG bits)
0
1
11bx indicator
TBD (actual 11cx-SIG bits)
0
0
11cx indicator
1
Propose a Prefix code for encoding the format

## Slide 6: Benefits of Proposed Step 2
With Step 1, 11ax devices can readily distinguish its packet from 11ac and earlier packet formats. However with Step 2, it can also distinguish itself from future extensions.
Step 2 can either serve as an additional check for detecting 11ax preambles or a built in spoofing method that can be used by future ammendments.
3. Once the received frame is judged to be of the new format, detections of the future extensions have
Accuracy - Equal to the BER of the L-SIG (or HE-SIG). This already has very good accuracy due to the Viterbi decoder.
Extensibility- Only one bit overhead for 11ax. Additional bit per future extension.
4. By using a prefix code based encoding, we don’t need to allot any bits for extensions that doesn’t exist yet.

## Slide 7: Updates for r2
1. Proposed Method applied to RLSIG method
2. Simulation Results
3. Other discussions

## Slide 8: Proposed Method applied to RLSIG preamble
SIGA
L-STF
L-LTF
L-SIG
TBD
RL-SIG
Advantages
When all 11ax devices set this bit to 1, future devices using the same detection circuit will easily know that the packet is 11ax
Future devices can set 11ax reserved bit to 0 to avoid false detection by 11ax devices.
11ax Reserved Bit | Value
1 | If FORMAT==HE
0 | otherwise

## Slide 9: Autodetection Method
START
L-SIG, RL-SIG repetition
Legacy
detection
Y
11ax Decode Procedure
N
LSIG Content Check
N
Y
11ax Reserved Bit==1?
Future Standard
Procedure
Y
N
Compare hamming
distance (HD) with
threshold

## Slide 10: Simulation Conditions
20MHz Bandwidth
1x1 antennas
Channel D NLOS
Real timing estimation, CFO, phase tracking
RL-SIG repetition detection
  Hamming Distance threshold = [8,12,16,20]

## Slide 11: False Detect Performance (11a)
RLSIG only
RLSIG + 11ax Reserved Bit check
Even against legacy devices, exactly 50% less false detect errors can be achieved)
50% Less errors

## Slide 12: False Detect Performance against Future devices
If a future standard set the 11ax Reserved bit to zero, 11ax False Detection will improve with SNR regardless of the HD threshold.
No high SNR errors

## Slide 13: Missdetect performance
Some degradation at very high thresholds. But very high thresholds result in high false detect and hence must be avoided anyway.
RLSIG only
RLSIG + 11ax Reserved Bit check

## Slide 14: Other discussions
On Future extensibility
- With the 11ax reserved bit, future WLANs will have the option to reuse 11ax autodetection circuit with the same performance.
On the 11ax Reserved Bit Indicator
- Based on our simulation, one bit is enough for the false detection error to track the LSIG PER curve (slide 12).

## Slide 15: References
[1] 11-15/0579, “Preamble design and auto-detection,” Hongyuan Zhang (Marvell)
[2] 15/0081, “Considerations on 11ax Auto-detection Methods,” Jaeyoung Song (KAIST)