## Slide 1: Consideration on Evaluation Methodology for 11ay
Date: 2015-07-DD
Authors:

## Slide 2: Introduction
This contribution suggest to consider the followings in 11ay Evaluation Methodology
  MIMO capability per device for MIMO simulation scenarios
  Mixture of 11ad and 11ay devices for channel bonding simulation scenarios

## Slide 3: Proposal 1. MIMO capability per device for MIMO simulation scenarios
Motivations
  Devices have different MIMO capability since they have different number of array antennas according to their form factors, services, and etc.
  It would emulate more realistic environments if we consider different MIMO capability per device in simulations, which, however, may provide simulation complexity
Proposal: Specify MIMO capability in Evaluation Methodology
  MIMO capability is the maximum number of array antennas that can be supported by a device
  Option 1. Set MIMO capability differently per device in Evaluation Methodology
    E.g. Set MIMO capability to four for TV/projector/monitor, and to two for mobile device/laptop/wearable devices
  Option 2. Set MIMO capability equally per device
    E.g. Set MIMO capability to four (or two) for all devices

## Slide 4: Proposal 2. Mixture of 11ad and 11ay devices for channel bonding simulation scenarios
Motivation
  It is required to see if 11ad and 11ay system coexist and fairly operate together.
  More specifically,11ay can operate in channel bonding, but, 11ad can not.
  So, the performance may be different according to the ratio of 11ay and 11ad devices especially in channel bonding
Proposal: Specify whether each device is 11ad or 11ay in Evaluation Methodology
  Especially for channel bonding simulation scenarios
  Or specify the portion of 11ad and 11ay, e.g. x% of 11ay, (100-x)% of 11ad

## Slide 5: Summary
We propose the following to be included in Evaluation Methodology:
  MIMO capability per device for MIMO simulation scenarios
  Mixture of 11ad and 11ay devices for channel bonding simulation scenarios

## Slide 6: Strawpoll 1
Which option do you prefer to specify MIMO capability per device in 11ay Evaluation Methodology?
  Option 1. Set MIMO capability differently per device
  Option 2. Set MIMO capability equally per device

## Slide 7: Strawpoll 2
Do you agree to specify whether each device is 11ad or 11ay in Evaluation Methodology?
  Y/N/A