## Slide 1: 802.11ax in 2.4 GHz
Date: 2015-07-06
Authors:

## Slide 2: Abstract
Recently more 802.11 devices capable of operating in 2.4 GHz & 5 GHz than devices supporting 2.4 GHz only have been shipped. However, the majority of BSSs still operate in 2.4 GHz and 5 GHz usage lacks behind.
  Although 2.4 GHz band is often referred to as “junk band,” it plays a vital role for 802.11. Also because the 2.4 GHz spectrum has a lower free space path loss than 5 GHz, the 2.4 GHz spectrum should not be given up.
  802.11ac addresses the 5 GHz only, but the industry’s interest in “backporting” features to 2.4 GHz outlines the importance of the latter spectrum.
  802.11ax will address both 802.11 bands and thus the 2.4 GHz band should not be ignored.
It has been shown that 802.11’s Basic Service Set (BSS) management works robust but inefficient. A lot of airtime (up to 58% = 90% × 64%, see [2]) is wasted with management frame traffic.
  We propose a simple addition to the 802.11ax Specification Framework Document (SFD) that has been highlighted by others before.

## Slide 3: 2.4 GHz channel assignment
802.11 default channel bandwidth is 20 MHz
5 MHz channel number increments
  Few non-overlapping channels (1, 6, 11)
  Some regulatory domains have extra channels (13, 14)
[3] reports about random channel assignment
  Many operators not aware of channel overlap
  Dissimilar channel numbers treated as indicator for dissimilar frequency channels

## Slide 4: Probe request frame transmissions
Many devices send probe frames on every channel available in 2.4 GHz (1 … 11 resp. 13)
  With DSSS, probes can be easily received when off one or two channels
    See [1-3]
  Huge amount of probe response frames
    APs on- and off-channel respond
    Probing device receives the same responses multiple times when “walking” through all 2.4 GHz channels

## Slide 5: HE STAs and 2.4 GHz channels
With OFDMA 802.11ax introduces a new paradigm
  Physical & virtual carrier sensing important to align with OBSS
  Avoid partially overlapping channels
HE operation (even if mixed with legacy modes) should ban the use of non-orthogonal channels
In the 2.4 GHz band, HE APs shall not operate on channels other than 1, 6, and 11
Non-AP HE STAs shall probe on channels 1, 6, and 11 before probing on any other channel in 2.4 GHz

## Slide 6: Straw Poll

## Slide 7: Straw Poll
Do you agree to add the following to the IEEE 802.11 TGax Specification Framework?
  Add to the end of Clause 6 (MAC): “The amendment shall define that HE APs shall not operate on channels other than 1, 6, and 11 in the 2.4 GHz band. Non-AP HE STAs shall probe on channels 1, 6, and 11 before probing on any other channel in 2.4 GHz.”

## Slide 8: Straw Poll (if previous unsuccessful)
Do you agree to add the following to the IEEE 802.11 TGax Specification Framework?
  Add to the end of Clause 6 (MAC): “The amendment shall define that HE APs should not operate on channels other than 1, 6, and 11 in the 2.4 GHz band. Non-AP HE STAs shall probe on channels 1, 6, and 11 before probing on any other channel in 2.4 GHz.”

## Slide 9: Motion
Transform successful straw poll into a motion

## Slide 10: Motion
Moved to add to the end of Clause 6 (MAC) of the IEEE 802.11 TGax Specification Framework:
  “The amendment shall define that HE APs shall/should not operate on channels other than 1, 6, and 11 in the 2.4 GHz band. Non-AP HE STAs shall probe on channels 1, 6, and 11 before probing on any other channel in 2.4 GHz.”
  Moved by:
  Seconded:

## Slide 11: References
B. Hart, “Renewing 2.4 GHz,” 11-13/1397
K. Yunoki et al., “Understanding Current Situation of Public Wi-Fi Usage - Possible Requirements for HEW,” 11-13/523
V.-P. Ketonen, “WLAN QoE, End User Perspective Opportunities to Improve,” 11-13/545