## Slide 1: 802.11ai & 802.11ax
Date: 2015-07-06
Authors:

## Slide 2: Abstract
802.11ax will introduce “improvement in the average throughput per station […] in a dense deployment scenario”
  In dense deployments, management traffic becomes a severe issue
  Several submissions revealed a high amount probe frame traffic
  802.11ai provides means to reduce probe frame traffic
We propose to adopt 802.11ai with 802.11ax

## Slide 3: Probe frame traffic
Many submissions to SG HEW and TGax identify excessive probe frame traffic
  See [1]
  Probe frame traffic can be severe airtime killer
Today, way more probe traffic than assumed in 802.11-1999
OFDMA, UL MU-MIMO etc. make medium usage more efficient, but don’t solve airtime waste
  Efficiency gains do not compensate for loss in airtime

## Slide 4: Probe frame sniffing
Fast Initial Link Setup (FILS) tackles several probe storm related problems
  Probe frames contain publicly available information
  However, with current implementations devices independently ask for information
  Multitude of probe frame request/response transmissions
802.11ai [2] allows for overhearing other stations’ probe responses
  Prevent stations from transmitting probe frames
  Uses information that is anyway on the wireless medium

## Slide 5: FILS discovery frames
802.11 default beacon transmission interval is 102.4 ms
Passive scanning requires stations to wait for beacon reception
  Can be time consuming with many channels
Most implementations use active scanning
  Station sends out probe request frame to learn about neighborhood
  Can clog the wireless medium
FILS discovery frames are much shorter than beacon frames
  Consume much less airtime
  Always transmitted at data rates ≥6 Mb/s
Default FILS discovery frame repetition rate is 20.48 ms
  Passive scanning becomes attractive
FILS discovery frames can substantially reduce the use of active scanning
  Less probe frames

## Slide 6: Straw Poll

## Slide 7: Straw Poll 1
Do you agree to add the following to the IEEE 802.11 TGax Specification Framework?
  Add to the end of Clause 6 (MAC): “The amendment shall define a HE STA to be a FILS STA.”

## Slide 8: Motion
Transform successful straw poll into a motion

## Slide 9: Motion
Moved to add to the end of Clause 6 (MAC) of the IEEE 802.11 TGax Specification Framework:
  “The amendment shall define a HE STA to be a FILS STA.”
  Moved by:
  Seconded:

## Slide 10: References
K. Yunoki et al., “Understanding Current Situation of Public Wi-Fi Usage - Possible Requirements for HEW,” 11-13/523
IEEE 802.11, “IEEE P802.11ai/D5.0,” June 2015