## Slide 1
Issues on Trigger Frame Retransmission
Date: 2015-07-12
Authors:

## Slide 2: Introduction
UL-OFDMA and UL-MU-MIMO are key enabling technologies to enhance the performance in dense environment in 11ax
Trigger Frame was adopted in SFD to initiate UL-OFDMA transmission[1]
The acknowledgement of Trigger Frame was discussed in the last meeting[2]
  UL MPDU/A-MPDU could be the acknowledgement of the trigger frame

## Slide 3: Trigger Frame based UL-OFDMA procedure
Trigger frame could be transmitted with contention based access scheme (similar to RTS frame)
UL PPDU could be the acknowledgement of trigger frame
M-BA is the acknowledgement of UL PPDUs
Conventional EDCA procedure follows UL OFDMA transmission

## Slide 4: Trigger Frame based UL-OFDMA procedure
Access Category(AC) of Trigger frame should be defined
  To determine Trigger Frame’s AIFS, CW, etc.
  Not only fixed values but also variable values could be considered
Absence of some or all UL PPDUs after Trigger Frame might mean a failure of trigger frame exchange
  At least, absence of all UL PPDUs after trigger frame means a failure of trigger frame exchange
  What is the next procedure of the trigger frame failure?

## Slide 5: Retransmission of Trigger Frame
Conventional retransmission of trigger frame
  Due to large retransmission delay, original UL OFDMA scheduling might be invalid
    UL STA could transmit its PPDU before TF retransmission
    Channel availability could be changed

## Slide 6: Retransmission of Trigger Frame
Conventional retransmission of trigger frame
  Trigger frame retransmission with conventional contention based retransmission could degrade 11ax system performance due to invalidity of UL OFDMA scheduling
We need to consider other type of retransmission procedure in case of trigger frame failure
  Criteria for retransmission
  Contention based retransmission or not
  Behavior of AP after retransmission failure

## Slide 7: Retransmission of Trigger Frame
Fast retransmission of Trigger Frame
  AP retransmits its trigger frame after sensing absence of UL-PPDU(s)
    If AP cannot detect UL OFDMA PPDU and the channel is idle, AP immediately retransmit its trigger frame
    Retransmission number or duration might be limited

## Slide 8: Retransmission of Trigger Frame
Fast retransmission of Trigger Frame
  In fast retransmission scheme, conventional retransmission scheme on trigger frame is not allowed
  Fast retransmission could sustain its reliability on UL OFDMA scheduling
  Original TXOP is not accessible in conventional 802.11 system
    AP get TXOP only if Downlink PPDU transmission and cannot detect collision
    Therefore, fast retransmission may not cause severe interferences than conventional 802.11

## Slide 9: Fast retransmission failure
Initial CW for next frame
  AP could transmit a next frame after fast retransmission failure
  The next frame could be a new trigger frame or DL data frame(s)
  Initial CW is applied to next frame because CW doubling is applied only on retransmission in conventional 802.11 system

## Slide 10: Fast retransmission failure
Doubled CW for next frame
  Although conventional retransmission rule is not applied to trigger frame, trigger frame failure could be considered as congestion situation
  To avoid congestion, CW doubling could be applied upon trigger frame failure
  Doubled CW is applied to the next frame

## Slide 11: Conclusion
We need to discuss access category parameters of trigger frame
Next procedure of trigger frame failure need to be defined
Conventional retransmission has some problems(issues) on trigger frame
Fast retransmission could be considered instead of conventional retransmission

## Slide 12: Straw Poll
Do you agree with trigger frame is not allowed to follow conventional retransmission procedure?
    Y
    N
    A

## Slide 13: References
[1] IEEE 802.11-15/0132r4 "Specification Framework for TGax"
[2] IEEE 802.11-15/0615r1 “UL OFDMA Bandwidth"