## Slide 1: Scheduled Trigger frames
Date: 2015-07-04
Authors:

## Slide 2
Authors (continued):

## Slide 3
Authors (continued)

## Slide 4
Authors (continued)

## Slide 5
Authors (continued)

## Slide 6
Authors (continued)

## Slide 7
Authors (continued)

## Slide 8: Introduction
MU procedures are under discussion in 11ax
  The AP enables multiple STAs to transmit UL frames via Trigger frames (TFs)
  MU STAs wait for the TF prior to transmitting UL frames
    Upon reception of a TF intended to them they can transmit to the AP
In this presentation we focus on trigger frame scheduling with TWT signaling [1]
  This way we also enable other useful operation modes for power save that fit in the 11ax use cases
    I.e., STAs wake up only in the allocated TWT SP and can sleep outside of them
For simplicity, we focus on the implicit TWT operation which enables:
  “Broadcast” TWT: Scheduled by the AP, irrespective of TWT requests, and indicated in the Beacon for multiple STAs (a generic scheduling mechanism that covers operation in [1])
  “Solicited” TWT: Scheduled by the AP, accounting for the STA’s TWT request

## Slide 9: Basics of Trigger TWTs
“Broadcast” trigger TWT:
  AP indicates the target trigger times in a TWT response included in the Beacon
    The pattern can be periodic, aperiodic (i.e., single indication for multiple Trigger frames)
      The pattern is only valid for the Beacon Interval following the Beacon.
    The AP can indicate the broadcast trigger TWTs during a TWT Setup
“Solicited” trigger TWT:
  A STA requests the AP to schedule TFs (using TWT request)
    TWT pattern is based on STA’s UL traffic pattern and QoS requirements
      The pattern can be periodic or aperiodic
  The AP responds confirming or providing alternative TWT schedules
    The AP allocates its resources based on multiple STA’s information
      STAs with similar traffic pattern can be allocated in similar TWTs, with similar TWT service periods (SPs), and other similar parameters
Beacon
TF
Next TWT
Beacon
TF
TF
TF
TWT element: Implicit TWT, Next TWT, TWT Wake Interval
TWT Wake Interval
DL/ULMU
DL/ULMU
DL/ULMU
DL/ULMU

## Slide 10: Solicited Trigger TWT
Trigger TWT setup (negotiated):
  Setup of TWT parameters is the same as for basic TWT operation with the following additions:
    The HE non-AP STA may request scheduling of a TF at the start of each TWT
    The AP confirms scheduling of a TF at the start of each TWT
Trigger TWT operation:
  AP schedules a TF at the beginning of each TWT SP
  Non-AP STAs wake up at the TWT, wait for the TF and get ready for MU DL/UL exchange
    STAs are not supposed to contend during the TWT SP but rather wait for the TFs sent by the AP
    During the TWT SP, STAs can exchange PS-Polls, APSD trigger frames, UL/DL BUs, etc. upon reception of TFs.
STAs that negotiate TWT need not wake up to read the Beacon frame
  DL BU availability is notified during the TWT SP itself.
  STAs can renegotiate their TWTs when a traffic pattern changes
STA 1
STA 2
Poll 4
Poll 2
Trigger
Poll 1
STA 4
TWT Wake Interval
TWT SP
Next TWT(s)
TWT Setup(s)
Ack
Trigger
BU 1
BU 2
BU 4
BA 1
BA 2
BA 4

## Slide 11: Broadcast Trigger TWT
TWT setup for broadcast trigger TWT
  TWT request/response can be exchanged by a STA and an AP to negotiate the target Beacon frame monitored by the PS STA.
  Example of operation
    A STA sends a TWT Request to request the broadcast trigger TWT operation.
    An AP sends a TWT Response including the Target Wake Time set to the target TBTT and TWT Wake Interval set to the ListenInterval of the STA.
    A STA monitors the Beacon frame with the period of TWT Wake Interval (ListenInterval) from the time of Target Wake Time (target TBTT).
    If a STA receives the target trigger times in a TWT response included in the Beacon, the STA may save its power till the time and the STA wakes up at the target trigger time to receive the Trigger frame.
    Otherwise, the STA save its power according to TWT Wake Interval.
  Note. It is applicable to PS STAs which should monitor the TIM Beacon frame with certain periodicity.

## Slide 12: Benefits of TWTs
TWT scheduling improves power saving for the SU case as exemplified in [1]
  It also eases contention as the STAs should not access the medium outside the TWT SPs
For the MU case, the STA indicates/negotiates with the AP:
  The TWT SPs during which it is active and the rest of the times during which it is inactive
    Similar benefits to the SU case: STAs save power, eases channel contention,
  To send TFs at the start of the TWT SPs
    Enables MU operation during the TWT SP and protects the medium access for the STA
      Increases throughput as transmissions are protected at the receiver
      Increases network efficiency due to MU transmissions and reducing collisions
The AP uses the TWT scheduling to:
  Spread out the wake up and access times of the STAs easing contention
  Allocate MU resources more efficiently (as it can be based on received feedback)
    Avoids allocating resources to STAs with no UL data

## Slide 13: TWT element
Define a Triggered subfield in the Request Type field of the TWT element:
  Set to 1 in a TWT Request to request for a TF at the start of the TWT
  Set to 1 in a TWT Response to indicate that a TF will be scheduled at the start of the TWT
Most of the use cases for 11ax seem to be covered by implicit TWT setup
  So suggestion is that for 11ax the Implicit field of the TWT element be set to 1
    Some more evaluations are needed to understand the benefits of explicit TWT
      Which requires the use of TACK/STACK/BAT frames
  Hence, here we focus only on the implicit TWT
 | B0 | B1 B3 | B4 | B5 | B6 | B7 B9 | B10 B14 | B15
 | TWT Request | TWT Setup Command | Reserved Triggered | Implicit | Flow Type | TWT Flow Identifier | Wake Interval Exponent | TWT Protection
Bits: | 1 | 3 | 1 | 1 | 1 | 3 | 5 | 1
 | Element ID | Length | Control | Request Type | Target Wake Time | TWT Group Assignment | Nominal Minimum Wake Duration | TWT Wake Interval Mantissa | TWT Channel | NDP Paging (optional)
Octets: | 1 | 1 | 1 | 2 | 8 or 0 | 9 or 3 or 0 | 1 | 2 | 1 | 0 or 4

## Slide 14: Summary of Trigger TWT
Define implicit TWT operation for 11ax that enables:
  Solicited TWT:
    STA and the AP negotiate the TWT parameters
      STA sends TWT request and AP responds with a TWT response
  Broadcast TWT:
    AP indicates to STAs the TWT parameters
      AP sends TWT response to the STAs without receiving TWT requests
The proposed Trigger TWT procedure
  Inherits the power saving properties of the TWT protocol [1]

## Slide 15: Straw Poll #1
Do you support to add the following text in the SFD:
  The spec shall include a mechanism that allows a target transmission time for a Trigger frame to be indicated. The mechanism is based on implicit TWT operation and additionally enables:
    Broadcast triggered TWT by including a TWT element in the Beacon
    Solicited triggered TWT by using implicit TWT negotiation procedure
Yes
No
Abstain

## Slide 16: Straw Poll #2
Do you support to add the following text in the SFD:
  When the broadcast triggered TWT is enabled, STA and AP may exchange TWT request/response to indicate the target Beacon frame to be monitored by the PS STA.
Yes
No
Abstain

## Slide 17: References
[1] M. Fischer (Broadcom) et. al., 11-12-0823-00-00ah-targetwaketime