## Slide 1: Regarding buffer status of UL-STAs in UL-OFDMA
Date: 2015-07-14
Authors:

## Slide 2: Introduction
Emphasizing the importance of buffer status information of UL-STAs in UL-OFDMA
Discussing buffer status report methods using random access UL-OFDMA

## Slide 3: Enhancing the efficiency of UL-OFDMA
The more number of assigned STAs per UL-OFDMA session, the more efficiency can be achieved
  Contention isolation: OFDMA replaces multiple contention periods [1]
AP assigns UL-STAs to available RUs with trigger frame
It is desirable for AP to secure the information of UL-STAs’ buffer status information as much as possible
  Which STAs are having what kind of data?
  ID, Data length, (AC etc.)
Methods for gathering buffer status information hasn’t been discussed very much

## Slide 4: UL-OFDMA without buffer status information
Without buffer status information
  Impossible to assign specific STA to RUs
  AP might open available RUs to let STAs access to randomly chosen RUs
  AP sends TF for random access
    with duration of random access UL-Data defined by AP
      Every UL-Data transmission should be end at the same time
  Random access of UL-Data might significantly degrade the effective TP of UL-OFDMA

## Slide 5: UL-OFDMA without buffer status information
Possibility of collisions and no-access
  The sparser the network, the more number of empty RUs will appear
  The denser the network, the more collision will occur

## Slide 6: UL-OFDMA without buffer status information
Depending on the variance of UL-Data length, the effective TP of UL-OFDMA might further decrease
  UL-STAs with shorter UL-Data length should add padding until the longest UL-Data ends
The more padding, the less effective TP

## Slide 7: UL-OFDMA without buffer status information
In order to reduce the negative effect of padding, AP might force shorter UL-Data length
  Every UL-Data must be fit into the appointed UL-Data length
  The total amount of padding will decrease
Overall system overhead will increase
  Requiring more number of UL-OFDMA sessions for the same amount UL-Data

## Slide 8: Buffer status report for UL-OFDMA
Buffer status information on AP side will provide more flexibility on RU assignment
  With STA ID (e.g., AID), collision and no-access RUs can be avoided
  With data length, padding can be minimized using RU granularity
Conventional polling based buffer status report incurs too much overhead [2]
1-bit indication method (e.g., more data in MAC header)
  AP could obtain only UL-STA IDs, no data length – limitation on quality
  Only STAs who had communicated with AP in the past can be assigned – limitation on quantity
  The validity of information degrades as time passes
It is necessary to consider appropriate buffer status reporting methods with reasonable overhead and delay bound

## Slide 9: Buffer status report using UL-OFDMA Random Access (case 1)
Buffer status report using UL-OFDMA Random Access
  UL-OFDMA random access have been introduced in the last meeting[4]
Case 1: using novel frame format for Buffer Status Report (BSR)
  AP sends TF for BSR Request (BSRR) at the beginning of UL-OFDMA session
    Including BSRR indication (AID for BSRR), RUs for BSR
  Each UL-STA sends BSR through randomly chosen RU as a response of BSRR
  AP assigns RUs to UL-STA based on BSR
  Normal trigger frame for UL-Data will follow the BSR
    Triggering actual UL-Data transmission

## Slide 10: Buffer status report using UL-OFDMA Random Access (case 1)
More details on RA BSR
  A new frame format might be defined
    Recognizable only for ax-STAs
    Reducing redundant part of MAC header or PHY preamble
      Minimizing the loss of spectral efficiency from collision or no-access
    Containing only essential information for RU assignment
      ID, data length
      Other parameters (e.g., AC) might be included
  AP might open RUs for BSR over multiple channels
    Available channel with AP’s perspective
  Collided BSR could be regarded as contention failure
  The following TF might take a role of acknowledgement for BSR
  AP may choose whether it send BSRR or not
    Considering its UL-STA pool

## Slide 11: Buffer status report using UL-OFDMA Random Access (case 2)
Case 2: Inserting buffer status information into UL-Data
  Starting with short random access UL-OFDMA by TF of AP
    AP doesn’t limit the use of random access RU
      STAs could send either management frame or UL-Data
  AP defines the RA UL-Data length considering common UL short frames
    E.g., association, probe request
  UL STAs randomly accessing RUs insert remaining data length in their buffer into their transmitting UL-Data
    Existing header field can be reused (e.g., QoS control field in MAC header [3])
    Inserting the length information after the body of UL-Data

## Slide 12: Buffer status report using UL-OFDMA Random Access (case 2)
(continued)
  Following the random access UL-OFDMA, AP triggers additional UL-OFDMA with specific RU assignment based on gathered buffer status information

## Slide 13: Conclusion
Insufficient information of UL-STAs buffer status might degrade the efficiency of UL-OFDMA
  In terms of overhead and effective TP
It is necessary to consider appropriate buffer status reporting methods with reasonable overhead and delay bound
Buffer status report based on random access could be considered as one of the solutions

## Slide 14: Reference
[1] 11-14-1442-01-00ax-considerations-on-dl-ofdma-control-mechanism
[2] 11-14-1431-00-00ax-issues-on-ul-ofdma
[3] 11-15-0608-01-00ax-regarding-trigger-frame-in-ul-mu

## Slide 15: Straw poll #1
Do you agree with the necessity of buffer status report of UL-STAs as part of a UL-OFDMA procedure?
Y
N
A

## Slide 16: Straw poll #2
Do you agree with random access based UL-OFDMA for UL-STAs’ buffer status report?
Y
N
A