## Slide 1: Enlarged minimal contention window size
Date: 2015-07-14
Authors:

## Slide 2: Abstract
802.11 OFDM PHYs foresee a minimal Contention Window size of 15. With many stations contending for access to the wireless medium (WM), this initial Contention Window might be too small.
A simple approach is presented that increases the number of contention slots without impacting any performance relevant aspects.

## Slide 3: Minimal Contention Window size, 2.4 GHz band
802.11-1997
  DSSS & FHSS
    CWmin = 31
802.11b-1999
  HR/DSSS
    CWmin = 31
802.11g-2003
  Long slot time mode
    CWmin = 31
  Short slot time mode
    CWmin = 15
802.11 DSSS set baseline in 2.4 GHz
  Most 802.11g deployments in “compatibility” mode
  Use of CWmin = 31 prevailing
802.11n-2009 uses CWmin = 15 in 2.4 GHz

## Slide 4: Minimal Contention Window size, 5 GHz band
802.11a-1999
  First use of OFDM
  CWmin = 15
802.11n-2009
  MIMO upgrade
  CWmin = 15
802.11ac-2013
  802.11n upgrade
  CWmin = 15
All 802.11 standards for the 5 GHz band use CWmin = 15

## Slide 5: 802.11e – Quality of Service
802.11e introduces support for QoS
  Distributed Coordination Function (DCF) replaced by Enhanced Distributed Channel Access (EDCA)
  EDCA introduces four priorities
EDCA priorities use different minimal and maximal contention window sizes
  Priorities adapt scaled CWmin value
  All 802.11n & 802.11ac STAs implement EDCA
All priority values derived from CWmin
  Apart from AIFSN

## Slide 6: CWmin design
An small, initial Contention Window causes high collision probability
  Airtime waste, growing contention windows, high jitter, retransmissions, …
Compromise: Single STA (peak) performance vs. optimal performance with many STAs
  No One-fits-all value

## Slide 7: Dense deployments
One BSS may serve many STAs
  With EDCA, AP can enlarge CWmin per priority
    Reduces peak performance
    Reduces collision probability & may increase performance
Current default values target single BSS performance
  EDCA parameter set adjustment seldom used
    Some implementations do not adopt parameters signaled by AP
    No influence on EDCA parameter set selection in neighboring BSSs

## Slide 8: How to reduce collision probability?
Enlarge CWmin
  Helps to reduce collision probability
  How to select optimal value?
    Dynamic, adaptive process needed
  How to signal/agree needed CWmin between different BSSs?
Enlarging default CWmin with 802.11ax
  Introduces coexistence problem
    PHYs prior to 802.11ax use CWmin = 15
  Would decrease 802.11ax access probability compared to prior PHYs

## Slide 9: Enlarge CWmin AND reduce aSlotTime
Consider 5 GHz
  aSlotTime = 9 µs
  CWmin = 15
  9 µs × 16/2 = 72 µs
Select 802.11ax aSlot & CWmin to achieve mean wait duration as previous PHYs
  Const = aSlotTime × (CWmin + 1)/2
802.11ax default set
  aSlotTime = 4.5 µs
  CWmin = 31
Twice the number of contention slots compared to 802.11n & 802.11ac
  Mean wait duration: 4.5 µs × 32/2 = 72 µs

## Slide 10: aSlotTime definition
aSlotTime = aRxTxTurnaroundTime + aMACProcessingDelay + aAirPropagationTime + aCCATime
Implementation dependent with 802.11ac
  aCCATime
  aMACProcessingDelay
  aRxTxTurnaroundTime
Static (range dependent)
  aAirPropagationTime

## Slide 11: 802.11ax aSlotTime = 4.5 µs
Assume 300 m range
  aAirPropagationTime = 1 µs
Thus today, aCCATime + aMACProcessingDelay + aRxTxTurnaroundTime ≤ 8 µs
To meet aSlotTime goal reduce previous sum from 8 µs to 3.5 µs
  Save 5 µs to sustain 300 m range assumption
aCCATime
  < 4 µs with 802.11a-1999
aMACProcessingDelay
  < 2 µs with 802.11a-1999
aRxTxTurnaroundTime
  < 2 µs with 802.11a-1999
With 802.11-2012, all values are noted as implementation dependent
  Only values for interoperability specified anymore

## Slide 12: Feasibility study
aMACProcessingDelay
  Max time for MAC to issue PHY-TXSTART.request
  Today’s hardware is more powerful than 802.11a hardware in 1999
aRxTxTurnaroundTime
  Max time to change from Rx to Tx
  Hardware evolution provides for substantially faster turnaround than in 1999
aCCATime
  Max time that CCA has available to detect start of a valid IEEE 802.11 transmission
  Major part in aSlotTime
  Today’s hardware needs less time than previous implementations
aSlotTime = 4.5 µs seems possible

## Slide 13: Further changes, observations
AIFS = SIFS + n × aSlotTime
  With 802.11ax double n to compensate for halved aSlotTime
  Keep Duration (AIFS802.11ac) = Duration (AIFS802.11ax)
With enlarged CWmin & reduced aSlotTime 802.11ax STAs achieve advantage over non-802.11ax STAs
  802.11ax STAs may access earlier
  Acceptable “penalty” on legacy STAs to be discussed

## Slide 14: Conclusion
aSlotTime = 4.5 µs seems possible with 802.11ax
  Increases Contention Window, reduces collision probability
  Suitable with dense deployments = 802.11ax scope
Halved aSlotTime gives earlier access to 802.11ax STAs
  Simulations to follow to show impact
  Can be balanced with legacy devices
Simple and non-intrusive approach