## Slide 1: 20150707 Wi-Fi Alliance feedback on 802.11 Task Group AY usage models
Date: 2015-07-07
Authors:

## Slide 2: Abstract
20150707 Wi-Fi Alliance feedback on 802.11 Task Group AY usage models
DATE: 7 July 2015
TO: Adrian Stephens, Chair, IEEE 802.11 Working Group
Edward Au. IEEE Task Group AY Chair pro-tem
RE: Wi-Fi Alliance feedback on 802.11 Task Group AY usage models
The IEEE 802.11 Working Group sent Wi-Fi Alliance a liaison on 18 May 2015 requesting input from Wi-Fi Alliance on questions related to use cases being considered by the 802.11ay Working Group. In particular, the IEEE 802.11 Working Group asked WFA to provide feedback and prioritization on provided usage models.
Wi-Fi Alliance members reviewed the usage models and provided prioritization (rankings) based on perceived “Bottleneck” and “Mainstream” market effect on the various usage models. During the review, some members requested the inclusion of additional use cases. These use cases are ranked alongside the usage models that the IEEE Working Group shared with Wi-Fi Alliance.
The data is provided as redacted raw results and average prioritization without interpreting any particulars from the results of the survey, which was open to participation by all members of Wi-Fi Alliance. Several members also provided individual comments for individual use cases, prioritization justification for high and low results, and the overall collection of use cases.
Please feel free to contact Wi-Fi Alliance with any questions or comments related to this liaison document.

## Slide 3: Use case ranking based on when they might become "MAINSTREAM"
“Please rank the following use cases based on when they might become "MAINSTREAM", with 1 being the soonest and 10 being the latest”
The chart shows the total number of votes for each use case ranking
Use case rankings are averaged and sorted from soonest to latest
Use Case | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | Rating Average
Wireless Office Docking (proposed new use case) | 3 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 3.57
Mobile Offloading and Multi-Band Operation (MBO) | 1 | 2 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 3.71
Augmented Reality/Virtual Reality Headsets and Other High-End Wearables | 0 | 3 | 0 | 2 | 1 | 0 | 0 | 0 | 1 | 0 | 4
Video/Mass-Data Distribution/Video on Demand System | 0 | 1 | 2 | 1 | 0 | 1 | 2 | 0 | 0 | 0 | 4.57
8K UHD Wireless Transfer at Smart Home | 1 | 0 | 1 | 2 | 1 | 1 | 0 | 0 | 0 | 1 | 4.71
Ultra Short Range (USR) Communications | 2 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 2 | 0 | 5
Wireless Backhauling | 0 | 0 | 1 | 2 | 1 | 1 | 1 | 1 | 0 | 0 | 5.29
Converged Backhaul/Access (proposed new use case) | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 3 | 0 | 7.29
Data Center 11ay Inter-Rack Connectivity | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 3 | 8.43
Mobile Fronthauling | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 2 | 0 | 3 | 8.43

## Slide 4: Use case ranking based on anticipated “BOTTLENECK”
“Please rank the following use cases based on your opinion of anticipated "BOTTLENECK" due to use of near term Wi-Fi (802.11ac) and WiGig (802.11ad) limitations, with 1 being the soonest and 10 being the latest ”
The chart shows the total number of votes for each use case ranking
Use case rankings are averaged and sorted from soonest to latest
Use Cases | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | Rating Average
Augmented Reality/Virtual Reality Headsets and Other High-End Wearables | 1 | 3 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 3.71
8K UHD Wireless Transfer at Smart Home | 2 | 1 | 1 | 0 | 2 | 0 | 0 | 0 | 0 | 1 | 3.86
Ultra Short Range (USR) Communications | 2 | 0 | 0 | 2 | 1 | 0 | 0 | 1 | 0 | 1 | 4.71
Wireless Office Docking (proposed new use case) | 1 | 0 | 1 | 1 | 3 | 0 | 0 | 0 | 0 | 1 | 4.71
Video/Mass-Data Distribution/Video on Demand System | 0 | 1 | 2 | 0 | 0 | 2 | 1 | 0 | 1 | 0 | 5.14
Wireless Backhauling | 0 | 2 | 1 | 1 | 0 | 0 | 1 | 0 | 2 | 0 | 5.14
Mobile Offloading and Multi-Band Operation (MBO) | 1 | 0 | 0 | 2 | 0 | 1 | 2 | 0 | 0 | 1 | 5.57
Data Center 11ay Inter-Rack Connectivity | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 3 | 0 | 1 | 6.71
Mobile Fronthauling | 0 | 0 | 1 | 0 | 0 | 0 | 3 | 1 | 1 | 1 | 7.29
Converged Backhaul/Access (proposed new use case) | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 1 | 3 | 1 | 8.14

## Slide 5
Feedback - Wireless Office Docking (proposed new use case)
Ranked in top two as “MAINSTREAM” use case
  Docking is an extension of an existing application today. The proposed data rates of 802.11ay will catch up with the bandwidth requirements of most desktop connected devices and allow a true wireless dock. The need for the wireless dock is driven by the migration of laptops to ultrabooks, tablets and ultimately smart phone platforms.
  Wireless office will become more mature, the monitor resolutions are going up (5k, 8k), in conjunction with faster internet connection and multiple simultaneous high performance links.
  Docking supports nomadic worker.
  It’s already on the market.
Ranked in top two as “BOTTLENECK” use case
  Mobile Office: 11ad is a bottleneck for USB3.
Ranked in bottom two as “BOTTLENECK” use case
  Should wireless docking begin to be shipped in larger quantities, it might become more critical to avoid the bottleneck with more throughput capacity. Video distribution in mass currently remains on the wire, so the same comment applies that we need to watch to see if higher resolutions are needed for this use case.
Additional feedback
  The demand for this application is increasing as consumers continue to migrate to more mobile form factors (ultrabooks, tablets, smartphones) for their everyday computing devices.
  Wireless docking is in direct competition with wired solutions e.g. USB Type C. Therefore we need higher wireless throughputs ASAP.

## Slide 6
Feedback - Mobile Offloading and
Multi-Band Operation (MBO)
Ranked in top two as “MAINSTREAM” use case
  Mobile offloading is driven by the ever increasing demand for wireless bandwidth.
  Mobile offloading is required since the communication traffic of the public network is increasing due to the spread of the smart and mobile devices.
  Mobile Offloading already has a good momentum with Wi-Fi. With .11ay and with growing market penetration of 60GHz devices this momentum can be increased.
  A real demand for high capacity mobile data networks.
  Data usage grows exponentially requiring higher capacity/throughput not provided by the actual solutions.
Ranked in top two as “BOTTLENECK” use case
  Mobile Offloading will be limited by 802.11ac and 802.11ad due to limitations in the number of clients supported by the protocols. This may prevent effective offloading.
Ranked in bottom two as “BOTTLENECK” use case
  In is not clear when the bottleneck will become obvious.
Additional feedback
  This is a natural fit for 802.11ay and any next generation wireless.
  It’s a good use case to expand the usage scene of 11ay.
  Growing need due to growing 3GPP offload demand.

## Slide 7
Feedback - Augmented Reality/Virtual Reality Headsets and Other High-End Wearables (1 of 2)
Ranked in top two as “MAINSTREAM” use case
  The size of video data will increase due to 4K/8K video file. End users need to move the video between stationary/mobile devices for a short seconds. Around 2020, the use of 8K UHD Video streaming contents and products increase and end users want to replace cable with wireless technology.
  Head Mounted Display seems to become popular as a personal display. Wireless Head Mounted Display is desired to improve the user experience.
  Consumer demand has already indicated that these use cases are in need of high speed video and data cable replacement in the next few years.
Ranked in bottom two as “MAINSTREAM” use case
  So far, compression is available for 8K usage. And wearable devices requires much power consumption.
Ranked in top two as “BOTTLENECK” use case
  High-End Wearable requirements can't be met by 802.11ac at all, and will run into bandwidth limitations with 802.11ad in scenarios where there is significant density of devices.
  In wearable product cases, higher throughput would be required to maintain the video streaming even if the location of antenna on wearables moves. The data rates of 11ac/11ad are not enough for the high rate and quality video transferring. From the throughput point of view, 11ac/11ad might not be able to achieve this usage model. And the 11ac would require a measurable amount of power consumption, which produces heat, is not good for headset wearables.
  Since the resolution of the video is becoming higher, the bandwidth of 11ac/11ad will not be enough. In case of 11ac, the collision will occur according to the user number increases which will be a problem for real-time application. The usage is assuming users moving in the walking speed, so the communication may be disconnected using 11ad. Video streaming may stop during the band switching using 11ac/11ad.
  Industry feedback indicates that these two use cases are in need of more capacity to support high resolution and low latency.

## Slide 8
Feedback - Augmented Reality/Virtual Reality Headsets and Other High-End Wearables (2 of 2)
Additional feedback
  High end wearables is very suitable for higher data-rate wireless, however it is unclear if this is truly a large market.
  Higher video quality should be required around 2020. For headsets use cases(i.e. HMZ-T3 and Oculus VR) of Usage Model 3, Data rate should be > 28Gbps at least (as same as Usage Model 2). In the future, 57.02Gbps should be required to transfer uncompressed 8K UHD(8K@60p,24bpp,4:4:4) video and similar video source device in Usage Model 2 would be commonly used at home. Although this defines that operating environment is indoor <5m usually, it should be scoped up to 10m to support largish living room. We believe that there would be a case where the user would use the wireless headsets anywhere freely in the largish living room which might have a distance of 10 meters between far corners - so resulting range highly depends on target data rate/EIRP on each scenarios. We'd ask to consider modifying "5 meters" to "10 meters" or "5~10 meters" in order to avoid unnecessary restriction.
  Reducing the power consumption is important in addition to suppressing delay and jitter.
  Cool but may be niche only.
  Concern of power consumption.

## Slide 9
Feedback - Video/Mass-Data Distribution/
Video on Demand System
Ranked in top two as “MAINSTREAM” use case
  It is foreseeable that support for fast transfer in dense environments would be required to meet the needs of major upcoming mass events such as Olympics in 2018/2020 and World Cup in 2018/2022.
  There is a clear demand on the video/mass data distribution.
Ranked in top two as “BOTTLENECK” use case
  11ac/ad cannot address co-existence between USR and normal range communication, nor very fast setup. Also, they cannot address high speed burst transmission requirements, especially in high density environment.
Ranked in bottom two as “BOTTLENECK” use case
  Should wireless docking begin to be shipped in larger quantities, it might become more critical to avoid the bottleneck with more throughput capacity. Video distribution in mass currently remains on the wire, so the same comment applies that we need to watch to see if higher resolutions are needed for this use case.
Additional feedback
  This is highly suitable for a next generation wireless technology, however the market for this application is limited compared to others.
  Technology to avoid interference is important since many users communicate simultaneously.
  Need to see first growth with 11ad devices.

## Slide 10
Feedback - 8K UHD Wireless Transfer at Smart Home (1 of 2)
Ranked in top two as “MAINSTREAM” use case
  Consumer demand has already indicated that these use cases are in need of high speed video and data cable replacement in the next few years.
Ranked in bottom two as “MAINSTREAM” use case
  So far, compression is available for 8K usage. And wearable devices require much power consumption.
Ranked in top two as “BOTTLENECK” use case
  Since the resolution of the video is becoming higher, the bandwidth of 11ac/11ad will not be enough. In case of 11ac, the collision will occur according to the user number increases which will be a problem for real-time application. The usage is assuming users moving at walking speed, so the communication may be disconnected using 11ad. Video streaming may stop during the band switching using 11ac/11ad.
  Industry feedback indicates that these two use cases are in need of more capacity to support high resolution and low latency.

## Slide 11
Feedback - 8K UHD Wireless Transfer at Smart Home (2 of 2)
Ranked in bottom two as “BOTTLENECK” use case
  Those use case could be achieved with higher layer techniques so far.
Additional feedback
  8K is an important application, but 4K is only just rolling out. 8K is likely 7-10 years from becoming mainstream.
  Multi-link connection may also be considered.
  They should add compression for power efficiency and better link performance.
  Compression is available.

## Slide 12
Feedback - Ultra Short Range (USR) Communications (1 of 2)
Ranked in top two as “MAINSTREAM” use case
  The size of video data will increase due to 4K/8K video file. End users need to move the video between stationary/mobile devices for a short seconds. Around 2020, the use of 8K UHD Video streaming contents and products increase and end users want to replace cable with wireless technology.
  It is foreseeable that support for fast transfer in dense environments would be required to meet the needs of major upcoming mass events such as Olympics in 2018/2020 and World Cup in 2018/2022.
  Simple and fast download supports distribution of multimedia content.
Ranked in bottom two as “MAINSTREAM” use case
  Ultra Short Range communication is increasingly becoming unnecessary with a move to cloud based applications and storage.
  Use Cases that are Ultra Short Range are already about to be serviced by 802.11ad at both long and short range. Perhaps the use case can merge into another use case such as UHD?
Ranked in top two as “BOTTLENECK” use case
  11ac/ad cannot address co-existence between USR and normal range communication, nor very fast setup. Also, they cannot address high speed burst transmission requirements, especially in high density environment.
  User will expect download of video content in few seconds.

## Slide 13
Feedback - Ultra Short Range (USR) Communications (2 of 2)
Ranked in bottom two as “BOTTLENECK” use case
  Ultra Short Range communication is unlikely to reach a bottleneck as 802.11ad can satisfy any data rates required by devices. The limitation is likely to be with other aspects of device hardware, in particular storage speed.
Additional feedback
  As data moves to the cloud and constant connectivity becomes increasingly prevalent, the need for this application diminishes.
  Need to see first growth with 11ad devices.

## Slide 14
Feedback - Wireless Backhauling
Ranked in top two as “BOTTLENECK” use case
  Traffic congestion with growing mobile data traffic.
  Low cost backhaul of multi-radio small cells (LTE, 11ac + 11ad)
  There are products already on the market using mmWave.
  Future networks require higher capacity backhaul with advanced features for beamforming to meet the nature of directional transmission in wireless backhauling.
Ranked in bottom two as “BOTTLENECK” use case
  11ac/11ad/11ay might not be able to meet the requirement on avoiding interference level or data bandwidth.
  Those use case could be achieved with higher layer techniques so far.
Additional feedback
  This is highly suitable for a next generation wireless technology, especially when combined with mobile offloading, multi-band operation and access.
  We need to see higher throughput and longer ranges with 11ay.

## Slide 15
Feedback - Converged Backhaul/Access
(proposed new use case)
Ranked in bottom two as “MAINSTREAM” use case
  The wired technology solution will be able to cover those use cases.
  Most complex use case. Will come later.
  Converged backhaul/access may lack of throughput, QoS and reliability due to relay feature.
Ranked in bottom two as “BOTTLENECK” use case
  The converged backhaul/access architecture is unlikely to run into limitations posed by 802.11ad in the near term due to the limited number of active nodes anticipated in the network. 802.11ac is not suitable for this application due to susceptibility to interference from the proliferation of other 802.11ac networks.
  11ac/11ad/11ay might not be able to meet the requirement on avoiding interference level or data bandwidth.
  High complexity, niche markets, not done wireless so far.
  Converged backhaul/access scenario may not be used soon.
Additional feedback
  This is a growing, important application of wireless technology. As wireless speeds exceed 1Gb/s it becomes feasible to replace cables/fibre with wireless over medium range distances.
  Complex, should have front- and backhauling first.

## Slide 16
Feedback - Data Center 11ay Inter-Rack Connectivity
Ranked in bottom two as “MAINSTREAM” use case
  We think that the usage scene is limited. We think that the market volume is not so high since it will not be used by end-user.
  The wired technology solution will be able to cover those use cases.
  Inter-Rack connectivity can better be solved by fibers.
  Data center redundancy certainly seems to have a lot of value and high data throughput, however it is adequately served by wired connections and other forms of redundancy.
Ranked in bottom two as “BOTTLENECK” use case
  Inter-Rack connectivity is expected to be solved by fibers.
Additional feedback
  This application demands a lot of bandwidth, and although cables may be a cost in rolling out rack infrastructure it is not a large limitation.
  Important for overflow and fallback connections.
  Can better be solved by fibers. Is also an 802.15 THz use case.

## Slide 17
Feedback - Mobile Fronthauling
Ranked in bottom two as “MAINSTREAM” use case
  Mobile fronthauling, although an application that may benefit from mmWave wireless technologies has very different and challenging requirements that mean it may not be well met using a standard developed for wireless networking.
  Usage scene is limited. The market volume is not so high since it will not be used by end-user.
  Mobile Fronthauling: Adds complexity, line of sight can be an issue, existing alternative solutions that might fit better.
Ranked in bottom two as “BOTTLENECK” use case
  It is not clear when the bottleneck will become obvious.
  High complexity, niche markets, not done wireless so far.
Additional feedback
  This application has extremely challenging requirements on the underlying technology that is very different from other consumer/enterprise applications.
  Something for a later stage only.
  There is a concern about timing synchronization.
  Will have very high requirements in future. No listen before talk technology may be useful.

## Slide 18
General feedback
The use cases provide a good cross-section of applications and should drive a number of new and innovative technologies that will enable other applications that haven't been imagined at this time.
Use cases are multifaceted. Use cases should opposed to 5G requirements if mobile network technology is addressed (fronthaul, backhaul).
IEEE has done a solid job of indicating potential needs in the coming years.