## Slide 1: Ra!, Ra!, SYNRA
Date: 2015-07-15
Authors:
Name | Affiliations | Address | Phone | Email
Donald Eastlake | Huawei Technologies | 155 Beaver Street, Milford, MA 01757 USA | +1-508-333-2270 | d3e3e3@gmail.com
David Kloper | Cisco Systems, Inc. | 170 W Tasman Dr San Jose, CA 95134 | 408-526-5041 | dakloper@cisco.com

## Slide 2: Abstract
A proposal for a better SYRNA, at least in the GLK-only case.

## Slide 3: Some Observations
Observation: If an AP is GLK-only, we can be sure that only GLK STAs are processing any Data frames transmitted by the AP.
Observation: If an AP must use the four address format and a SYNRA for all Data frames it sends with a group addressed RA, then associated STAs know the RA is a SYNRA if the group bit is on in that RA.
Conclusion: At least in the GLK-only case, we have 47 bits to play with.

## Slide 4: Example
Bits | Meaning
0 | Group bit = 1
1-2 | Type = 0 (other values reserved)
3 | Include/exclude values outside of bitmap
4-15 | Offset in units of 8 bits (0 to 32,760)
16-47 | 32 bit bitmap

## Slide 5: What about a mixed BSS?
If an AP will associate with both GLK and non-GLK STAs, what is the probability that some STA, possibly due to some proprietary feature, would be confused by a group addressed, four address format Data frame using a SYNRA that might collide with a real multicast address?
Extremely low > we can just use the one SYNRA such as on previous slide
Not so low > we need a backwards compatibility SYNRA2 using up a newly allocated OUI

## Slide 6: Straw Polls
Should we pursue the type of SYNRA shown on slide 4 at least for the GLK-only case?
Do we need a backwards compatible SYNRA2 with a newly allocated OUI for the mixed GLK and non-GLK case?