## Slide 1: PDF of Spatial Angles Reflected from Ceiling in the Conference Room Channel Model
Date: 2015-09-14
Authors:
Name | Affiliations | Address | Phone | Email
Shouxing Simon Qu | BlackBerry, Ltd. | 1001 Farrar Rd., Ottawa, ON, Canada | 1-613-595-4205 | squ@blackberry.com
James Lepp | BlackBerry, Ltd. | 1001 Farrar Rd., Ottawa, ON, Canada | 1-613-595-4156 | jlepp@blackberry.com

## Slide 2: Abstract
This submission presents an analytical expression for the probability density function (PDF) of the spatial angles with 1st-order reflection from the ceiling in the conference room channel model specified in [1].
[1] Alexander Maltsev et al.: “Channel models for 60 GHz WLAN systems”, IEEE 802.11-09/0334r8.

## Slide 3: Introduction
The IEEE 802.11ad group has developed a set of channel models in 60 GHz band based on the results of experimental measurements.
The developed models include conference room, living room, and enterprise cubicle environments [1]-[2].
Statistic characteristics of arriving and departure angles were reported in [1] based on experimental results.
No analytical results were available.
As proposed in [3] for NG60, the set of 802.11ad model is to be updated and improved.

## Slide 4: Ray Tracing Model for Conference Room in [1]
(Figure copied from [1])

## Slide 5: Spatial Angles with 1st-Order Reflection from Ceiling

## Slide 6
What is the PDF of the elevation angle (EA) ?
h: distance between table surface and the ceiling.
specifies the location of Tx.
specifies the location of Rx.
and are independently and uniformly distributed on the table surface.
No general and accurate analytical expression for the PDF of EA was available.

## Slide 7: Experimental Result of the PDF Reported in [1]
(Figure copied from [1])

## Slide 8: Approximate PDF from Experimental Result [1]
An approximate PDF of EA with 1st-order reflection from ceiling has been proposed in [1].
For Lx = 2.5m, Ly = 1m, h = 2m only.

## Slide 9: Comments on the Approximate PDF
Piece-wise linear approximation.
Error is relatively large around the peak.
Yielding negative values around a = 90°.

## Slide 10: Analysis of General and Accurate PDF of EA
h: constant.
, are independent and uniform RVs.
A general and accurate PDF of EA is derived analytically.

## Slide 11: Analytical PDF Expression for the Elevation Angles
(1) for :
×
.

## Slide 12
(2) for :
×

## Slide 13
3) for :
×

## Slide 14
(Lx = 2.5m, Ly = 1m, h = 2m)
negative

## Slide 15: New Approximate PDF of EA (Lx=2.5m, Ly=1m, h=2m)

## Slide 16
New Approximate PDF of EA
(Lx=2.5m, Ly=1m, h=2m)

## Slide 17: Conclusions
An accurate analytical expression for the PDF of the spatial angles with first-order reflection from the ceiling in the conference room model specified in [1] is presented.
Only elementary functions are involved. No special function is needed.
While the corresponding statistical distribution obtained from experiment in [1] is consistent with the analytical result for the specific example, the analytical result provides a theoretical, general and accurate PDF for the EA.
A new approximate PDF with higher accuracy is proposed.

## Slide 18: References
[1] Alexander Maltsev et al.: “Channel models for 60 GHz WLAN systems”, IEEE 802.11-09/0334r8.
[2] Alexander Maltsev et al.: “Verification of IEEE 802.11ad channel model for enterprise cubical environment”, IEEE 802.11-15/0630r0.
[3] Alexander Maltsev et al.: “NG60 channel modeling plan”, IEEE 802.11-15/0614r1.