## Slide 1: Notification of Operating Mode Changes
Date: 2015-09-13
Authors:

## Slide 2: Introduction
802.11ac has introduced Operating Mode Notification frame and element for the following use cases
  STA may change BW for performance or power save
  STA may shut down some RF chains for PS
  AP may ask whole BSS to change channel/BW
Many commercialized 802.11ac Wi-Fi devices are supporting it
The Operating Mode Notification frame and element are still useful for 802.11ax power saving mechanism and are preferred to be revised for 802.11ax

## Slide 3: Operating Mode Changes of HE STA
The Operating Mode Notification frame and element are used to notify STAs that the transmitting STA is changing its operating channel width, the maximum number of spatial streams it can receive, or both
  Definition of an operating channel width from 802.11 spec
    The channel width in which the station (STA) is currently able to receive
  Current Operating Mode Notification frame are element are considering a receive mode only

## Slide 4: Operating Mode Changes of HE STA
Depending on an implementation, the operating mode changes may have effect on a transmit mode as well
  For example, a channel width and a number of spatial streams of a transmitting PPDU can be limited to values indicated in the Operating Mode Notification frame (or element)
  This effect was not an issue in 802.11ac because a channel width and a number of spatial streams of transmitting PPDU are in control of a STA

## Slide 5: Operating Mode Changes of HE STA
However, in 802.11ax, a channel width and a number of spatial streams of an UL MU frame are in control of AP, not STA
Before triggering an UL MU frame, AP should know what is a channel width and a number of spatial streams a STA can transmit
  Otherwise, a performance of an UL MU is degraded

## Slide 6: Operating Mode Changes of HE STA
UL MU issue after change of a channel width
  It is not clear what is a channel width that a STA can transmit after change its operating channel width through the Operating Mode Notification frame (or element)
    If a transmit channel width is limited to a channel width value indicated in the Operating Mode Notification frame, AP shall not trigger an UL MU frame for the STA that use a greater bandwidth than that indicated in the Operating Mode Notification frame
    Otherwise, a performance is degraded as a below figure

## Slide 7: Operating Mode Changes of HE STA
UL MU issue after change of a Rx NSS
  It is unclear what is a number of spatial streams (Tx NSS) that a STA can transmit after change its Rx NSS through the Operating Mode Notification frame (or element)
    If a Tx NSS is limited to a Rx NSS value indicated in the Operating Mode Notification frame, AP shall not trigger an UL MU frame for the STA that use a greater number of spatial streams than that indicated in the Operating Mode Notification frame
    Otherwise, a performance is degraded as a below figure

## Slide 8: Operating Mode Changes of HE STA
Proposal for UL MU issues after the operating mode changes
  The Operating Mode Notification frame and element specifies
    A channel width that a STA can transmit
    A number of spatial streams (Tx NSS) that a STA can transmit
  But, a signaling method is TBD. The following shows one of examples
 | Rx Channel Width | Rx NSS | Rx NSS Type | Tx Channel Width | Tx NSS | Reserved
Bits: | 2 | 3 | 1 | 2 | 3 | 5

## Slide 9: Conclusion
In this presentation, the following items have been addressed
  Operating Mode Notification frame and element are still useful for 802.11ax power saving mechanism
  UL MU issues after the operating mode changes

## Slide 10: Straw Poll 1
Do you agree to add the TGax SFD:
  6.2 Power Save HE STA may use a notification of its operating mode changes for 802.11ax power saving mechanism

## Slide 11: Straw Poll 2
Do you agree to add the TGax SFD:
  6.2 Power Save The Operating Mode Notification frame and element specifies
    A channel width that a STA can transmit
    A number of spatial streams (Tx NSS) that a STA can transmit
  But, a signaling method is TBD.