## Slide 1: Overall Protocol of UL MU BA for Multicast Transmission
Date: 2015/09/14
Authors:

## Slide 2: Agenda
Background & recap
Details of overall protocol
  Protocol overview of UL MU BA for Multicast
  Summary of 802.11aa
  BAR for MU BA
Simulation results
  Example of BAR design for UL MU BA
Conclusion
Straw poll

## Slide 3: Background
The TGax Spec Framework Document (SFD)[1] includes mention of BA/ACK multiplexing, as follows;
  The amendment shall include a mechanism to multiplex BA/ACK responses to DL MU transmission. [MU Motion #4, March 2015]
The TGax SFD also includes a definition, as follows;
  MU features include UL and DL OFDMA and UL and DL MU-MIMO.
Response Phase
UL multiplexed BA/ACK
BA/ACK
BA/ACK
BA/ACK
AP
STA x
STA y
STA z
Data Transmission Phase
AP
STA x
STA y
STA z
DL MU PPDU
DL MU(OFDMA/MU-MIMO) PPDU

## Slide 4: Recap of previous work
  The contribution[2] showed Multiplexing of acknowledgements can be applied for Multicast PPDU to reduce overheads of BA/ACKs from multiple multicast receivers.
  It included a straw poll for a general proposal of multiplexing of acknowledgements as follows, and it received no objection.
  Do you agree that multiplexing of acknowledgements can work effectively for Multicast PPDU in a similar manner as DL-MU(OFDMA/MU-MIMO) PPDU? (Results = Yes:35 /No:0 /Abstain:28)
Data Transmission Phase
AP
STA x
STA y
STA z
DL MC PPDU
DL MC(Multicast) PPDU
Response Phase
BA/ACK
BA/ACK
AP
STA x
STA y
STA z
BA/ACK
Overhead
UL multiplexed BA/ACK
BA/ACK
BA/ACK
BA/ACK
AP
STA x
STA y
STA z
Multiplexing of acknowledgements
can reduce the overhead

## Slide 5: Purpose of this contribution
  We received some questions about the previous contribution, therefore this contribution shows some answers to them.
  In addition, this contribution includes simulation results to show effect of UL MU BA for Multicast.
  Summary of questions and answers
  About protocol overview of UL MU BA for Multicast ➔ This contribution shows details of overall protocol
  About requirement of update from 802.11aa ➔ The protocol is generally based on 802.11aa GCR BAR design only need to be adjust for UL MU BA
  About determination of BAR destinations ➔ Determination based on throughput by using MD report is one of solution. Details are in another[6] and previous contributions[7][8].

## Slide 6: Agenda
Background & recap
Details of overall protocol
  Protocol overview of MU BA for Multicast
  Summary of 802.11aa
  BAR design for MU BA
Simulation results
  Example of BAR design for UL MU BA
Conclusion
Straw poll

## Slide 7: Protocol overview of UL MU BA for Multicast
  BAR-BA frame exchange is based on 802.11aa Groupcast with Retries
  Multiplexing of UL BA (e.g. 4 user multiplexing in this picture)
  Trigger Frame including BAR for multiple devices.
AIFS+BO
Multicast
PPDU
Trigger Frame
including BAR
BA
BA
TBD
BA
BA
AP
STA 1
STA 4
STA 3
STA 2
AIFS+BO
Multicast
PPDU
BAR
BA
SIFS
AP
STA 1
STA 4
STA 3
STA 2
AIFS+BO
BAR
BA
AIFS+BO
BAR
BA
Conventional
Proposed

## Slide 8: Summary of 802.11aa features
  The picture below summaries 802.11aa features [3].
  Required features to enhance 802.11ax Multicast are in red.
Mandatory
Optional
802.11aa features
1. Group address transmission service
4. Management of overlapping networks
Groupcast with Retries (GCR)
Advanced GCR
GCR for Mesh
AP Peer Key
Qload Report
HCCA TXOP Update Count element
3. Intra-access category prioritization
2. Stream classification service
5. Support for the IEEE 802.1Q
Stream Reservation Protocol
Required features to enhance 802.11ax Multicast
Groupcast with Retries (GCR)
GCR Group membership procedures
GCR setup procedures
GCR frame exchange procedures
Concealment of GCR transmissions
GCR unsolicited retry
Advanced GCR
GCR Block Ack
GCR-SP

## Slide 9: Required 11aa features to enhance 11ax Multicast
  Based on 802.11aa GCR Procedures, AP can collect capabilities, Group Address information and setting of GCR from STAs.
This procedure defines initiation/termination of GCR and how STAs request Retransmission Policy
Authentication & Association Procedure
GCR Group Membership Procedures
GCR Setup Procedures
GCR Frame Exchange Procedures
11aa Mandatory
11aa Optional
This procedure defines how an AP collects STAs’ capabilities. (Robust AV Streaming etc.)
This procedure defines how an AP collects Group Address information the STAs receive.
This procedure defines details of Retransmission Policy operation and how an AP or STAs change GCR service.
BlockAckReq and BlockAck exchange, and Management of Bitmap are defined.
Concealment of GCR Transmissions
GCR concealment address is defined for legacy protection.
GCR Block Ack

## Slide 10: Summary of 802.11aa GCR Block Ack
  BlockAckReq(BAR) and BlockAck(BA) frame exchanges
  AP transmits A-MSDUs to the GCR group address before sending a BAR. Upon reception of the BA, the AP sends a BAR to another, and this process is repeated.
  STA transmit a BA at a delay of SIFS after the BAR when the STA receives a BAR.
  After completing the BAR and BA frame exchanges, the AP determines which A-MSDUs need to be retransmitted from the information provided in the BA bitmap.
  To realize BAR and UL MU BA frame exchange, BAR need to be adapted to it
11aa Mandatory
11aa Optional

## Slide 11: BAR for MU BA
BAR need to adapt to UL MU BA in GCR BAR and BA frame exchange sequence.
Discussion about this design will be later of this contribution.
Multicast
PPDU
BA
BA
BA
BA
AP
STA 1
STA 4
STA 3
STA 2
Trigger Frame
including BAR

## Slide 12: Agenda
Background & recap
Details of overall protocol
  Protocol overview of MU BA for Multicast
  Summary of 802.11aa
  BAR design for MU BA
Simulation results
  Example of BAR design for UL MU BA
Conclusion
Straw poll

## Slide 13: Simulation condition
Conditions
  19 BSS, 1 AP and 40 STAs in each BSS
  30 STAs receive Multicast traffic(DL) from AP, 10 STAs transmit interference
  The number of BAR destinations is variable, 0 to 30
    More details, please see appendix
Details of BA multiplexing
  BAR destinations are selected based on their though put.
    Though put information is collected with MD Report, and STAs with worse though put are selected as BAR destinations in bad order.
  Assumed MU scheme is 4-user MU-MIMO, and the rest of 4-user MU is/are multiplexed with only themselves (no additional destinations).
STA-a
STA-b
STA-c
STA-d
STA-e
STA-f
STA-g
STA-h
STA-i
STA-j
Example :
BAR destinations=7
4-user MU
MU group (4 users)
MU group (3 users)
not BAR destinations
Worse through put

## Slide 14: Simulation results
  MU BA improves Multicast performance as shown in the graph.
  With adequate BAR destination and MU BA mechanism, Packet Loss Rate of Multicast traffic can be lower than target PLR.
No MU BA
4user MU BA
Reducing
Packet Loss Rate

## Slide 15: Agenda
Background & recap
Details of overall protocol
  Protocol overview of MU BA for Multicast
  Summary of 802.11aa
  BAR design for MU BA
Simulation results
  Discussion about BAR design for UL MU BA
Conclusion
Straw poll

## Slide 16: BAR design for UL MU BA
BAR need to adapt to UL MU BA in GCR BAR and BA frame exchange sequence.
  Similar discussion is in [9]
The BAR for UL MU BA requires:
  To be received by multiple STAs that receive the multicast PPDU.
  Capability to select destination STAs individually. (groupcast is not suitable.)
  For low overhead, not to be repeated. (Traditional BAR is unicast and repeated)
Multicast
PPDU
BA
BA
BA
BA
AP
STA 1
STA 4
STA 3
STA 2
Trigger Frame
including BAR

## Slide 17: Example of BAR frame format (1/2)
  Latest SFD and original contribution[4] includes Multi-STA BA frame format and details.
  BAR design for UL MU BA can follow this concept.
  Define a variant of BlockAckRequest frame format for Multi-STA BAR by re-using the Multi-TID BlockAckRequest frame format.
  Including indication (TBD) that the frame is a multi-STA BAR
  RA field contains TBD (can be GCR Group Address)
  Each BAR Information field can be addressed to different STAs by B0-B10 of the Per TID Info field with a (Partial) AID identifying the intended receiver
Frame Control
Duration / ID
TA
BAR Control
BAR Information
FCS
BAR Ack Policy
Multi-TID
Compressed Bitmap
GCR
Reserved
TID_INFO
Per TID Info
Block Ack Starting Sequence Control
TID Value
Repeat for each STA
2
2
6
6
2
Variable
4
B0
B1
B2
B3
B4-B11
B12-B15
2
2
B0-B10
Reserved
B11
B12-B15
RA
AID

## Slide 18: Example of BAR frame format (2/2)
UL MU BA requires not only Multi-STA BAR but Trigger Frame that provides resource allocation information to STAs that send MU BAs.
  Details of Trigger Frame format is included in SFD[1].
  Usage of Trigger Frame is discussed in original contribution [5] as follows.
    The definition of the trigger as a MAC MPDU enables several possible operation modes, based on existing specs constructs
      (omission)
      Another example is that the trigger frame may be included in an A-MPDU
  Aggregation of Multi-STA BAR and Trigger Frame is one of solution for UL MU BA.

## Slide 19: Agenda
Background & recap
Details of overall protocol
  Protocol overview of MU BA for Multicast
  Summary of 802.11aa
  BAR design for MU BA
Simulation results
  Example of BAR design for UL MU BA
Conclusion
Straw poll

## Slide 20: Conclusion
  This contribution showed details of the overall protocols of UL MU BA for Multicast transmission.
  The simulation results showed that UL MU BA can improve performance of Multicast transmission significantly.
  This contribution also summarized 802.11aa features and included discussion about BAR design that enables UL MU BA in 802.11aa GCR BAR and BA frame exchange.

## Slide 21: Straw poll 1
  Do you agree to add to the TG Specification Frame work document?
  4.y.z. The amendment shall include a mechanism to multiplex acknowledgment frames to Multicast transmission.
  Yes: /No: /Abstain:

## Slide 22: Straw poll 2
  (not SFD proposal)
  Do you agree that Multi-STA variant of BAR aggregated with Trigger Frame can be BAR design for UL MU BA in GCR BAR and BA frame Exchange?
  Yes: /No: /Abstain:

## Slide 23: Reference
[1] 15/0132r7 “Specification Framework for TGax”
[2] 15/0800r0 “Multiplexing of Acknowledgements for Multicast Transmission”
[3] IEEE Std. 802.11aa
[4] 15/0366r2 “Multi-STA Acknowledgment”
[5] 15/0877r1 “Trigger Frame Format”
[6] 15/1044r0 “Further Study of 11ax Multicast”
[7] 15/0046r0 “11aa GCR-BA Performance in OBSS”
[8] 15/0320r1 “GCR-BA Performance with Measurement Report in OBSS”
[9] 15/1053r1 “Multi-User Block ACK Request (MU-BAR)”
[10] 14/1404r0 “11aa GCR-BA Performance in OBSS”

## Slide 24
Appendix

## Slide 25: Simulation results
  MU BA improves Multicast performance with selecting BAR destination either based on throughput or randomly. But random BAR destinations can not achieve target performance.
Random BAR destinations
Throughput based
BAR destinations
No MU BA
4user MU BA

## Slide 26: Simulation conditions
Node | AP x 19, STA x 30 x19 (multicast), STA x 10 x 19
Num of Drops [times] | 1
Traffic Model & Load | DL: CBR UDP 3 Mbps (multicast) UL(Interference): CBR UDP 10 Mbps, from single cell (unicast)
Traffic Duration [sec] | 39 sec (approx. 10,000 packet transmission at app)
Access Category | AC_BE (unicast), CWmin=15, CWmax=1023, AIFSN=3, TXOP limit=0 AC_xx (Multicast), CWmin=127, CWmax=1023, AIFSN=3, TXOP limit=0
Tx Power [dBm] | +23(AP), +15(STA)
MCS | 7 (HT80, 2SS)
Link Adaptation | Off
Packet Length [byte] | (MPDU, MSDU, APP)=(1530, 1500, 1472) Fixed
L2 Retry | 10 (multicast)/ 10 (unicast)
BAR/Ack Rate | Lowest (MCS0:6Mbps)
RTS Threshold | ∞(Disabled)
Aggregation | (A-MPDU, A-MSDU)=(64KB, NA)
NF [dB] | 7
Channel | (Dist, Shadow, Fading)=(TGn, σ=5dB, K=12dB-Rice)
Detect Th [dBm] | (PD, ED) = (-82, -62)
Channel Setting [MHz] | (CenterFreq, BW)=(5180, 80)
Antenna Gain [dBi] | 0(AP), -2(STA)
Antenna Height [m] | 3(AP), 1.5(STA)
Tx buffer size [Byte] | 375k [default=∞] (size that can hold 1 sec data size)
Wraparound | Enabled
TTL [sec] | 1 sec
PLCP Header Error Det | Enabled
The Number of Multiplexing BA Users | 1(No-multiplexing), 4, 8
Leader Selection | Random / Throughput based(with MD Report)
MSDU Count Duration [sec] | 1
Rx MSDU Threshold to determine send Report | 1000000 (All STA send BAR frames)
Statistics start delay max time [sec] | 0 (All STA start measurement at the same time)
Report transmission delay max time [sec] | 1 (Same as MSDU count Duration)
Topology (followed ss3)

## Slide 27: Summary of 802.11aa Concealment address
    Concealment of GCR transmissions (11aa Mandatory)
      To avoid that legacy STA receives an original frame and a retransmitted frame with same sequence number, the retransmitted frame shall be concealed with dot11GCRConcealmentAddress.
      The concealed GCR Group Address is included in DA field in A-MSDU. The retransmitted frame has Retry=1 in Frame Control field, dot11GCRConcealmentAddress in Address1 field.
A-MSDU
MPDU
Duration
Address 1
Frame Control
Address 2
Address 3
Sequence Control
(Address 4)
QoS Control
(HT Control)
Frame Body
FCS
dot11GCRConcealmentAddress
Retry=1
MSDU
Padding
DA
SA
Length
GCR Group Address
GCR Group Address