## Slide 1: Receive Operating Mode Indication for Power Save
Date: 2015-09-14
Authors:

## Slide 2
Authors (Continued)

## Slide 3
Authors (Continued)

## Slide 4
Authors (Continued)

## Slide 5
Authors (Continued)

## Slide 6
Authors (Continued)

## Slide 7
Authors (Continued)

## Slide 8
Authors (Continued)

## Slide 9
Authors (Continued)

## Slide 10: Outline
Existing spatial multiplexing features in 802.11n/ac
Proposal
Receive operating mode (ROM) indication
Discussion
Conclusion

## Slide 11: Existing Spatial Multiplexing Power Save for HT STA (11n)
An HT STA (11n) uses the spatial multiplexing (SM) power save feature to “allow a STA to operate with only one active receive chain for a significant portion of time” [1] for the purpose of power conservation
There are currently two SM power save modes i.e. static and dynamic
  In static mode, a STA operates with only one active receive chain
  In dynamic mode, a STA enables all its receive chains upon receipt of an individually addressed single-spatial stream frame, e.g. RTS, … ; STA reverts back to one active receive chain upon completion of the current frame exchange
A STA in dynamic SM power save mode notifies the AP of changes to the number of active receive chains either by an exchange of HT Capabilities element, or SM Power Save frame

## Slide 12: Existing Spatial Multiplexing Power Save for HT STA (11n)
Drawbacks of this mechanism
  A single-spatial stream frame needs to be sent prior to the transmission of a multiple spatial stream frame; this overhead affects MAC efficiency
  Choice of either one or maximum number of active receive chains available; inflexibility in the number of active receive chains leads to sub optimal power consumption
  Operating bandwidth is unchanged, i.e. fixed at negotiated bandwidth

## Slide 13: Existing Operating Mode Notification for VHT STA (11ac)
An VHT STA (11ac) uses an Operating Mode Notification frame or element to “notify STAs that the transmitting STA is changing its operating channel width, the maximum number of spatial streams it can receive, or both” [2]
The Operating Mode Notification frame or element contains the Operating Mode field that conveys
  Channel width, i.e. 20, 40, 80, 160 MHz
  Maximum number of spatial streams that STA can receive, i.e. 1, 2, …, 8
Improves 802.11n mechanism by allowing
  Configurable maximum number of active receive chains
  Configurable channel width

## Slide 14: Existing Operating Mode Notification in VHT STA (11ac)
Drawbacks of this mechanism
  Operating Mode Notification frame exchange is needed for any changes in channel width or maximum number of active receive chains; this overhead affects MAC efficiency
  Slow adaptation of number of active receive chains and channel width to match existing link conditions, i.e. <MCS, BW, NSS> where NSS denotes number of spatial streams

## Slide 15: Proposal
This contribution describes a mechanism for receive operating mode indication for STAs to dynamically adapt the number of active receive chains and channel width for reception of the subsequent PPDUs
  Allow STAs to operate in a lower power RX operating mode for a significant portion of time
  Improve MAC efficiency, i.e. reduction in management frame exchanges

## Slide 16: Receive Operating Mode Indication (1)
Proposed a receive operating mode indication mechanism allow STAs to adapt and operate with an appropriate number of active receive chains and channel width for reception of the subsequent PPDU frames

## Slide 17: Receive Operating Mode Indication (2)
Introduce a one byte Receive (RX) Operating Mode (ROM) field in the MAC header of DATA
  RX NSS (3-bit), denotes the number of receive spatial streams of the receiver
  RX Channel Width (3-bit), denotes the channel width of the receiver
Presence of RX operating mode field indicated using a reserved bit in both HT and VHT variant of HT Control field
QoS
Control
HT
Control
RX
Operating Mode
Frame Body
FCS
Frame
Control
….
2
2
4
1
variable
4
MAC Header
Octets:

## Slide 18: Receive Operating Mode Indication (3)
Format of Receive (RX) Operating Mode (ROM) field in DATA type MAC header is TBD

## Slide 19: Receive Operating Mode Indication (4)
The STA originating a unicast frame exchange shall use the RX Operating Mode field in the DATA type MAC header to indicate to the intended receiving STA the state of its receiver upon successful receipt of the response frame
The STA receiving the RX Operating Mode field in the DATA type MAC header shall not transmit a multiple spatial stream frame with a larger number of spatial stream and bandwidth back to the originating STA after an outage time (TBD)
  Different outage times may be specified for NSS (TBD ms) or BW (TBD ms)
  Outage times may be negotiated by a management frame exchange (e.g. Association)

## Slide 20: Example of Receive Operating Mode Indication Operation
AP
STA
RX, NSS=2, BW=40MHz
DATA
BA
BA
DATA
NSS=2
BW=40MHz
Accepted
AP sends DATA in NSS=2 and BW=40MHz
TX
STA sends DATA with RX NSS=2, and RX Channel Width=40MHz
Outage
AP shall not start any PPDU transmissions to this STA after outage time

## Slide 21: Discussion
Power conservation, i.e. minimizing the number of active receive chains and bandwidth while anticipating the next intended frame
  In a congested environment, a STA can spend a significant amount of time and power on Listen state
Improved MAC efficiency, i.e. no need for exchange of Management frames on a per frame basis to change the NSS and channel width; these frames are typically sent at legacy rates
  Instead of using RTS to trigger a dynamic NSS and bandwidth change on the intended receiving STA the proposed mechanism uses information in the MAC header of data frame
Proposed mechanisms can be supported between multiple STAs, i.e. no AP-STA requirement unlike in legacy SM power save in HT STA

## Slide 22: Conclusion
This contribution proposed a mechanism for receive operating mode indication so as to dynamically adapt the number of active receive chains and channel width for reception of the next subsequent PPDU
  Allow STAs in Listen state to save power
  Improve MAC efficiency
Add one byte Receive (RX) Operating Mode field in the Data type MAC header to include
  RX NSS (3-bit)
  RX Channel Width (3-bit)
Use outage time(s) to give receivers ample time to adjust to the new NSS or BW settings

## Slide 23: Straw Poll
Do you support defining a mechanism for a transmitting STA to indicate its RX operating mode, i.e. RX NSS, RX channel width, in a transmitted DATA type MAC header, so that the responding STA shall not transmit a subsequent PPDU using an NSS or channel width value not indicated as supported in the RX operating mode of the transmitting STA.
    The responding STA shall not adopt the new NSS and BW until a time TBD.
  Yes
  No
  Abstain

## Slide 24: Motion
Move to add to the spec framework:
  The spec shall define a mechanism for a transmitting STA to indicate its RX operating mode, i.e. RX NSS, RX channel width, in a transmitted DATA type MAC header, so that the responding STA shall not transmit a subsequent PPDU using an NSS or channel width value not indicated as supported in the RX operating mode of the transmitting STA.
  The responding STA shall not adopt the new NSS and BW until a time TBD.
  Yes
  No
  Abstain

## Slide 25: References
IEEE 802.11-2012
IEEE 802.11ac-2013
IEEE 802.11REVmc D4.0
“802.11 HEW SG Proposed PAR,” 11-14/0165r0